## Slide 1: Randomized MAC Addresses for Privacy Enhancement
Date: 2014-03-18
Authors:

## Slide 2: Abstract
This slide deck presents the idea of using randomized MAC addresses as a tool to enhance privacy in 802.11

## Slide 3: What’s the Privacy Issue?
Passive observation of 802.11 bands reveals MAC addresses
  STAs active probing when not connected to a network
  Communication to connected network
Location plus time plus frequency plus MAC address allows sensitive information to be gleaned
  This MAC address pops up around the AIDs clinic twice a week
  This MAC address is near the liquor store at 8am every day
  This MAC address leaves a certain apartment building in the early morning almost every weekend
Social networks of such meta data can be built with good accuracy in positive identification

## Slide 4: What’s the Privacy Issue?
Sample headlines from 11-13/1448r1:
Seattle Police Deactivate Wi-Fi Spy Grid After Privacy Outcry (Nov 2013)
  A DHS and Seattle police network collecting location information
CreepyDOL Wi-Fi Surveillance project debuts at BlackHat/DEFCON (Aug 2013)
  DIY surveillance with low-cost Wi-Fi based sensors that capture MAC addresses
Wi-Fi Trashcans Now Silently Tracking Your Smartphone Data (Aug 2013)
  ... the company boasted that the cans, which included LCD advertising screens, "provide an unparalleled insight into the past behavior of unique devices"—and hence of the people who carry them around
Guardian article last week:
Phone call metadata does betray sensitive details about your life (Mar 2014)
Stanford researchers were able accurately identify volunteers in a study that gave up their meta data, determining that one person probably had MS, another probably had an abortion, and another probably grew marijuana

## Slide 5: Proposal
When not attached to a network…
  Assign a random MAC address to the wireless interface of portable and mobile STAs (not fixed STAs and APs)
  Periodically change to a new random MAC address
  Don’t actively probe for known networks
When attaching to a network…
  Choose a new random MAC address and connect
While attached to a network…
  Keep the same MAC address for the life of the connection
  Cache PMKSAs (and the MAC address therein) in an RSN
When reattaching to a network…
  Assign the MAC address from the cached PMKSA, then connect

## Slide 6: What’s a Random MAC address?
Take a 48-bit datum
  Assign the datum a random 48-bit string
  Set the bit indicating “locally administered MAC”
  Clear the “unicast/multicast” bit indicating unicast
Assign that 48-bit datum to the MAC address

## Slide 7: Obvious Question #1
Whaddya mean random?
  Make a random selection from the pool of available MAC addresses
  Each possible MAC address from the pool of available MAC addresses has equal probability of being chosen
  I mean the same thing as is meant by the use of the word in section 8.2.4.3.4 in IEEE Std 802.11-2012
But where does it say how to do that?
  Well, appendix M.5 of IEEE Std 802.11-2012 has some fine recommendations for implementers to follow
Note: I’m not blazing a new trail by using the word random!

## Slide 8: Obvious Question #2
What are you gonna do about collisions? Nothing!
There are 246 possible random MAC addresses
The chosen MAC addresses have to be unique in the DS (or IBSS), they don’t have to be globally unique
  There will be a few hundred, maybe a tad over a 1000 STAs
  Much higher and things melt down (remember Verilan in Dallas?)
  How many possible ways for 1000 STAs to choose 246 values?
  with m = 246 = 7x1013, n = 1000 the number of choices is astronomical
  The probability of 2 of the 1000 STAs choosing the same MAC is infinitesimally small… don’t worry about it!
m
n
= m!/n!(m-n)!
“m choose n” is

## Slide 9: Obvious Question #3
Won’t this screw up a whole bunch of 802.11?
  Don’t think so, unless pervasive monitoring is viewed as a positive
Won’t this screw up services provided to users of 802.11?
  Depends on the service, but probably there are some.
  It’s optional; UIs (not done here) can make this an opt-in
  If you want to take advantage of a service that requires you to be tracked then don’t use this optional feature
    Patient: “Doctor it hurts when I do this”
    Doctor: “Don’t do that”

## Slide 10: References
11-13/1448r1 – 802.11 privacy