## Slide 1: DNSSD Activities of IETF
Date: 2014-3-20
Authors:

## Slide 2: Abstract
For your eyes, this presentation shows the activities of DNSSD(DNS-SD/mDNS Extensions) WG of IETF which seem to be related to TGaq. TGaq might need to look around what are happening in the domain of service discovery standards for our own work. The below might be relevant to Tgaq’s work.
The requirement of DNSSD[1] assumes an issue is related to 802.11.
A proposed amendment suggests a proxy hybrids multicast and unicast for the clients on different subnets.

## Slide 3: The Requirements of IETF DNSSD (1/2)
1. Introduction
  …
  DNS-SD/mDNS in its present form is also not optimized for network technologies where multicast transmissions are relatively expensive. Wireless networks such as [IEEE.802.11] may be adversely affected by excessive mDNS traffic due to the higher network overhead of multicast transmissions.
  …

## Slide 4: The Requirements of IETF DNSSD (2/2)
2.2. IEEE 802.11 Wireless LANs
  Multicast DNS was originally designed to run on Ethernet - the dominant link-layer at the time. In shared Ethernet networks, multicast frames place little additional demand on the shared network medium compared to unicast frames. In IEEE 802.11 networks however, multicast frames are transmitted at a low data rate supported by all receivers. In practice, this data rate leads to a larger fraction of airtime being devoted to multicast transmission. Some network administrators block multicast traffic or convert it to a series of link-layer unicast frames. Wireless links may be orders of magnitude less reliable than their wired counterparts. To improve transmission reliability, the IEEE 802.11 MAC requires positive acknowledgement of unicast frames. It does not, however, support positive acknowledgement of multicast frames. As a result, it is common to observe much higher loss of multicast frames on wireless as compared to wired network technologies. Enabling service discovery on IEEE 802.11 networks requires that the number of multicast frames be restricted to a suitably low value, or replaced with unicast frames to use the MAC's reliability features.

## Slide 5: Service Discovery Proxy in a Proposed Extension
DNS-SD[2] specifies the unicast query and response.
A proposal, Hybrid Unicast/Multicast DNS-Based Service Discovery[3], describes a way to provide wide-area service discovery for devices that only advertise their services using link-local Multicast DNS and it mentions a service discovery proxy.
The proxy might be related to PADP proxy. The topology of the blow could be an example.
AP
Printer
Hybrid DNS-SD
Proxy
STA
multicasts

## Slide 6: References
[1] Requirements for Scalable DNS-SD/mDNS Extensions
  http://www.ietf.org/id/draft-ietf-dnssd-requirements-01.txt
[2] DNS-Based Service Discovery
  IETF RFC 6763
[3] Hybrid Unicast/Multicast DNS-Based Service Discovery
  http://tools.ietf.org/id/draft-cheshire-dnssd-hybrid-01.txt