## Slide 1: Proposed Resolution to CID 72, 119 and 128
Date: 2014-05-21

## Slide 2: Introduction
This presentation proposed the resolutions to Comment CID 72, 119 and 128 to Tgaj draft specifications D0.01 in CC12.
The resolutions addressed the following comments in the comments database IEEE 802.11-14-0332r0
  CID 72
  CID 119
  CID 128
Incorporate changes to text proposal amendments after discussions during the presentation of IEEE 802.11-14/0509r1.

## Slide 3: Response to CID 72 & 128 (1/4)
CID 72
  "In 11ad, the decision process is clearly identified as "out of standard scope". The same reason applies here.
CID 128
  “The decision process at the PCP/AP to perform spatial sharing is implementation dependent and should not be mandated in the standard.”
Accept in principle.

## Slide 4: Response to CID 72 & 128 (2/4)
Suggested Remedy (CID 72)
  Remove the whole modification under 10.31.3.
Suggested Remedy (CID 128)
  1. The original statement in 11ad "The decision process at the PCP/AP to perform spatial sharing of a candidate and an existing SP is implementation dependent and beyond the scope of this standard." should be recovered.
  2. Changing "The decision process at the PCP/AP to perform spatial sharing of a candidate and an existing SP is given as below" to "A possible decision process at the PCP/AP to perform spatial sharing of a candidate and an existing SP is described below ".

## Slide 5: Response to CID 72 & 128 (3/4)
In IEEE 802.11-14/0509r1, we propose to adopt suggested remedy in CID128.
However, there is a further comment to shift the description of the decision process in the main text to an (informative) Annex.
We looked at the earlier amendments in IEEE 802.11 but cannot find any similar precedents we can follow.
Nevertheless, we decide to accept the comment to shift the description to an Annex.

## Slide 6: Response to CID 72 & 128 (4/4)
Proposed to remove the whole modification under 10.31.3.
In Section 10.31.1, we introduce the informative Annex as part of the description of the new information element (See CID 119 text proposal)
Insert a new informative Appendix AB. The complete revised text proposal is provided in IEEE 802.11-14-00508r2.

## Slide 7: Response to CID 119 (1/3)
Comment
  "In purpose of spatial sharing, an SSW-ACK frame shall also be sent by the responder to the PCP/AP with the best TX sector, which indicates the beamforming information between the initiator and the responder." How is this going to work? 1) What if the PCP is in power save? 2) After the SSW-ACK is transmitted, the initiator can start data transmission within SIFS. How does this work if the responder is transmitting another SSW-ACK? 3) As it is specified now, this creates backward compatibility problems with 11ad devices.

## Slide 8: Response to CID 119 (2/3)
Suggested Remedy
  This will cause a major impact to the BF protocol and make it non-backwards compatible with 11ad devices. Suggest to remove this change. Instead, it would be more appropriate to include this feedback as part of a new Action frame dedicated to this function. This would allow the same goal to be accomplished, but without a major impact to the BF protocol.
Accept in principle and revise accordingly.
Proposed Revision
  Remove the changes in Section 9.35.2.5
  Add a new information element that may be transmitted in the Information Request and Information Response Action frame: SSW Report element described in subclauses 8.4.2.162

## Slide 9: Response to CID 119 (3/3)
Add a new paragraph in Section 10.31.1 to introduce the new information element.
“AP or PCP may use the beamforming training information among any pair of STAs within the BSS obtained through the SSW Report information element (8.4.2.162) to achieve spatial sharing and interference mitigation. The AP or PCP can transmit an Information Request frame (8.5.20.4) addressed to a STA for a response with a SSW Report element (8.4.2.162) contained in an Information Response frame (8.5.20.5). A non-PCP/non-AP STA can also send an unsolicited Information Response frame with a SSW Report element after the STA has completed the beamforming procedure with at least another STA. The SSW Report information element may be used to facilitate the selection of candidates for spatial sharing as described in Annex AB.”
Line in red above is added after comments to CID 72 & 128 in IEEE 802.11-14/509r1.
The complete revised text proposal to resolve CID 119 is provided in IEEE 802.11-14-00508r2.

## Slide 10: Revised Text
The complete revised text proposal to resolve CID 72, 119, 128 is provided in IEEE 802.11-14-0508r2.
Suggest to remove the changes in D0.01 and revised the text proposal according to IEEE 802.11-14-0508r2.

## Slide 11
THANK YOU