## Slide 1: 802.11ak and 802.1AC Convergence Function
Date: 2014-03-10
Authors:

## Slide 2: Abstract
Building upon a model being proposed for the IEEE 802.11 Portal Convergence Function, this presentation carries that concept into the 802.11ak concepts, and 802.1AC considerations for these extended concepts.

## Slide 3
Following are several slides from the 802.11 portal presentation (being considered in ARC, and 802.1AC) – 11-14/497 …

## Slide 4: This is an example of a physical network
802.3
Two physical boxes, commonly (but inaccurately) called “APs,” connected by an IEEE 802.3 link.
Two clients of “AP 1” shown, two wireless and one wired clients of “AP 2” not shown.
No VLANs.
This example will be used repeatedly in this deck.
“AP” 1
“AP” 2
802.3

## Slide 5: Layering
In the ISO layering model, a DATA.request is presented by a higher layer to a lower layer, and a DATA.indication is presented by a lower layer to a higher layer.
In all further diagrams in this deck, the “higher” layer is closer to the top of the slide, and the “lower” layer closer to the bottom.

## Slide 6: Let’s start at the beginning.
MAC
PHY
MAC
PHY
MAC
PHY
AP STA
Non-AP STAs
DSAF
“DSAF” = “Distribution System Access Function” (as opposed to the whole AP, which covers many sublayers).
“nAP STA” == upper layers of a non-AP STA.
The symbols are Service Access Points to the IEEE 802.11 Clause 5 MAC Service offered to the users of the non-AP STAs.
requests
indications
MAC
PHY
nAP STA
nAP STA
nAP STA
user
user
user
SAP
SAP
SAP
SAP
The medium (the “ether”)

## Slide 7: What is relationship between DSAF & DS?
First interpretation: “The Distribution System provides instances of a service to the DSAF(s).”
We’ll call this DSAF/DS (“DSAF over DS”).
(IEEE 802.11-2012 Annex R.2.2.2.3 says this, explicitly. Annex R is non-normative, but this is the only place in 802.11-2012 (that we have found) that the relationship is stated unambiguously (see e.g. Figure 4-2).
Distrib. System (DS)
MAC
PHY
DSAF
MAC
PHY
DSAF
requests
indications

## Slide 8: What is relationship between DSAF & DS?
Second interpretation: “The Distribution System peers with the DSAF(s) via real or virtual links.”
We’ll call this DSAF=DS (“DSAF peers with DS”).
requests
indications
MAC
PHY
MAC
PHY
Distrib. System (DS)
DSAF
DSAF

## Slide 9: What is relationship between DSAF & DS?
Third interpretation: “The Distribution System utilizes instances of a service provided by the AP(s).”
We’ll call this DS/DSAF (“DS over DSAF”).
Distrib. System (DS)
MAC
PHY
DSAF
MAC
PHY
DSAF
requests
indications

## Slide 10: What the DS is NOT (I hope!)
Non-useful interpretation: “The Distribution System’s position in the layering diagram is undefined.”
There is no place for an undefined amorphous cloudish thingamajig in the ISO layering model.
MAC
PHY
DSAF
MAC
PHY
DSAF
DS

## Slide 11: This is the relationship for this deck
“The Distribution System provides instances of a service to the DSAF(s).”
Because this is the only one to which these authors can find a specific reference in IEEE Std 802.11.
Distrib. System (DS)
MAC
PHY
DSAF
MAC
PHY
DSAF
requests
indications

## Slide 12: A standard view of that same network in 802.11 today
Distribution System (DS)
MAC
PHY
MAC
PHY
MAC
PHY
AP STA 1
Non-AP STAs
MAC
PHY
AP STA 2
unspecified
portal
AP
AP
MAC
PHY
802.3
This is similar to IEEE 802.11-2012, Figure R-1, but drawn with “request down indication up” rigorously applied.
The DS has three users, two APs and a portal, so is shown passing behind a MAC.

## Slide 13: One possible 802.1AC-to-portal architecture
A connecting link is required, because the portal uses a SAP; it does not provide one.
Therefore an 802.1AC convergence layer specific to 802.11 is not necessary.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
portal
AP
MAC
PHY
MAC
PHY
anything, e.g. 802.3
802.3
MAC
PHY
802.1Q bridge relay
MAC
PHY
MAC
PHY
Non-AP station
end station

## Slide 14: But, there is an alternate approach.
This interface is defined.
It is the DS_SAP, illustrated in IEEE Std 802.11-2011 Figure R-1.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
portal
AP
MAC
PHY
MAC
PHY
anything, e.g. 802.3
802.3
MAC
PHY
802.1Q bridge relay
MAC
PHY
MAC
PHY
Non-AP station
end station

## Slide 15: So, another representation could be …
That is, the 802.1AC Clause 12.2.1 “portal convergence function” is not an interface to a portal; .1AC 12.2.1, plus a bridge relay function, is an example of a portal.
.1AC 12.2.1 connects the ISS to the DS_SAP.
Distrib. System (DS)
MAC
PHY
AP STA
unspecified
AP
802.1Q bridge relay
MAC
PHY
Non-AP station
MAC
MAC
802.3
PHY
PHY
end station
.1AC
One example (of many) of a portal

## Slide 16
New for 802.11ak consideration…

## Slide 17
MAC
PHY
MAC
PHY
PHY
MAC
AP STA 2
PHY
MAC
AP STA 1
Non-AP STAs
802.3
Extending this to P802.11ak + P802.1Qbz
MAC
PHY
802.1Q bridge relay
AP
AP
Conv.
Funct
.1AC CF
SAP[ ]
SAP
SAP
.1AC CF
SAP[ ]
SAP
SAP
That is, 802.1AC/802.11ak are defining a SAP and a convergence function that supports multiple, logical links as seen by the Bridge, to each of the 11ak-aware non-AP endpoints.
Note: “SAP” is a single instance, “SAP[]” has a port vector.
802.1AC 12.2.2

## Slide 18: P802.11ak and non-11ak STNs on one AP.
DS
AP w/Bridge and
non-11ak (legacy) access
11ak STAs
MAC
PHY
MAC
PHY
Non-11ak STAs
MAC
PHY
MAC
PHY
AP
Bridge
.1AC
MAC
PHY
.1AC
SAP[ ]
SAP
SAP
SAP[ ]
SAP
802.1AC 12.2.2
802.1AC
12.2.1

## Slide 19: P802.11ak and non-11ak STNs on two APs.
Non-
11ak
STA(s)
11ak
STA(s)
Non-
11ak
STA(s)
11ak
STA(s)
AP w/Bridge and
non-11ak (legacy) access
AP w/Bridge,
uses DS
for non-11ak access
.1AC 12.2.2
.1AC 12.2.2
DS
MAC
PHY
MAC
PHY
MAC
PHY
MAC
PHY
AP
Bridge
.1AC 12.2.1
MAC
PHY
MAC
PHY
AP
Bridge
Note that connectivity between this 11ak STN and the other stations depends on some connection between the Bridges not shown.
isolated

## Slide 20: P802.11ak and non-11ak STNs on two APs.
Non-
11ak
STA(s)
11ak
STA(s)
Non-
11ak
STA(s)
11ak
STA(s)
AP w/Bridge and
non-11ak (legacy) access
AP w/Bridge,
uses DS
for non-11ak access
.1AC 12.2.2
DS
.1AC 12.2.2
DS
MAC
PHY
MAC
PHY
MAC
PHY
MAC
PHY
AP
Bridge
.1AC 12.2.1
MAC
PHY
MAC
PHY
AP
Bridge
Now, all stations are fully connected, and the DS is split.
1AC 12.2.1

## Slide 21: P802.11ak and non-11ak STNs on two APs.
It is important to understand that the DS does NOT somehow morph to include the bridge!
The reason is that, once the data hits the bridge, it belongs to all bridge peers, e.g. other DSs that are using the same bridged network. The DS is not a peer of the bridge. The bridge is not part of the DS.
.1AC 12.2.2
DS
.1AC 12.2.2
DS
MAC
PHY
MAC
PHY
MAC
PHY
MAC
PHY
AP
Bridge
.1AC 12.2.1
MAC
PHY
MAC
PHY
AP
Bridge
1AC 12.2.1
DS
X

## Slide 22: P802.11ak and non-11ak STNs on two APs.
  DS tunnel
DS
It is certainly possible to invert the stack using a DS tunnel technology (mac-in-mac, Ether-over-VPLS-over-MPLS-over-Ether, etc.) to make a single DS.
But then, you’re back to a single 12.2.1 portal.
.1AC 12.2.2
.1AC 12.2.2
DS
MAC
PHY
MAC
PHY
MAC
PHY
MAC
PHY
AP
Bridge
.1AC 12.2.1
MAC
PHY
MAC
PHY
AP
Bridge

## Slide 23: To summarize
A given DS has exactly one Portal to a Bridged LAN, no matter how many APs it serves.
If, in order to avoid sending a packet from AP1 to AP2 and back again, you would like to have multiple Portals, you have to separate the DSs, and let the Bridge LAN move the data.