## Slide 1: Residential Scenario CCA/TPC Simulation Discussion
Date: 2014-05-13
Authors:

## Slide 2: Abstract
In this submission we report the results of simulations with varying CCA threshold and transmit power adjustments in the Residential Scenario. Data throughput and delay are shown as a result of the applied power and threshold values.

## Slide 3: Simulation Scenario and Assumptions
We have chosen to use:
  The Residential Apartment Building scenario, with some minor modifications [1]
    APs are centered in the apartment
    Penetrations loss (floor/wall) [4,5], [2, Table3]:
  802.11n MAC simulations
    A full buffer traffic model, with FTP over TCP, run for 80 sec (after warm-up)
    Adaptive Auto Rate Fallback (AARF)
    1500 byte packets
  AWGN 20 MHz PHY, 5 GHz Band, 2x2 MIMO, TGn B
  Additional simulation details are in the appendix

## Slide 4: Simulation Cases
We provide simulation results (throughput and delay) for the following cases (all single channel):
  A single floor re-use of 1 with all apartments active
    Ran simulation with and without penetration losses
  Frequency re-use 1 with all apartments active
  Frequency re-use 3 with 1/3 apartments active

## Slide 5
Observations:
  Throughput peaks at a CCA level. For the plot without penetration loss, the peak is at -70 dBm. For the plot with penetration loss, approximately -70 to -80 dBm.
  Throughput results vary at each CCA with changing Tx power level.
  Conclusions:
    Increasing CCA level widens opportunities for concurrent OBSS transmission – increasing global throughput while increasing OBSS interference.
    Wall and floor penetration losses increase throughput through the suppression of OBSS interference.
One Floor Global UL Throughput - Re-use 1
No Penetration Loss
With Penetration Loss

## Slide 6
  Conclusions:
    Higher CCA and Tx power levels increase OBSS interference. Tx power mitigates it somewhat by increasing received signal level.
    Wall and floor penetration losses reduces delay significantly via the suppression of OBSS interference.
One Floor Global UL Delay - Re-use 1
No Penetration Loss
With Penetration Loss

## Slide 7
  Conclusions:
    Delay shows significantly different performance depending on Tx power and CCA level.
    The lowest delay appears to be at a CCA level of -80dBm.
    Throughput appears to be saturated with little dependence on Tx power or CCA level.
      Previously reported results show throughput variation with CCA level.
      Therefore, we decided to attempt to reduce the saturation by introducing a reuse of 3.
Five Floors: Global UL Comparison - Re-use 1

## Slide 8: Reuse 3 (single channel)
511 | 512 | 513 | 514 | 515 | 516 | 517 | 518 | 519 | 520
501 | 502 | 503 | 504 | 505 | 506 | 507 | 508 | 509 | 510
5th Floor
411 | 412 | 413 | 414 | 415 | 416 | 417 | 418 | 419 | 420
401 | 402 | 403 | 404 | 405 | 406 | 407 | 408 | 409 | 410
4th Floor
311 | 312 | 313 | 314 | 315 | 316 | 317 | 318 | 319 | 320
301 | 302 | 303 | 304 | 305 | 306 | 307 | 308 | 309 | 310
3rd Floor
211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220
201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210
2nd Floor
111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120
101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110
1st Floor
10m
10m
3m
3m
3m
3m
Active
Co-channel apartments

## Slide 9
  Observations:
    Throughput results appear to saturate above -90 dBm CCA level.
      At -90 dBm CCA, there’s some degradation at highest Tx power level.
    Delay results vary at each CCA with changing Tx power level.
    Delay appears lowest at -80 dBm CCA level with lowest Tx power level.
Five Floors: Global UL Comparison - Re-use 3

## Slide 10: Summary/Conclusions
Discrete combinations of CCA and Tx power levels were explored in the HEW Residential Scenario.
Throughput and delay results show sensitivity to geometry assumptions in [1].
Calibration efforts to refine assumptions are needed before technology evaluations are made.

## Slide 11: References
IEEE 802.11-13/1001r8, HEW SG Simulation Scenarios, Qualcomm, et.al., March 2014
ITU-R P1238-7, Propagation data and prediction methods for the planning of indoor radio communication systems and radio local area networks in the frequency range 900 MHz to 100 GHz, 02/2012
IEEE 802.11-13/1487r1, Dense Apartment Complex Capacity Improvements with Channel selection and Dynamic Sensitivity Control, DSP Group, December 2013
IEEE 802.11-14/0082r0, Improved Spatial Reuse Feasibility – Part I, Broadcom, January 2014
IEEE 802.11-14/0083r0, Improved Spatial Reuse Feasibility – Part II, Broadcom, January 2014
IEEE 802.11-14/0523r0, MAC simulation results for Dynamic sensitivity control (DSC - CCA adaptation) and transmit power control (TPC), Orange, April 2014
IEEE 802.11-13/1359r1, HEW Evaluation Methodology, Broadcom, et.al., March 2014

## Slide 12: Appendix

## Slide 13: Simulation Assumptions (1 / 2)
TGax (HEW) Apartment Building Scenario (based upon 11-13/1001r8)
Modified 11-13/1001r8 Assumptions
 | Scenario Name | Topology | Management | Channel Model | Homogeneity | ~Traffic Model
1 | Residential | A - Apartment bldg. e.g. ~10m x 10m apts in a multi-floor bldg ~10s of STAs/AP, P2P pairs | Unmanaged | Indoor | Flat | Home
Parameter | Value
Topology | 
Topology Description | Multi-floor building 5 floors, 3 m height in each floor 2x10 rooms in each floor Apartment size: 10m x 10m x 3m
APs location | One AP per apartment at center location at 1.5m above the floor level.
AP Type | 802.11n, 20 MHz BW nodes. All nodes in each apartment are associated with the apartment’s AP (BSS). All BSS use the same channel.
STAs location | Random xy-locations (uniform distribution) at 1.5m above the floor level (no minimum distance from the AP)
Number of STAs | In each apartment, 5 STAs
Channel model | TGn channel model B GF Wall penetration loss = 13 dB, Floor penetration loss = 13 dB; No interior walls; Penetration loss expression below (11-14/0083r0); Penetration loss values (ITU-R P1238-7 (2012) Table 3)
Frank LaSita, InterDigital

## Slide 14: Simulation Assumptions (2 / 2)
Parameter | Value
PHY parameters | 
Center frequency and BW: | All BSSs at 5GHz, using 20 MHz BW
MCS: | 802.11n MCS 8 – 15 using Adaptive Auto-Rate Fallback (AARF) Link Adaptation
GI: | Long, 800 ns
Data Preamble: | 802.11n
STA TX power Adjustments | 17 dBm; 14 dBm; 11 dBm;
AP TX Power | 23 dBm; 20 dBm; 17 dBm;
AP #of TX antennas | 2 for 802.11n (Nss = 2)
AP #of RX antennas | 2 for 802.11n (Nss = 2)
STA #of TX antennas | 2 for 802.11n (Nss = 2)
STA #of RX antennas | 2 for 802.11n (Nss = 2)
AP antenna gain | 0 dBi
STA antenna gain | 0 dBi
CCA Threshold | -90 dBm; -80 dBm; -70 dBm; -60 dBm; -50 dBm
Noise Figure | 5 dB
MAC parameters | 
Access protocol parameters: | EDCA with default parameters for 802.11n
Primary channels | 5GHz All BSS use one 20 MHz channel.
Aggregation: | Maximum transmitted A-MSDU size = 7935 B; Maximum acceptable A-MPDU size = 65535 B
Max # of retries | Maximum retries = 4
RTS/CTS Threshold | No RTS/CTS
Fragmentation Threshold | None
Rate adaptation method | Adaptive Auto-Rate Fallback (AARF)
Association | 100% of STAs in an apartment are associated to the AP in the apartment
Management frames | Periodic, 100 msec Beacons No probing or association messaging
Frank LaSita, InterDigital

## Slide 15: Additional Simulation Details
Performance Results
  Average Global (Aggregate) Throughputs
    Throughput results are calculated from the average of drop throughputs (10 drops). Each drop throughput is determined by dividing the total number of bits successfully received during the drop by the transmission duration.
    Represents the total average data traffic in bits/sec successfully received during the bucket duration and forwarded to the higher layer by the WLAN MAC. This statistic does not include the data frames that are
      1) unicast frames addressed to another MAC,
      2) duplicates of previously received frames, and
      3) incomplete, meaning that not all the fragments of the frame were received within a certain time, so that the received fragments had to be discarded without fully reassembling the higher layer packet.

## Slide 16: Additional Simulation Details
Performance Results
  Global Average Delay
    Delay results are calculated from the average of the drop delays (10 drops). Each drop delay is comprised of bucket delays which are averages over each bucket duration.
    Represents the average end to end delay of all the data packets that are successfully received during the bucket duration by the wireless LAN MACs of all WLAN nodes in the network and forwarded to the higher layer. This delay includes medium access delay at the source MAC, reception of all the fragments individually (if any), and transfer of the frames via AP, if the source and destination MACs are non-AP MACs of the same infrastructure BSS. The medium access delay at the source MAC - includes queuing and medium access delays.