## Slide 1: Further Discussions on PHY Abstraction
Date: 2014-05-16
Authors:
Name | Affiliations | Address | Phone | email
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-3847 | yakunsun@marvell.com
Jinjing Jiang | Marvell Semiconductor |  |  | 
Yan Zhang | Marvell Semiconductor |  |  | 
Hongyuan Zhang | Marvell Semiconductor |  |  | 

## Slide 2: ESM for PHY Abstraction
Effective SINR is an average mapped equalizer-output SINR over all subcarriers.
  Hedge factors alpha and beta can be used to calibrate and compensate any residual errors, if necessary.
OFDM transmission is modeled as an AWGN channel with one effective SINR.

## Slide 3: Effective SINR Mapping Functions
PHY Abstract | SINR Mapping | 
EESM | Exponential mapping | 
CM based RBIR | Mutual information assuming CM | 
BICM based RBIR | Mutual information assuming BICM | 
MMIB | Mutual information by LLR channels | 

## Slide 4: Benefit of MIESM
Mutual information based ESM (MIESM) has been proposed for PHY abstraction [1,2,3].
  RBIR and MMIB are basically equivalent, just two approaches to compute the mutual information conditioned on the modulation.
MIESM based effective SNR vs. PER performance is channel type independent.
  1 set of PER look up tables is enough, very easy to implement in SLS
  highly extensible for any future technologies (and the associated effective channels/scenarios)
  Very easy to calibrate across companies (no or minimal number of tuning parameters)
Minimal effort in implementing MIESM.
  Merely a lookup table (RBIR) or a closed form (MMIB) for a packet (with a MCS).
Implementation loss can be included in per tone SINR calculation
  After a modeling of SINR loss, the procedure of ESM is identical as ideal receiver.
  enable using ideal receiver performance as PER LUT baseline

## Slide 5: Independence on Channel Type
Channels simulated:
  AWGN, B_LOS/NLOS, D_NLOS, F_NLOS
  An extreme channel type “X”: Equal power PDP with the delay spread of channel F (600ns).
20MHz, 2.4GHz, 1x1, 8000 bits per packet.
Ideal channel estimation
PHY-abstraction: RBIR-BICM based
  The results of RBIR-CM/MMIB based PHY abstraction (not plotted) are very close.
Effective SNR vs. PER for different channel types are within a very small range.
  RBIR-based PHY abstraction is robust to channel frequency selectivity (and frequency selective interference).
  Using a universal (AWGN) curves to predict PER for various types of channels are reliable.

## Slide 6: Independence on Channel Type (2)
AWGN (black)
D_NLOS(blue)
F_NLOS(red)
X_NLOS (green)
Effective SNR vs. PER for a large variety of channel types (AWGN, B-LOS/NLOS, D/F/X-NLOS) are almost identical.
B_LOS (cyan)
B_NLOS (magenta)

## Slide 7: Independence on Channel Type (2)
AWGN (black)
D_NLOS(blue)
F_NLOS(red)
X_NLOS (green)
Effective SNR vs. PER for a large variety of channel types (AWGN, B-LOS/NLOS, D/F/X-NLOS) spans 0.5dB±0.2dB.
B_LOS (cyan)
B_NLOS (magenta)

## Slide 8: Frequency Selective Interference
Frequency selective interference can be experienced in OBSS scenarios and caused by potential 11ax technologies such as OFDMA.
PHY abstraction should be accurate and robust in this case.
  Infinite number of possible interference levels, cannot rely on tune-up per case.
Interference Level
Freq

## Slide 9: Freq Selective Interference – 10dB Rise
Assume ¼ of tones are under 10dB stronger interference.
  AWGN, BCC, MCS 0/7
Compare effective SNR vs. PER results against those of various channel types in the previous results.
Interference Level
freq
10dB
0.25*Ntone
0.75*Ntone

## Slide 10: Robustness to Freq Selective Interference
Effective SNR vs. PER for 10dB interference rise well aligned with results of various channel types w/ flat noise.
MIESM is accurate and robust to the frequency selective interference.

## Slide 11: PER Prediction
TGac channel: D-NLOS, F-NLOS, B-LOS
  Channel realizations in PER prediction simulations are independent with the ones used for effective SNR vs. PER lookup table generation.
  Case 1: one randomly selected (and fixed) channel realization
  Case 2: 4000 channel realizations
PER is obtained for each SNR point in two ways:
  Simulated: count by decoding errors
  Predicted: predict PER by PHY abstraction.
    For each channel realization:
      Calculate a PER based on effective SNR (from RBIR mapping),
      Then flip a coin to decide if the packet is correctly received based on the calculated PER. (Namely, draw a random variable x ~U[0,1]; packet fails if x < PER.)
    PER = total number of failed packets/total number of packets.
Predicted PER is very close to simulated PER.
  Using RBIR and AWGN curves to predict PER for various types of channels are reliable.

## Slide 12: Case 1: A Random/Fixed Channel Realization (D_NLOS)
For an arbitrary channel realization, PER prediction by RBIR-based PHY prediction is accurate for LDPC and less than 0.3dB offset (PER=10%) for BCC.

## Slide 13: Case 1: Statistics on More Random/Fixed Channel Realizations (D_NLOS)
Okay, we can be lucky in the previous specific random and fixed channel realization.
100 more tests on random/fixed channel realizations.
Look at the SNR offset @ PER = 10% for each channel realization.
MCS | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Mean (dB) | -0.35 | -0.42 | -0.39 | -0.21 | -0.31 | -0.17 | -0.13 | -0.41 | -0.13 | -0.29
Var (dB) | 0.74 | 0.73 | 0.97 | 0.51 | 0.89 | 0.50 | 0.81 | 0.78 | 0.49 | 0.60
MCS | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Mean (dB) | 0.01 | -0.02 | -0.01 | 0.01 | -0.05 | -0.11 | -0.03 | 0.07 | 0.07 | 0.01
Var (dB) | 0.19 | 0.15 | 0.20 | 0.10 | 0.18 | 0.12 | 0.11 | 0.19 | 0.18 | 0.12
LDPC
BCC

## Slide 14: Case 2: 4000 Channel Realizations (D_NLOS)
PER prediction by RBIR-based PHY prediction is accurate for LDPC and less than 0.5dB offset (PER=10%) for BCC over channel realizations.

## Slide 15: Case 2: 4000 Channel Realizations (F_NLOS)
Same observation as D-NLOS channel

## Slide 16: Case 2: 4000 Channel Realizations (B_LOS)
Similar observation as D-NLOS channel (even less offset for BCC)

## Slide 17: Conclusions
MIESM-based PHY abstraction is independent to channel types/interference scenarios.
AWGN-based SNR vs. PER lookup table can accurately predict PER for various channel types.

## Slide 18: Reference
[1] 11-14-0117-00-0hew-PHY-abstraction-for-HEW-system-level-simulation
[2] 11-13-1131-00-0hew-phyabstraction-for-hew-system-level-simulation
[3] 11-14-0353-00-0hew-suggestion-on-phy-abstraction-for-evaluation-methodology
[4] 11-14-0043-02-0hew-PHY-abstraction-in-system-level-simulation-for-HEW-study
[5] 11-14-0335-00-0hew-instantenous-sinr-calibration-for-system-simulation