## Slide 1: Further Discussions on Instantaneous SINR Calibration for System Simulation
Date: 2014-05-11
Authors:
Name | Affiliations | Address | Phone | email
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-3847 | yakunsun@marvell.com
Jinjing Jiang | Marvell Semiconductor |  |  | 
Yan Zhang | Marvell Semiconductor |  |  | 
Hongyuan Zhang | Marvell Semiconductor |  |  | 

## Slide 2: Overview
The discussions on instantaneous SINR calibration for SLS have been kicked off [1,2]
Several different options on how this should be done
We have some further results and discussions on this topic

## Slide 3: Recap on Our Previous Results [1]
Method of SINR collection:
  Minimal MAC: CSMA (EDCA with default parameters)
  Fixed MCS for all nodes, fixed packet size.
  Collect SINR at the equalizer output for the desired packet.
Calibration metric as the distribution of
  Option 1: SINR per tone
  Option 2: Effective SNR per packet
By-product:
  To simplify the SLS complexity, approximate some interfering channels, whose signal is below a threshold, to be AWGN
  Use the distribution of instantaneous SINR to determine the threshold
    With maximum interfering channels simplified and
    with the minimal impact on SINR introduced
  The step2 calibration is the perfect time to study and agree on such a threshold.

## Slide 4: Further Discussions (1) – Simple MAC
MAC = channel access rule for this step  simple MAC
Why channel access rule for SINR calibration?
  Instantaneous SINR naturally implies some channel access.
  Avoid additional work to bypass channel access.
    Typically fading channel generation is deeply embedded in the simulator.
    Instantaneous SINR collection with no channel access (as done for long term SINR) requires additional work.
A minimalist MAC is preferable for instantaneous SINR calibration
  Option 1: CSMA
  Option 2: CCA-only

## Slide 5: Simple MAC: CCA-only Model
A slotted transmission is assumed
  Each transmitting node will transmit simultaneously and over a fixed/identical duration.
  In each slot, some nodes are active (try to access the channel) depending on UL/DL traffic ratio.
Who to transmit? CCA-based channel access rule
  All active nodes are independently ordered for each slot, nodes up front has a high probability of transmission.
  Each node checks for CCA to determine if it can access the channel.
  Interference only counts already determined transmitters at the moment of CCA.
  One node per BSS can transmit.
After the transmitting nodes are selected for a given slot, compute the instantaneous SINR at each receiver.
  Determine the desire receiver for each transmitting node: AP (if node is STA) or a random STA associated with node (if node is AP).
  Interference comes from all undesired transmitting nodes through fading channels.

## Slide 6: An Example of CCA-only Channel Access

## Slide 7: Comparison on Simple MAC Models
 | Pros | Cons
CSMA | Captures the close-to-reality SINR Enables the study of interfering channel approximation | More effort is needed to implement.
CCA-only | Very easy to implement | The results are only accurate with respect to the channel calibration. Hardly useable for future system performance evaluation due to inaccuracy

## Slide 8: Further Discussions (2): SINR Metric
Option 1: SINR per tone
Option 2: Effective SNR per packet
SINR per tone is preferred because:
  SINR per tone is simpler  available before effective SNR mapping and no additional processing
  Effective SNR is a highly compressed value for the fading channel, hiding the mismatch of channel implementation
  The reason of calibrating via effective SNR is to guarantee the system performance afterward (the same effective SNR, the same PER/Throughput). No consensus on effective SNR yet.

## Slide 9: Procedure of Statistics Collection
Detailed PHY is assumed
  Fading channel models, Doppler spectrum, and antenna correlation (if MIMO) defined by scenarios
  Receiver algorithm is reflected (MMSE for MIMO, or MRC for single stream)
  PER decision is not required (irrelevant) at this step
Simple MAC is assumed
  CCA-only
  CSMA
    Full buffer traffic (active nodes always try to access channel)
    Each AP and STA transmits a packet of a fixed (and equal) size at a fixed MCS.
    Only collect the desired data frame.
Multiple drops of AP/STAs are simulated for a scenario
  In each drop, collect the equalizer-output SINR
Generate the distribution (CDF) of dynamic physical layer receiver output SINR

## Slide 10: Simulation Setup
Simulation is based on scenarios in [3].
  Distribution of uplink instantaneous SINR are plotted as an example.
  We can select only one scenario for calibration.
Detailed/optional simulation assumptions:
  2.4GHz Channel with 20MHz Bandwidth
  No antenna gain, no cable loss
  1 Tx and 1 Rx are assumed (other than defined in [3])
  STAs and APs are dropped and associated based on scenario [3]
  CSMA:
    EDCA with AC2 for all STAs/APs (using default parameters)
    MCS 7, each packet of 1584 bytes
  CCA-only:
    1 slot = 1 ms
    CCA_level = -82dBm

## Slide 11: Simulation Assumptions (Scenario 1)
Parameter | Value
Number of STAs | 4 STAs per apartment
Channel Model | TGn B (AP-AP, STA-STA, AP-STA)
Penetration Loss | Wall 12dB, Floor 17dB, linear for multiple walls/floors
BW | 20MHz at 2.4GHz. Each BSS randomly selects one channel out of 3.
TX Power | AP: 23dBm, STA: 17dBm
Association | 100% STA in an apartment associated with the AP in the room.

## Slide 12: Instantaneous UL SINR Per Tone
SINR by CCA-only has a different distribution than that of CSMA, due to the synchronous vs. asynchronous transmissions.

## Slide 13: Simulation Assumptions (Scenario 2)
Parameter | Value
Number of STAs | 4 STAs per cubicle, 4 AP per BSS
Channel Model | TGn D (AP-AP, STA-STA, AP-STA)
Penetration Loss | Wall 7dB, linear for multiple walls
BW | 20MHz at 2.4GHz. Each AP selects one channel out of 4 in a BSS. (BSS4k+1,BSS4k+2,BSS4k+3,BSS4k+4)= (ch1,ch2,ch3,ch4)
TX Power | AP: 24dBm, STA: 21dBm
Association | 100% STA in a BSS associated with an AP in the BSS by RSSI, no P2P STA
Based on [2] before the document was updated at the meeting.

## Slide 14: Instantaneous UL SINR Per Tone

## Slide 15: Simulation Assumptions (Scenario 3)
Parameter | Value
Environment | BSSs in Hexagon (figure 5), simulated BSS in 1 channel (figure 6) BSS radius: R=7m
Number of STAs | 30 STAs per BSS
Channel Model | TGn D (AP-AP, AP-STA), TGn B (STA-STA)
Penetration Loss | None
BW | 20MHz at 2.4GHz. Each simulated BSS selects the same channel.
TX Power | AP: 17dBm, STA: 15dBm
Association | 100% STA associated with the strongest AP

## Slide 16: Instantaneous UL SINR Per Tone

## Slide 17: Simulation Assumptions (Scenario 4)
Parameter | Value
Environment | BSSs in Hexagon (figure 8), ICD = 130m
Number of STAs | 10 STAs per BSS (100% outdoor)
Channel Model | UMi (AP-AP, AP-STA, STA-STA)
Penetration Loss | None
BW | 20MHz at 2.4GHz. Each simulated BSS selects the same channel.
TX Power | AP: 30dBm, STA: 15dBm
Association | 100% STA associated with the strongest AP

## Slide 18: Instantaneous UL SINR Per Tone

## Slide 19: Summary
Two options of instantaneous SINRs calibration are proposed.
Suggestion1:
  Use SINR per tone given its convenience and readiness.
Suggestion2:
  Use simple MAC for channel access
  Open to discussion on CSMA or CCA-only

## Slide 20: References
[1] 11-14-0335-00-0Instantaneous-SINR-Calibration-For-System-Simulation
[2] 11-14-0307-00-0PHY-Calibration-Results
[3] 11-13-1001-06-0hew-HEW-evaluation-simulation-scenarios-document-template