## Slide 1: Discussions on adaptive frame length in MAC based on block ACK
Date: 2014-05-05
Authors:
Name | Affiliations | Address | Phone | Email
Ningbo Zhang | Beijing University of Posts and Telecommunications (BUPT) | Xitucheng Road 10, Haidian District, Beijing, China | 15810007211 | nb52zhang@gmail.com
Guixia Kang |  |  | 13911060877 | gxkang@bupt.edu.cn
Bingning Zhu |  |  | 13811625409 | 407549401@qq.com
Doc.: IEEE 11-14-0613-00-00ax

## Slide 2: Background
Frame length is an essential impact on performance of WLAN
  Next generation WLAN network expects for higher throughput and more adaptive schemes in MAC layer
  Frame length directly impacts the throughput and efficiency of MAC layer
  It seems necessary to get the optimal frame length in different situation
Frame aggregation and BA (Block Acknowledgement) are discussed in previous study
  In the latest IEEE 802.11ac [1] and 802.11ad [2], above technologies are both introduced and enhanced
  In [3], step by step detailed procedure for a system simulation based on MAC/PHY features of 802.11 is discussed
  In [4], MAC efficiency is analyzed considering both frame aggregation and BA for dense deployment scenarios
This contribution is to discuss adaptive frame length
Doc.: IEEE 11-14-0613-00-00ax

## Slide 3: Current enhanced MAC scheme
Two main technologies: Frame Aggregation and Block Acknowledgement
MAC efficiency is influenced by
  Number of blocks in an aggregated frame
  Number of BAs
  Number of retransmission
RTS
CTS
Aggregated
Frame
BA
pr
pr
pr
pr
SIFS
SIFS
SIFS
DIFS
CW (variable)
overhead
overhead
Actual data
BA
pr
SIFS
SIFS
overhead
Variable, no more than
maximum length
MAC throughput =
Total MAC payload (bits)
Time consumed for transmitting total MAC payload (sec)
MAC efficiency =
MAC throughput
PHY rate
Aggregated
Frame
pr
Doc.: IEEE 11-14-0613-00-00ax

## Slide 4: Frame aggregation
The frame aggregation structure is illustrated in the figures
  Frame aggregation schemes mainly include A-MSDU and A-MPDU, which are classified by different sub-frames being aggregated.
  In MAC layer, MSDU(MAC Service Data Unit) combines with header, additional information to form MPDU(MAC Protocol Data Unit).
Doc.: IEEE 11-14-0613-00-00ax

## Slide 5: Block Acknowledgement
The BA scheme is illustrated in the figure above
  BA always used to enhance the performance of frame aggregation schemes.
  The receiver sends a BA frame to feedback that it has received the data frame.
  The bit map in BA indicates whether each block is transmitted correctly or not.
Doc.: IEEE 11-14-0613-00-00ax

## Slide 6: Performance analysis of current MAC
Advantages
  Frame aggregation and BA obviously decrease MAC header, inter-frame space, number of BAs and other additional overhead;
  Furthermore, the media contention time is incurred only once in the transmission of the large frame instead of multiple small packets;
  Thus can increase throughput and efficiency in MAC layer.
  Disadvantages
  As wireless links are error-prone and changeable, the probability of the successful transmission of a large frame might be smaller than multiple small packets.
  Find the optimal frame size  decrease retransmission number
  & get the highest efficiency
Doc.: IEEE 11-14-0613-00-00ax

## Slide 7: Proposed adaptive frame length scheme
Self adaptive frame size scheme: based on the block ACK in each BA frame.
Detailed description for the scheme:
  1. Set initial parameters at the transmitting terminal:
    Block numbers in aggregated frame as and its maximum value as , error block numbers computed based on BA frame as , threshold of to determine the change of
  2. the adaptive value of based on
  3. The transmitter sends a frame with blocks. The receiver responds with BA frame. Then the transmitter updates the parameters’ value based on the information in BA frame and starts to transmit again.
Doc.: IEEE 11-14-0613-00-00ax

## Slide 8: Performance Analysis -----parameters
Pervious study has proved that MAC access mechanisms and the number of nodes have less effect on the optimal frame length. For simplicity, we set access mechanism, the number of nodes and frame aggregation scheme as DCF with RTS/CTS, 5 and A-MSDU, respectively. Other detailed parameters are shown in the right table.
Name | Description | 802.11ac
threshold | Threshold of error sub-frames | 1
Slot | Slot time | 9 us
SIFS | SIFS duration | 16 us
DIFS | DIFS duration | 34 us
Lrts | RTS frame size | 20 bytes
Lcts | CTS frame size | 14 bytes
Lback | Block ACK frame size | 24 bytes
Lhdr | MAC overhead | 34 bytes
LmaxPL | Maximum MAC payload | 5000 bytes
CWmin,max | Contention window size | {15,127}
NAMSDU | Number of aggregated MSDU | {1,8}
δ | Propagation delay | << 1 us
Doc.: IEEE 11-14-0613-00-00ax

## Slide 9: Performance Analysis -----results
System performance including throughput, delay and number of retransmission are illustrated above.
Red curve indicates the performance of adaptive frame size scheme. Compared to fixed number of sub-frames, it is clear that the performance of proposed scheme are significantly improved.
(a) Throughput
(b) Delay
(c) Retransmission number
Doc.: IEEE 11-14-0613-00-00ax

## Slide 10: Summary
Virtue of Self adaptive frame length scheme
  Not much additional modification compared to IEEE 802.11 standards.
  Adaptive to interference and environment change.
  Clearly, adaptive scheme achieves higher throughput and better performance than non-adaptive scheme.
Next step
  Work out an optimal set of parameters for self adaptive frame length scheme.
  Calibrate the WLAN system performance with the adaptive frame length scheme for a number of simulation scenarios.
Doc.: IEEE 11-14-0613-00-00ax

## Slide 11: References
[1] IEEE 802.11ac-2013, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications--Amendment 4: Enhancements for Very High Throughput for Operation in Bands below 6 GHz,” 2013.
[2] IEEE 802.11ad-2012, “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment 3: Enhancements for Very High Throughput in the 60 GHz Band,” 2012.
[3] 11-14-0070-00-0hew-joint-mac-phy-evaluation-methodology.
[4] 11-13-0505-00-0hew-mac-efficiecy-analysis-for-hew-sg.
Doc.: IEEE 11-14-0613-00-00ax