## Slide 1: Link Adaptation for PHY SLS calibration
Date: 2014-05-12
Authors:

## Slide 2: Motivation
In evaluation methodology document [1], some parameters related to link adaptation have not been decided yet.
Based on evaluation, we propose to add some descriptions on link adaptation for MCS selection in evaluation methodology document.

## Slide 3: Link adaptation
Link adaptation is to adaptively decide the parameters related to packet transmission such as
  Number of spatial stream, MIMO type, MCS level, etc.
This contribution focuses on MCS level adaptation which is done as the following steps:
  Step 1. Set the initial SINR value. Or use the feed-backed SINR value if possible.
  Step 2. Select the best MCS level using the proper criterion based on modified SINR value1).
  Step 3. Make Tx packet using the MCS level and data size according to the MCS level.
From the next slide, we see the underlined issues in the above in detail.
1) Open loop link adaptation: SINR value here has been modified from the SINR value in step 1 by applying SINR margin as follows: SINR margin is increased by Y/(1/X-1) dB when the transmission is succeeded, and SINR margin is decreased by Y dB when the transmission is failed to satisfy Target PER (e.g. X=10%) .
Jinyoung Chun et.al, LG Electronics

## Slide 4: Issue 1. Initial SINR setting
    Option 1. Set to MCS0
      Just put initial MCS level to 0.
    Option 2. Distance-based SINR
      Calculate the initial SINR based on the distance-based values such as path loss, penetration loss, and etc.
      Option 2.1. Interference-free SNR =
        L= penetration loss + pathloss + shadowing + cable loss – BS gain,
        Ptx= Transmission Power per tone, N: thermal noise per tone
      Option 2.2. Interference-included SINR =
      ICI = the sum of the worst interference under CCA level from each BSS except its own BSS.
Jinyoung Chun et.al, LG Electronics

## Slide 5: Issue 2. SINR feedback method
    Option 1. Feed-backed SINR (feedback delay)
      Calculate SINR of latest frame and modified it using open look link adaptation, and select MCS level for next transmission.
    Option 2. Genie SINR (No feedback delay)
      Use ‘Genie SINR’ to select MCS level of the current frame.
    Notes:
      Here, we just consider SINR feedback. More feedback schemes such as sounding, beamforming, MIMO feedback are FFS.
Jinyoung Chun et.al, LG Electronics

## Slide 6: Issue 3. MCS selection method
    Option 1. Goodput-maximizing MCS selection
      Find MCS maximizing goodput=(1-PER)* Tx rate [2]
    Option 2. X % PER based MCS selection
      Find the highest MCS satisfying PER <= X % (X is typically 10)
    For both options, we consider the following two cases:
      Select MCS every TX events
      Select MCS during warm-up time and fix the MCS for all TX events within a drop (Call ‘fixed MCS’)
    Note that after some time, PER is saturated to Target PER (X %), then these two options are identical.
Jinyoung Chun et.al, LG Electronics

## Slide 7: Simulation results: initial S(I)NR setting
Distance-based SINR (Option 2.2) converges fast both in residential and in outdoor scenarios [See Appendix]
Option 1. set to MCS 0
Option 2.2. Interference-included SINR
Option 2.1. Interference-free SNR
Residential
Outdoor
(Assuming SINR margin = 2dB, 10% per based MCS selection)
Jinyoung Chun et.al, LG Electronics

## Slide 8: Simulation results: SINR feedback method
Feed-backed SINR (Option 1) has no gain both in residential and outdoor scenarios due to feedback delay
Genie SINR (Option 2) shows large gain in outdoor scenario which is more time-varying in nature.
  Genie SINR can be the upper bound of any feedback schemes.
Outdoor Large BSS scenario |  | 
DL | UL | Total
4.9 | 5.27 | 10.17
4.61 | 4.8 | 9.41
5.47 | 5.59 | 11.06
Residential scenario |  | 
DL | UL | Total
8.8 | 12.1 | 20.9
8.8 | 12.1 | 20.9
8.9 | 12.4 | 21.3
(Assuming SINR margin = 2dB, 10% per based MCS selection, warm-up time 10sec and run time 20sec)
No feedback
Option 1. Feed-backed SINR
Option 2. Genie SINR
Average throughput per BSS
Jinyoung Chun et.al, LG Electronics

## Slide 9: Simulation results: MCS selection method
Goodput maximization MCS selection (Option 1) and 10% PER-based MCS selection (Option 2) show the same results as expected.
Fixed MCS shows the similar performance with Full MCS.
(Assuming SINR margin = 2dB, Distance-based initial SINR setting, warm-up time 10sec and run time 20sec)
Outdoor Large BSS scenario |  | 
DL | UL | Total
4.94 | 5.28 | 10.22
4.91 | 5.28 | 10.19
4.9 | 5.27 | 10.17
4.92 | 5.28 | 10.2
Residential scenario |  | 
DL | UL | Total
8.8 | 12.1 | 20.9
8.72 | 11.4 | 20.12
8.8 | 12.1 | 20.9
8.72 | 11.4 | 20.12
Option 1. Goodput max.
Option 1. Goodput max. (fixed MCS)
Option 2. 10% PER-based
Option 2. 10% PER-based (fixed MCS)
Average throughput per BSS
Jinyoung Chun et.al, LG Electronics

## Slide 10: Suggestion on Evaluation Methodology
We propose to add the following descriptions on link adaptation in evaluation methodology document
Jinyoung Chun et.al, LG Electronics
Link adaptation schemes for MCS selection
  Set the initial SINR value as
    where
      L: pathloss including shadowing, cable loss, penetration loss and antenna gain,
      Ptx: transmission power per tone,
      N: thermal noise per tone
    ICI: sum of worst interference under CCA level from each BSS except its own BSS
  SINR is modified from the SINR value in 1) by applying SINR margin (margin is increased by 2/9 dB when the transmission is succeeded, and decreased by 2 dB when the transmission is failed.
  Select the highest MCS level satisfying PER <= 10 %
  Make Tx packet using the MCS level and data size according to the MCS level.

## Slide 11: Reference
[1] 11-13-1359-00-0hew-hew-evaluation-methodology
[2] IEEE 802.11-14/0083r0, “improved-spatial-reuse-feasibility-part-ii”, Broadcom
[3] 11-14-0307-00-0hew-phy-calibration-results, Broadcom
[4] 11-14-0353, “Suggestion on PHY Abstraction for Evaluation Methodology”, LG Electronics
[5] 11-13-1001-06-0hew-simulation-scenarios-document-template

## Slide 12: Appendix. Simulation parameters (1)
Jinyoung Chun et.al, LG Electronics
Simulation scenario | Outdoor Large BSS scenario | Residential
Tx/Rx power | 30/15dBm | 23/17dBm
# of users | 50 | 10
Channel model | UMi | TGnB
Penetration loss | 0 | [3]
Indoor users | 0% | N/A
# of retransmission | 10 | 4
Channel coding | BCC | 
Noise figure | 5dB | 
Interference | AWGN | 
BW | 2.4GHz, 20MHz (64 FFT) | 
GI | Long (0.8 us) | 
Antennas for AP & STA | 1x1 SISO | 
DL & UL traffic | Full buffer (DL & UL ratio: based on PHY system simulation in [2]) | 

## Slide 13: Appendix. Simulation parameters (2)
Jinyoung Chun et.al, LG Electronics
Simulation time | Warm-up time: 10s, run time: 20s, drop: 3
Data size | 1ms TXOP less fixed overhead (RTS/CTS off) Normal overhead: SIFS + ACK + 2*PLCP header - Feedback overhead: ACK frame with feedback (<1symbol = 4us)
CCA level | Preamble detection: -82dBm (both AP and STA) Energy detection: -62dBm (both AP and STA)
DL/UL ratio | 1:1 random selection
PHY abstraction | MMIB [4] with extension to 256QAM ¾ (MCS8)

## Slide 14: Appendix. PER distribution
In initial S(I)NR setting, the fluctuation of throughput is caused by the unstable PER at the first time of the simulation.
Option 2.2. Interference-included SINR
Option 2.1. Interference-free SNR
  (Assuming SINR margin = 2dB, 10% per based MCS selection, Outdoor scenario)
Jinyoung Chun et.al, LG Electronics
Option 1. set to MCS 0
Residential
Outdoor