## Slide 1: Measurements on CCA Thresholds in OBSS Environment
Date: 2014-05-13
Authors:

## Slide 2: Background
There have been some discussions on CCA threshold adjustment for 11ax [1]-[8].
The previous works have addressed the benefits of increased CCA threshold resulting greater spatial reuse in OBSS environment.
This contribution focuses on performance of the increased CCA threshold in OBSS environment where non-overlapping channels are utilized.

## Slide 3: Wi-Fi hotspot deployments
SK Telecom is operating approx. 130,000 Wi-Fi hotspots in Korea
  and many of them are operated by 802.11n APs at 2.4GHz.
Observed performance degradation in 2.4GHz dense OBSS environment
  When majority of (operator-owned) APs are operating on non-overlapping channels (e.g. 1, 5, 9, 13 channels), still there are non-negligible interferences due to spurious power emissions from adjacent orthogonal channels.

## Slide 4: Interferences from orthogonal channels in dense OBSS
In dense OBSS environment with orthogonal channel assignment,
  still APs can be located close to each other,
  and/or STAs associated with different APs can be located close to each other.
  Then the spurious power from orthogonal channels can reduce the probability of accessing the medium under the fixed CCA threshold [10]
5GHz band can benefit from large number of channels, but may suffer when it becomes crowded
Preliminary experiment to investigate whether increasing the CCA threshold of victim AP can mitigate this scenario
CH1
CH5
CH9
Transmit spectral mask for 20MHz transmission in the 2.4GHz
(FCC requires to measure emissions at 3 meters from TX)
AP@CH5 may suffer from spurious interferences from both AP@CH1 and AP@CH9
-28dBr

## Slide 5: Experiment – Set up
Common Settings
  AP: 802.11n@2.4GHz, 20MHz, 20dBm TX power, 2 Tx ant.
  STA: 802.11n@2.4GHz, Android smartphone
Interfering APs/STAs
  3 APs in CH1, each associated with 1 STA
  3 APs in CH9, each associated with 1 STA
  All STAs have continuous TCP DL traffic
Target AP/STAs
  1 AP in CH5, associated with 2 STAs
  CCA level of AP is increased from “default” to “default+40dBm”*
  Measured DL/UL TCP throughputs of CH5-STA-1 and CH5-STA-2 for 10 seconds respectively
CH9-
AP-3
CH9-
AP-1
CH1-
AP-2
CH1
AP-3
CH1-
AP-1
CH9
AP-2
10m
45m
10m
20m
CH9-
STA-1
CH1-
STA-1
CH1-
STA-2
CH9-
STA-2
CH9-
STA-3
CH1-
STA-3
CH5-AP
CH5-
STA-1
CH5-
STA-2
[Experiment layout]
* CCA Threshold on AP chipset was not accessible, we could increase RST(Receiver Sensitivity Threshold) instead which has the same effects

## Slide 6: Experiments - Results
Increasing RST about +15dBm performs optimal in our experiment, where increasing further results in poor connectivity with CH5-STA-2 (far)
Our observations on DL/UL throughput increases
  Increased AP’s RST  Increased prob. of accessing the medium  Increased DL throughput
  Increased AP’s RST  Reduced delay of DL (TCP ACK)  Increased UL (TCP DATA) throughput
Interferences from orthogonal channels can be mitigated by increasing the target AP’s RST (CCA) level
STA | CH5-STA-1 (near) |  | CH5-STA-2 (far) | 
RST (CCA) | default | default+15dBm | default | default +15dBm
DL | 14.81 | 33.52 | 4.46 | 26.21
UL | 9.47 | 18.96 | 1.55 | 8.13
[Mbps]
Chart: 
| CH5-STA-1 (near) | CH5-STA-2 (far)
DL (default) | 14.81 | 4.46
DL (default+15dBm) | 33.52 | 26.21
UL (default) | 9.47 | 1.55
UL (default+15dBm) | 18.96 | 8.13

## Slide 7: Summary
We noticed performance degradations in dense OBSS deployments even though APs are utilizing non-overlapping channels due to Adjacent Channel Interferences.
We presented preliminary experiment results showing performance improvements with the increased receive threshold on target AP.
For future works,
  investigate performance improvements under 11ax simulation scenario-based experiment settings,
  with evaluations of tradeoff regarding legacy fairness, per link SINR, and network coverage.

## Slide 8: Appendix: Previous Contributions on CCA
[1] validated improved spatial reuse with increasing CCA thresholds at the expense of decreased per-link SINR.
[2]-[7] proposed DSC (Dynamic Sensitivity Control) algorithm that adjusts each STA’s receive sensitivity based on RSSI level of the received Beacon plus additional margin.
[8] simulated performance of DSC and TPC (Transmit Power Control).
[9] introduced Inter-BSS & Intra-BSS CCA level differentiation by introducing BSS color field in 802.11ah.

## Slide 9: References
[1] 11-14/0082r0 Improved Spatial Reuse – Part I
[2] 11-13/1012r4 Dynamic Sensitivity Control
[3] 11-13/1290r1 Dynamic Sensitivity Control for HEW
[4] 11-13/1487r2 Apartment Capacity – DSC and Channel Selection
[5] 11-14/0294r2 DSC Channel Selection and Legacy Sharing
[6] 11-14/0297r0 CCA Proposal
[7] 11-14/0328r2 Dense Apartment Complex Throughput Calculations
[8] 11-14/0523r0 MAC simulation results for DSC and TPC
[9] 11-13/1207r1 CID 205 BSSID Color Bits
[10] S. Lakshmanan, et al. “Realizing High Performance Multi-radio 802.11n Wireless Networks,” IEEE SECON ‘11