## Slide 1: Dynamic Sensitivity Control Implementation
Date: 2014-May
Authors:

## Slide 2: Background
802.11 uses CSMA/CA carrier sense multiple access with collision avoidance.
STA listens before transmitting
Two methods of sensing the medium
  Physical Carrier Sense
  Virtual Carrier Sense
Clear Channel Assessment (CCA)
  OFDM transmission => minimum modulation and coding rate sensitivity (6Mbps) (-82dBm for 20MHz channel, -79dBm for 40MHz channel)
  If no detected header, 20 dB higher, i.e. -62dBm
Receive Sensitivity
  Minimum receive sensitivity defined for each PHY
This presentation intended to help with those interested in using DSC for simulations

## Slide 3: Dynamic Sensitivity Control - DSC
Scheme where STA measures the RSSI of the AP Beacon (R dBm)
Sets RX Sensitivity Threshold at (R – M) dBm, where M is the “Margin”
  Example:
    STA receives Beacon at -50dBm, with Margin = 20dB STA sets RX Sensitivity Threshold to -70dBm.
Also set an Upper Limit, L, to Beacon RSSI to cater for case when STA is very close to AP.
  Need to ensure that all the STAs in the wanted area do see each other. Hence if one STA very close to AP, then it could set RX Sensitivity too high.
  Example:
    STA receives Beacon at -15dBm, L = -30dBm, M = 20dBm
    STA sets RX Sensitivity Threshold at -30 -20 = -50dBm (NOT –35dBm)
If the RX sensitivity threshold is higher than the CCA Threshold then CCA Threshold = RX Sensitivity Threshold

## Slide 4: RX Sensitivity
  UL = Upper Limit M = Margin R = Received RSSI RX Sensitivity = RxS
  Reff = MIN (RxS, UL)
  RxS = (Reff – M)
  Example, FOR UL = -40dBm and M = 20dB
  Min RX Sensitivity = -91dBm CCA Threshold = -82dBm
Average RSSI, dBm | R effective, dBm | RX Sensitivity, dBm | CCA Threshold, dBm
-15 | -40 | -60 | -60
-30 | -40 | -60 | -60
-50 | -50 | -70 | -70
-60 | -60 | -80 | -80
-80 | -80 | -91 | -82

## Slide 5: RX Sensitivity Threshold and CCA Threshold
CCA Thresholds are as per the Standard (unchanged)
  E.g. -82dBm (OFDM 20MHz BW)
  E.g. -62dBm ED-CCA
If the RX sensitivity threshold is higher than the CCA Threshold then CCA Threshold = RX Sensitivity Threshold
If RX sensitivity threshold is lower than the CCA Threshold then CCA Threshold = Default CCA Threshold
Hence, CCA threshold is never lower than default.

## Slide 6: Hidden STAs – Fixed CCA vs DSC
DSC
Note NO hidden STAs

## Slide 7: Setting the Margin an Upper Limit
The Margin needs to be set to account for:
Large enough to provide adequate SNIR
  A STA at edge of CCA transmits at same time. The Margin is the effective SNIR. Possibility of more than one.
Large enough to account for sudden changes in reception of Beacon signal
  If STA goes behind obstruction, RSSI will drop. If the drop is higher than the Margin, then the AP Beacon is lost.
Suggested Margin is in the order of 20dB to 25dB.
Upper Limit sets the minimum area coverage
AP then sets its own Sensitivity or CCA
  Based upon the Margin and Upper Limit
  In the area of Margin + Upper Limit.

## Slide 8: Algorithm for setting RX sensitivity
The Beacon RSSI will vary as the STA moves, for example. Therefore, the calculation of the CCA threshold or Receive Sensitivity is a continuous one.
A suggested algorithm outline is:
  Start a timer T
  Record RSSI of each Beacon
    Check is > Upper Limit, if so RSSI = Upper Limit
  Calculate average RSSI
    Use a moving average such that last reading has higher influence
  Check if T > Update period (e.g. 1 second)
    No, continue
    Yes, Convert the Averaged RSSI to RX Threshold
      RX Threshold = Ave RSSI – Margin.
      Check that RX threshold not less than minimum
  In addition, check if a Beacon or consecutive Beacons are missed, and if so decrement the average RSSI by a set amount and reset the RX sensitivity instantly

## Slide 9: Summary
The default mandatory CCA levels are maintained.
DSC is basically setting the RX Sensitivity according to the strength of received signal from AP.
If RX Sensitivity > CCA threshold
  CCA Threshold = RX sensitivity
If RX Sensitivity < CCA threshold
  CCA Threshold = CCA Threshold
DSC is designed for relatively small network coverage areas so as to improve channel re-use and overall throughput in a total coverage area.