## Slide 1: Message flows for local network service discovery
Date: 2014-05-12
Authors:

## Slide 2: Abstract
Message flows for a STA to discover local network services in common network types

## Slide 3
Camera (Soft AP)
Phone (non-AP STA)
1
2
AP
?
Type 1
Type 2
Camera (non-AP STA)

## Slide 4
STA
STA
AP
Probe Request
Probe Response
Query (using multicast Data frame)
Response (using multicast Data frame)
Smartphone
Camera
Beacon
Association
AP Discovery
Service Query
Query (using multicast Data frame)
Response (using multicast Data frame)
Get IP
Advertisement (using multicast Data frame)
Current Post-Association Service Discovery in type 1
User manually determines the BSS to associate with
Launch App

## Slide 5
STA
AP
Probe Request
Probe Response
Query (using multicast Data frame)
Response (using multicast Data frame)
Smartphone
Soft AP (Camera)
Beacon
Association
AP Discovery
Service Query
Control message (using unicast Data frame)
Response (using unicast Data frame)
Operation
Remote control, browse images
Get IP
May not be necessary in Soft AP scenario
Get SSID
Current Manual PAD in type 2
User manually determines the BSS to associate with
Interworking element:
Internet (not specified),
Personal device network
Launch App

## Slide 6: The reason of doing PAD
Users typically want to accomplish a certain task by launching an application
Is Internet available? (Mail, social network, messenger, news feed …)
Is camera service available?
Is TV service available?
Is printing service available?
(The active discovery process should be service-centric rather than device-centric to reduce network traffic.)
Need to associate with the correct/suitable network for it; otherwise, user would encounter failure of connection and have to figure out the relation between network and specific service. Not friendly to users without networking knowledge.

## Slide 7
STA
STA
AP
Probe Request
Probe Response
Smartphone
Camera
Beacon
Association
AP Discovery
Advertisement (using multicast Data frame)
Query (PADP element: Request; SPI; Service Type Mask)
Response (PADP element: Response; Service Descriptor)
Query (PADP element: Request; SPI; Service Type Mask)
Response (PADP element: Response; Service Descriptor)
Transparent mode PAD in type 1 network
Interworking element: Internet (YES),
Advertisement Protocol: PADP (STP),
PAD General Query element (Service Type: Peripheral; SSDP/UPnP)
Launch App
Wake up notification
Service Query
(support or not)
Query (PADP element: Encapsulation)
Response (PADP element: Encapsulation)
Query (PADP element: Encapsulation)
Response (PADP element: Encapsulation)
Service Query
(detailed)

## Slide 8
STA
STA
AP
Probe Request
Probe Response
Smartphone
Camera
Beacon
Association
AP Discovery
Advertisement (using multicast Data frame)
Query (PADP element: Request; SPI; Service Type Mask)
Response (PADP element: Response; Service Descriptor)
Query (PADP element: Encapsulation)
Response (PADP element: Encapsulation)
Opaque mode PAD in type 1 network
Interworking element: Internet (YES),
Advertisement Protocol: PADP (STP),
PAD General Query element (Service Type: Peripheral; SSDP/UPnP)
Service Query
(support or not)
Launch App
Query (PADP element: Encapsulation)
Response (PADP element: Encapsulation)
Service Query
(detailed)
Wake up notification

## Slide 9
STA
AP
Probe Request
Probe Response
Smartphone
Soft AP (Camera)
Beacon
Association
AP Discovery
Advertisement
Interworking element: Internet (not specified),
Personal device network
PAD General Query element (Service Type: Peripheral; SSDP/UPnP)
Launch App
PAD in type 2 network
Query (PADP element: Request; SPI; Service Type Mask)
Response (PADP element: Response; Service Descriptor)
Response (PADP element: Encapsulation)
Service Query
(detailed)
Query (PADP element: Encapsulation)
Service Query
(support or not)
Possibly attaching to Beacon or Probe Response to save this step?
Notes: Advertisement, Query response -> Beacon, Probe Response
Query -> Probe Request

## Slide 10: Comparisons between the two types of network
Message flow optimizations
  The Soft AP usually has specific/limited services to provide. Selected information may be embedded in its Beacon or Probe Response rather than in Query Response to reduce network traffic
  ULP Encapsulation/Decapsulation by the AP/proxy is helpful for legacy service providing products
Power saving
  The service provider in type 1 network may enter Doze state when the STA is searching for the service
    A proxy recording the sleep situation of STA helps
    Opaque mode can be utilized
  The Soft AP also have power saving issue to solve when service discovery is required

## Slide 11: Summary
The message flows applying the existing proposed elements for the two types of network are presented
For local service discovery, the power saving situation of service providers should also be considered in AP/proxy

## Slide 12: Appendix
“3.1 Definitions
Infrastructure: The infrastructure includes the distribution system medium (DSM), access point (AP), and portal entities. It is also the logical location of distribution and integration service functions of an extended service set (ESS). An infrastructure contains one or more APs and zero or more portals in addition to the distribution system (DS).”
“ 4.3.4.2 Extended service set (ESS): The large coverage network
The DS and infrastructure BSSs allow IEEE Std 802.11 to create a wireless network of arbitrary size and complexity. IEEE Std 802.11 refers to this type of network as the ESS network. An ESS is the union of the infrastructure BSSs with the same SSID connected by a DS. The ESS does not include the DS.”

## Slide 13: Appendix
Comparison between Wi-Fi Direct (P2P) and Ad-hoc (IBSS) mode
If taking the definition of peer-to-peer (P2P) which is “Peers are equally privileged, equipotent participants in the application”, Wi-Fi Direct, despite its name “P2P”, is not a real peer-to-peer protocol. It is essentially a protocol for forming hierarchical group and mostly used to connect just two devices. The devices are only equal peers until they connect to each other, and one of them becomes group owner. After that they follow the hierarchical roles of AP and client.
By the same logic, Soft AP is not peer-to-peer and should be infrastructure BSS.

## Slide 14: Existing PADP Elements Proposal
Advertisement protocol
  STP / PADP (ref 14/260r2)
PAD General Query(aka Service Capability or Service Type Advertisement) (13/1384r3, 13/0788r5)
  Identify Service Types and ULPs Support by an AP in beacon or probe response
STP Elements
  Request
    Service Protocol Identifier (SPI), Service Type Mask
  Response
    Service Descriptor
  Encapsulation
    Exchange ULP frames using GAS protocol
  Location
    Location info about the STA requesting service info and/or location info about the service supported by the AP