## Slide 1: LB201 Scanning Related Comments
Date: 2014-05-14
Authors:

## Slide 2: Abstract
The submission discusses on scanning related comments that are given in LB201.
The 802.11mc published new revision of the 802.11mc draft on April. The latest version 2.8 has major changes in the scanning clauses.
Resolutions to all comments are available at latest on July 2014 Plenary meeting.

## Slide 3: New REVmc D2.8
The 802.11mc published on April a new revision of the 802.11mc draft
  The 802.11ai letter ballot 201 was ongoing when the draft was published
  Nothing could have been done to prevent these comments
The REVmc separated scanning functions for DMG STA (802.11ad capable STA) and non-DMG STA
  As discussed on Tue PM1, the FILS scanning enhancements will be implemented only to non-DMG STAs

## Slide 4: New REVmc D2.8
Some comments were given to 802.11ai D2.0 because it looked that 802.11ai would be defining new operation to IBSS and DMG scanning
In practise the location of the scanning rules in IBSS and DMG have moved, no new operation were added
  802.11ai incorporation to new REVmc solves these comments
The new active scanning clauses in REVmc are in good quality!
  However, the text is changed a lot in REVmc

## Slide 5: MIB Parameters for FILS Functionality
In D2.0 all FILS capability is coordinated with dot11FILSActivated MIB variable
Coordination of all FILS functionality with a single MIB variable is not useful:
  The FILS authentication should enable a DMG and OFDM / HT/ VHT capable STA to operate both in PBSS and BSS
    Otherwise additional authentication is needed for PBSS
  However, the DMG STAs have own procedures for scanning and 802.11ai scanning enhancements are not targetted for DMG STAs

## Slide 6: MIB Parameters for FILS Functionality
One solution is to define two separate MIB parameters:
dot11FILSScanningActivated
  When set to true the FILS scanning is activated
dot11FILSAuthenticationActivated
  When set to true the FILS Authentication and Higher Layer Setup are activated

## Slide 7: Measurement Pilot
Currently all FILS STAs receive Measurement Pilot (MP) frames during the scanning
AP needs to support 802.11k to transmit MP frames
  Very few or no APs in the market transmit MP frames
MP frame is similar to FILS Discovery frame, but
  The MP frames are transmitted with precise schedule
  The MP frame is much larger than FILS Discovery frame
   FILS Discovery frame is superior compared to MP frame
Proposal to group: MP frames are received if the STA is 802.11k capable
  FILS capability does not include MP frames reception during scanning

## Slide 8: Miscallenous
There are substantial number of duplications and repetition on the comments
The 802.11ai use of terms, reference numbering and unnecesssary repetition triggered many comments

## Slide 9: References
https://mentor.ieee.org/802.11/dcn/14/11-14-0565-04-00ai-tgai-lb201-comments-for-draft-2-0.xlsx
802.11 REVmc D2.8
802.11ai D2.0