## Slide 1: PHY SIG Frame Structure for IEEE 802.11aj (45GHz)
Authors/contributors:
Date: 2015-11-14
Presenter: Haiming WANG

## Slide 2
项目:中国无线个域网项目组
提案标题: [802.11aj(45GHz)PHY SIG Frame Structure 提交日期: [2014年03月19日]
摘要: [PHY SIG Frame Structure for IEEE 802.11aj (45GHz)]
提案目的: [PHY SIG Frame Structure for IEEE 802.11aj (45GHz) ]
注意事项: 此文档为辅助中国无线个域网工作组而准备，它作为工作组讨论的一个基础，不构成对提案作者和提交单位的一种约束。经过进一步的研究，此文档中的材料在形式和内容上都可能发生改变。提案作者保留对其中材料进行添加、修改和删除的权利。
提案作者 | 单位 | 电话 | E—mail | 地址
何世文 | Southeast University |  | hesw01@seu.edu.cn | 
王海明 | Southeast University |  | hmwang@seu.edu.cn | 
黄永明 | Southeast University |  | huangym@seu.edu.cn | 
洪伟 | Southeast University |  | weihong@seu.edu.cn | 
杨绿溪 | Southeast University |  | lxyang@seu.edu.cn | 
孙波 | ZTE |  | sun.bo1@zte.com.cn | 
余光识 | Southeast University |  | ygs-ymz@163.com | 

## Slide 3: Abstract
This presentation describes a New Technique proposal of the Distributed Timeslot Allocation (DTA) Mechanism for IEEE 802.11aj (60 GHz).
Using the proposed DTA mechanism, more than two non-overlapped BSSs can be established with only 2×2.16 GHz channels at 60 GHz band in China.

## Slide 4: Outline
Challenges of future WPAN
Limited spectrum resources
Requirement of high data transfer rates
Features of future WPAN
Large bandwidth
Multiple channel mode
Multi-user
Multi-stream
45GHz millimeter-wave communication
object to digital home appliances
object to ultra-high-speed wireless transmission applications
achieve 10Gbps throughput

## Slide 5: Background
Challenges of future WPAN
spectrum resources limited
high data transfer rates required
Features of future WPAN
large bandwidth
multiple channel mode
multi-user
multi-stream
45GHz millimeter-wave communication
object to digital home appliances
object to ultra-high-speed wireless transmission applications
achieve 10Gbps throughput

## Slide 6: Technology Object
The proposal presents a kind of physical layer SIG frame structure in millimeter-wave multi-user MIMO WLAN communication
The SIG frame structure try to achieve the following technical goals
  Dynamic bandwidth
  Multi-user & Multi-stream
  Energy efficiency
  Scrambler
  Single & Multi-carrier

## Slide 7: Technology Object
Dynamic bandwidth
Achieve dynamically transform of channel bandwidth for 1080MHz channel to enhance the adaptability in different channel environments and improve bandwidth utilization.
Multi-user & Multi-stream
Achieve a multi-user multi-stream control to obtain the multiplexing gain.
Energy efficiency
Achieve energy efficient communication, i.e., allow non-AP STAs in TXOP power save mode to enter Doze state during a TXOP.
Scrambler
Scrambling effectively reduces the PAPR in OFDM system .
Single carrier & Multi-carrier
Switch in single carrier and multi-carrier

## Slide 8: SIG-A structure

## Slide 9: Fields in SIG-A
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7 | SC/OFDM | 1 | Set to 0 if SC transmission is adopted for PPDU, set to 1 if OFDM transmission is adopted for PPDU;
B8 | BW | 1 | Set to 0 for 540MHz, set to 1 for 1080MHz;
B9 | Dynamic Bandwidth | 1 | If BW=1 and Duplicate=1: set Dynamic Bandwidth to 1 for allowing dynamic bandwidth; set to 0 for non allowing dynamic bandwidth. Otherwise set to 0; (Reserved)
B10-B11 | Sub-Band | 2 | Bitmap (B10-B11): If Dynamic Bandwidth=1, set to 10 for using the primary 540MHz channel, set to 01 for using the secondary 540MHz channel; set to 11 for using 1080MHz channel; Otherwise set to 00 (reserved).
Dynamic bandwidth
Notes: Agilent technologies
  E8267D PSG Vector Signal Generator, up to 44GHz, 160 MHz (extendable to 2 GHz) RF modulation bandwidth
  E4448A PSA Spectrum Analyzer, 3 Hz - 50 GHz, Analysis Bandwidth
    10 MHz analysis bandwidth (option B7J for the Basic mode)
    Optional 40 or 80 MHz analysis bandwidth to capture and measure complex signals. View the demo
    -78 dB (nominal) third order intermodulation for 40 or 80 MHz analysis bandwidth
    Up to 300 MHz analysis bandwidth for calibrated VSA measurements
Rohde&Schwarz (R&S)

## Slide 10: Fields in SIG-A
Multi-user & Multi-stream
Bit | Fields | Number of Bits | Description
B12-B29 | Length | 18 | SU：Number of data octets in the PSDU, Range 1-162143; MU：Maximum number of data octets in the PSDU of all users, Range 1-162143;
B30 | STBC | 1 | For an SU PPDU: set to 1 if space time block coding is used and set to 0 otherwise. For a MU PPDU: set to 0.
B31-B36 | GroupID | 6 | Set to the value of the TXVECTOR parameter GROUP_ID. A value of 0 or 63 indicates a SU PPDU; otherwise, indicates a MU PPDU.
B37 | Aggregation | 1 | Set to 1 indicate that the PPDU in the data portion of the packet contains an A-MPDU; otherwise, set to 0.
Notes: Agilent technologies
  E8267D PSG Vector Signal Generator, up to 44GHz, 160 MHz (extendable to 2 GHz) RF modulation bandwidth
  E4448A PSA Spectrum Analyzer, 3 Hz - 50 GHz, Analysis Bandwidth
    10 MHz analysis bandwidth (option B7J for the Basic mode)
    Optional 40 or 80 MHz analysis bandwidth to capture and measure complex signals. View the demo
    -78 dB (nominal) third order intermodulation for 40 or 80 MHz analysis bandwidth
    Up to 300 MHz analysis bandwidth for calibrated VSA measurements
Rohde&Schwarz (R&S)

## Slide 11: Fields in SIG-A
Multi-user & Multi-stream
Bit | Fields | Number of Bits | Description
B38-B48 | NSTS/Partial AID | 11 | For a MU PPDU: NSTS is divided into 4 user positions of 2 bits each. User position , where , uses bits B(38+ ) to B(39+ ). The number of space time streams for user are indicated at user position =USER position[ ], where …..,NUM-USERS-1, and the notation A[b] denotes the value of array A at index b. Zero space-time streams are indicated at positions not listed in the USER_POSITION array. Each user position is set as follows: Set to 0 for 0 space-time streams Set to 1 for 1 space-time stream Set to 2 for 2 space-time streams Set to 3 for 3 space-time streams Set to 4 for 4 space-time streams B46-B48：set to zero, reserved For a SU PPDU: B38-B39 Set to 0 for 1 space-time stream Set to 1 for 2 space-time streams Set to 2 for 3 space-time streams Set to 3 for 4 space-time streams B40-B48 Partial AID: Set to the value of the TXVECTOR parameter PARTIAL_AID. Partial AID provides an abbreviated indication of the intended recipient(s) of the PSDU.
Notes: Agilent technologies
  E8267D PSG Vector Signal Generator, up to 44GHz, 160 MHz (extendable to 2 GHz) RF modulation bandwidth
  E4448A PSA Spectrum Analyzer, 3 Hz - 50 GHz, Analysis Bandwidth
    10 MHz analysis bandwidth (option B7J for the Basic mode)
    Optional 40 or 80 MHz analysis bandwidth to capture and measure complex signals. View the demo
    -78 dB (nominal) third order intermodulation for 40 or 80 MHz analysis bandwidth
    Up to 300 MHz analysis bandwidth for calibrated VSA measurements
Rohde&Schwarz (R&S)

## Slide 12: Fields in SIG-A
Multi-user & Multi-stream
Bit | Fields | Number of Bits | Description
B49-B51 | SU MCS | 3 | For a SU PPDU: MCS index For a MU PPDU: reserved
B52 | Precoded | 1 | For a SU PPDU: Set to 1 if a Beam-forming steering matrix is applied to the waveform in an SU transmission as described in TBD, set to 0 otherwise. For a MU PPDU: Reserved and set to 1
B53 | TXOP_PS_NOT_ALLOWED | 1 | Set to 0 by AP if it allows non-AP STAs in TXOP power save mode to enter Doze state during a TXOP. Set to 1 otherwise.
B54-B69 | CRC | 16 | SIG-A check sequence. Definition of this field calculation is in TBD.
B70-B71 | Reserved | 2 | Reserved
Notes: Agilent technologies
  E8267D PSG Vector Signal Generator, up to 44GHz, 160 MHz (extendable to 2 GHz) RF modulation bandwidth
  E4448A PSA Spectrum Analyzer, 3 Hz - 50 GHz, Analysis Bandwidth
    10 MHz analysis bandwidth (option B7J for the Basic mode)
    Optional 40 or 80 MHz analysis bandwidth to capture and measure complex signals. View the demo
    -78 dB (nominal) third order intermodulation for 40 or 80 MHz analysis bandwidth
    Up to 300 MHz analysis bandwidth for calibrated VSA measurements
Rohde&Schwarz (R&S)

## Slide 13: Fields in SIG-A
Energy efficiency
Bit | Fields | Number of Bits | Description
B49-B51 | SU MCS | 3 | For a SU PPDU: MCS index For a MU PPDU: reserved
B52 | Precoded | 1 | For a SU PPDU: Set to 1 if a Beam-forming steering matrix is applied to the waveform in an SU transmission as described in TBD, set to 0 otherwise. For a MU PPDU: Reserved and set to 1
B53 | TXOP_PS_NOT_ALLOWED | 1 | Set to 0 by AP if it allows non-AP STAs in TXOP power save mode to enter Doze state during a TXOP. Set to 1 otherwise.
B54-B69 | CRC | 16 | SIG-A check sequence. Definition of this field calculation is in TBD.
B70-B71 | Reserved | 2 | Reserved
Notes: Agilent technologies
  E8267D PSG Vector Signal Generator, up to 44GHz, 160 MHz (extendable to 2 GHz) RF modulation bandwidth
  E4448A PSA Spectrum Analyzer, 3 Hz - 50 GHz, Analysis Bandwidth
    10 MHz analysis bandwidth (option B7J for the Basic mode)
    Optional 40 or 80 MHz analysis bandwidth to capture and measure complex signals. View the demo
    -78 dB (nominal) third order intermodulation for 40 or 80 MHz analysis bandwidth
    Up to 300 MHz analysis bandwidth for calibrated VSA measurements
Rohde&Schwarz (R&S)

## Slide 14: Fields in SIG-A
Scrambler
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7 | SC/OFDM | 1 | Set to 0 if SC transmission is adopted for PPDU, set to 1 if OFDM transmission is adopted for PPDU;
B8 | BW | 1 | Set to 0 for 540MHz, set to 1 for 1080MHz;
B9 | Dynamic Bandwidth | 1 | If BW=1 and Duplicate=1: set Dynamic Bandwidth to 1 for allowing dynamic bandwidth; set to 0 for non allowing dynamic bandwidth. Otherwise set to 0; (Reserved)
B10-B11 | Sub-Band | 2 | Bitmap (B10-B11): If Dynamic Bandwidth=1, set to 10 for using the primary 540MHz channel, set to 01 for using the secondary 540MHz channel; set to 11 for using 1080MHz channel; Otherwise set to 00 (reserved).
Notes: Agilent technologies
  E8267D PSG Vector Signal Generator, up to 44GHz, 160 MHz (extendable to 2 GHz) RF modulation bandwidth
  E4448A PSA Spectrum Analyzer, 3 Hz - 50 GHz, Analysis Bandwidth
    10 MHz analysis bandwidth (option B7J for the Basic mode)
    Optional 40 or 80 MHz analysis bandwidth to capture and measure complex signals. View the demo
    -78 dB (nominal) third order intermodulation for 40 or 80 MHz analysis bandwidth
    Up to 300 MHz analysis bandwidth for calibrated VSA measurements
Rohde&Schwarz (R&S)

## Slide 15: Fields in SIG-A
Single carrier & Multi-carrier
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7 | SC/OFDM | 1 | Set to 0 if SC transmission is adopted for PPDU, set to 1 if OFDM transmission is adopted for PPDU;
B8 | BW | 1 | Set to 0 for 540MHz, set to 1 for 1080MHz;
B9 | Dynamic Bandwidth | 1 | If BW=1 and Duplicate=1: set Dynamic Bandwidth to 1 for allowing dynamic bandwidth; set to 0 for non allowing dynamic bandwidth. Otherwise set to 0; (Reserved)
B10-B11 | Sub-Band | 2 | Bitmap (B10-B11): If Dynamic Bandwidth=1, set to 10 for using the primary 540MHz channel, set to 01 for using the secondary 540MHz channel; set to 11 for using 1080MHz channel; Otherwise set to 00 (reserved).
Notes: Agilent technologies
  E8267D PSG Vector Signal Generator, up to 44GHz, 160 MHz (extendable to 2 GHz) RF modulation bandwidth
  E4448A PSA Spectrum Analyzer, 3 Hz - 50 GHz, Analysis Bandwidth
    10 MHz analysis bandwidth (option B7J for the Basic mode)
    Optional 40 or 80 MHz analysis bandwidth to capture and measure complex signals. View the demo
    -78 dB (nominal) third order intermodulation for 40 or 80 MHz analysis bandwidth
    Up to 300 MHz analysis bandwidth for calibrated VSA measurements
Rohde&Schwarz (R&S)

## Slide 16: SIG-B structure

## Slide 17: SIG-B structure
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7-B9 | MCS | 3 | MCS index;
B10-B27 | Length | 18 | Number of data octets in the PSDU, Rang 1-162143
B28-B31 | Reserved | 4 | Reserved.
B32-B47 | HCS | 16 | SIG-B check sequence. Definition of this field calculation is in TBD.

## Slide 18
Thanks for Your Attention.