## Slide 1: PHY SIG Frame Structure for IEEE 802.11aj (45GHz)
Authors/contributors:
Date: 2014-05-21
Presenter: Shiwen HE

## Slide 2
May 2014
Shiwen He, Haiming Wang
Slide 2
Abstract
The proposal presents a kind of physical layer SIG frame structure in millimeter-wave multi-user MIMO WLAN communication for IEEE 802.11 aj (45GHz).
Notes: 2

## Slide 3
May 2014
Shiwen He, Haiming Wang
Slide 3
Background
Challenges of future WPAN
Limited spectrum resources
Requirement for high data rate
Features of future WPAN
Large bandwidth
Multiple channel mode
Multi-user
Multi-stream
45GHz millimeter-wave communication
Digital home appliances
Ultra-high-speed (10Gbps) wireless applications
Notes: 3

## Slide 4
May 2014
Shiwen He, Haiming Wang
Slide 4
Technology Objects
The SIG frame structure try to achieve the following technical goals
  Dynamic bandwidth
  Multi-user & Multi-stream
  Energy efficiency
  Scrambler
  Single & Multi-carrier
Dynamic bandwidth
Achieving dynamically channel bandwidth selection for 1080MHz BSS to enhance the adaptability in different channel environments and improve spectral efficiency.
Notes: 4

## Slide 5
May 2014
Shiwen He, Haiming Wang
Slide 5
Technology Objects
Multi-user & Multi-stream
Achieve a multi-user multi-stream control to obtain the multiplexing gain.
Energy efficient communication
Achieve energy efficient communication, i.e., allow non-AP STAs in TXOP power save mode to enter Doze state during a TXOP.
Scrambler
Scrambling effectively reduces the PAPR in OFDM system .
Single carrier & Multi-carrier
Switch in single carrier and multi-carrier
Notes: 5

## Slide 6
May 2014
Shiwen He, Haiming Wang
Slide 6
SIG-A structure
Notes: 6

## Slide 7
May 2014
Shiwen He, Haiming Wang
Slide 7
SIG-A structure
Scrambler
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7 | SC/OFDM | 1 | Set to 0 if SC transmission is adopted for PPDU, set to 1 if OFDM transmission is adopted for PPDU;
B8 | BW | 1 | Set to 0 for 540MHz, set to 1 for 1080MHz;
B9 | Dynamic Bandwidth | 1 | If BW=1 and Duplicate=1: set Dynamic Bandwidth to 1 for allowing dynamic bandwidth; set to 0 for non allowing dynamic bandwidth. Otherwise set to 0; (Reserved)
B10-B11 | Sub-Band | 2 | Bitmap (B10-B11): If Dynamic Bandwidth=1, set to 10 for using the primary 540MHz channel, set to 01 for using the secondary 540MHz channel; set to 11 for using 1080MHz channel; Otherwise set to 00 (reserved).
Notes: 7

## Slide 8
May 2014
Shiwen He, Haiming Wang
Slide 8
SIG-A structure
Single carrier & Multi-carrier
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7 | SC/OFDM | 1 | Set to 0 if SC transmission is adopted for PPDU, set to 1 if OFDM transmission is adopted for PPDU;
B8 | BW | 1 | Set to 0 for 540MHz, set to 1 for 1080MHz;
B9 | Dynamic Bandwidth | 1 | If BW=1 and Duplicate=1: set Dynamic Bandwidth to 1 for allowing dynamic bandwidth; set to 0 for non allowing dynamic bandwidth. Otherwise set to 0; (Reserved)
B10-B11 | Sub-Band | 2 | Bitmap (B10-B11): If Dynamic Bandwidth=1, set to 10 for using the primary 540MHz channel, set to 01 for using the secondary 540MHz channel; set to 11 for using 1080MHz channel; Otherwise set to 00 (reserved).
Notes: 8

## Slide 9
May 2014
Shiwen He, Haiming Wang
Slide 9
SIG-A structure
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7 | SC/OFDM | 1 | Set to 0 if SC transmission is adopted for PPDU, set to 1 if OFDM transmission is adopted for PPDU;
B8 | BW | 1 | Set to 0 for 540MHz, set to 1 for 1080MHz;
B9 | Dynamic Bandwidth | 1 | If BW=1 and Duplicate=1: set Dynamic Bandwidth to 1 for allowing dynamic bandwidth; set to 0 for non allowing dynamic bandwidth. Otherwise set to 0; (Reserved)
B10-B11 | Sub-Band | 2 | Bitmap (B10-B11): If Dynamic Bandwidth=1, set to 10 for using the primary 540MHz channel, set to 01 for using the secondary 540MHz channel; set to 11 for using 1080MHz channel; Otherwise set to 00 (reserved).
Dynamic bandwidth
Notes: 9

## Slide 10
May 2014
Shiwen He, Haiming Wang
Slide 10
SIG-A structure
Multi-user & Multi-stream
Bit | Fields | Number of Bits | Description
B12-B29 | Length | 18 | SU：Number of data octets in the PSDU, Range 1-162143; MU：Maximum number of data octets in the PSDU of all users, Range 1-162143;
B30 | STBC | 1 | For an SU PPDU: set to 1 if space time block coding is used and set to 0 otherwise. For a MU PPDU: set to 0.
B31-B36 | GroupID | 6 | Set to the value of the TXVECTOR parameter GROUP_ID. A value of 0 or 63 indicates a SU PPDU; otherwise, indicates a MU PPDU.
B37 | Aggregation | 1 | Set to 1 indicate that the PPDU in the data portion of the packet contains an A-MPDU; otherwise, set to 0.
Notes: 10

## Slide 11
May 2014
Shiwen He, Haiming Wang
Slide 11
SIG-A structure
Multi-user & Multi-stream
Bit | Fields | Number of Bits | Description
B38-B48 | NSTS/Partial AID | 11 | For a MU PPDU: NSTS is divided into 4 user positions of 2 bits each. User position , where , uses bits B(38+ ) to B(39+ ). The number of space time streams for user are indicated at user position =USER position[ ], where …..,NUM-USERS-1, and the notation A[b] denotes the value of array A at index b. Zero space-time streams are indicated at positions not listed in the USER_POSITION array. Each user position is set as follows: Set to 0 for 0 space-time streams Set to 1 for 1 space-time stream Set to 2 for 2 space-time streams Set to 3 for 3 space-time streams Set to 4 for 4 space-time streams B46-B48：set to zero, reserved For a SU PPDU: B38-B39 Set to 0 for 1 space-time stream Set to 1 for 2 space-time streams Set to 2 for 3 space-time streams Set to 3 for 4 space-time streams B40-B48 Partial AID: Set to the value of the TXVECTOR parameter PARTIAL_AID. Partial AID provides an abbreviated indication of the intended recipient(s) of the PSDU.
Notes: 11

## Slide 12
May 2014
Shiwen He, Haiming Wang
Slide 12
SIG-A structure
Multi-user & Multi-stream
Bit | Fields | Number of Bits | Description
B49-B51 | SU MCS | 3 | For a SU PPDU: MCS index For a MU PPDU: reserved
B52 | Precoded | 1 | For a SU PPDU: Set to 1 if a Beam-forming steering matrix is applied to the waveform in an SU transmission as described in TBD, set to 0 otherwise. For a MU PPDU: Reserved and set to 1
B53 | TXOP_PS_NOT_ALLOWED | 1 | Set to 0 by AP if it allows non-AP STAs in TXOP power save mode to enter Doze state during a TXOP. Set to 1 otherwise.
B54-B69 | CRC | 16 | SIG-A check sequence. Definition of this field calculation is in TBD.
B70-B71 | Reserved | 2 | Reserved
Notes: 12

## Slide 13
May 2014
Shiwen He, Haiming Wang
Slide 13
SIG-A structure
Energy efficiency
Bit | Fields | Number of Bits | Description
B49-B51 | SU MCS | 3 | For a SU PPDU: MCS index For a MU PPDU: reserved
B52 | Precoded | 1 | For a SU PPDU: Set to 1 if a Beam-forming steering matrix is applied to the waveform in an SU transmission as described in TBD, set to 0 otherwise. For a MU PPDU: Reserved and set to 1
B53 | TXOP_PS_NOT_ALLOWED | 1 | Set to 0 by AP if it allows non-AP STAs in TXOP power save mode to enter Doze state during a TXOP. Set to 1 otherwise.
B54-B69 | CRC | 16 | SIG-A check sequence. Definition of this field calculation is in TBD.
B70-B71 | Reserved | 2 | Reserved
Notes: 13

## Slide 14
May 2014
Shiwen He, Haiming Wang
Slide 14
SIG-B structure
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7-B9 | MCS | 3 | MCS index;
B10-B27 | Length | 18 | Number of data octets in the PSDU, Rang 1-162143
B28-B31 | Reserved | 4 | Reserved.
B32-B47 | CRC | 16 | SIG-B check sequence. Definition of this field calculation is in TBD.
Notes: 14

## Slide 15
May 2014
Shiwen He, Haiming Wang
Slide 15
SIG-B structure
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7-B9 | MCS | 3 | MCS index;
B10-B27 | Length | 18 | Number of data octets in the PSDU, Rang 1-162143
B28-B31 | Reserved | 4 | Reserved.
B32-B47 | HCS | 16 | SIG-B check sequence. Definition of this field calculation is in TBD.
Notes: 15

## Slide 16
May 2014
Shiwen He, Haiming Wang
Slide 16
Thanks for Your Attention
Notes: 16