## Slide 1: Consideration on UL MU transmission
Date: 2014-07-14
Authors:

## Slide 2: Motivation
In [1], we checked PHY and MAC feasibility to support UL MU transmission.
In this contribution, we further discuss the procedure of UL MU transmission and the related issues in 11ax.

## Slide 3: Procedure of UL MU transmission
AP’s scheduling
  For STAs to transmit UL data frame simultaneously, AP has to set TXOP and let each STA know its own resource such as frequency band in FDM and stream index in SDM.
Therefore, we suggest the procedure of UL MU transmission as below.

## Slide 4: UL MU transmission
UL Scheduling frame
  AP sets TXOP for UL MU transmission and indicates the transmission method to STAs such as frequency/spatial resource to use.
  Issue 1. How to send UL MU scheduling frame
  Issue 2. How to choose UL MU STAs
UL data frames
  STAs transmit their UL data frames respectively as AP indicates.
  Issue 3. How to make UL data frames synchronously received by AP.
ACK frame
  AP transmits ACK frame(s) to STAs separately or together.

## Slide 5: Issue 1. How to send UL MU scheduling frame
Option1. With PIFS access
  It is used to send CF-Poll frame for assignment of polled TXOP
  It provides the highest priority to access channel and doesn’t have to manage CW
Option2. Using a specific AC (e.g., AC_VO) parameters
  It is used to send a management frame using AC_VO
  It provides fixed priority to access channel and has to manage CW
Option3. Using AC parameters of STAs assigned UL MU TXOP
  It is used to send RTS or CTS frame using the access category of the corresponding QoS Data
  It provides variable priority to access channel and has to manage CW

## Slide 6: Issue 2. How to choose UL MU STAs
In order to select UL MU STAs and to set UL MU TXOP,
  STA’s buffer status helps the AP assigning UL MU resource efficiently.
To report the STA’s buffer status
  Current standard can be leveraged, i.e.,
    Piggybacked in UL data (e.g., Queue size in QoS Control field)
    Standalone UL frame (e.g., QoS Null frame including Queue size)
  Additionally
    Piggybacked in DL dependent UL control frames (e.g., Modified CTS, BA, ACK, etc.)

## Slide 7: Issue 3. How to make UL data frames synchronously received by AP (1/2)
Timing synchronization
  Need 2 or 4 times longer CP for UL MU transmission in outdoor environment
Frequency synchronization
  By [2], over±4kHz difference between 2 STAs causes performance degradation in UL MU MIMO.
Power synchronization [1]
  More critical in SDM/CDM than in FDM where UL data is separated in frequency domain before quantization.
 | Indoor (scenario 3) | Outdoor (scenario 4)
Radius [3] | 20 meters | 150 meters
95% channel delay[1] | 58 nsec | 700/1200 nsec in UMi/UMa
Max. round trip delay | 67 nsec | 500 nsec
Time difference | 125 nsec | 1200 nsec ~ 1700 nsec

## Slide 8: Issue 3. How to make UL data frames synchronously received by AP (2/2)
Potential solution(s) for synchronization in UL MU
  Longer CP size
    Need 2 or 4 times longer CP for UL MU in outdoor environment
    Need further system-level verification
  Adjustment procedure for synchronization
    AP indicates each STA to adjust time/frequency/power difference.
    AP calculates the difference among MU STAs by frame exchange with STAs.
  UL MU only for STAs who are sufficiently synchronized
    Implementation-specific, but usage is limited

## Slide 9: Conclusion
We discussed the procedure of UL MU transmission and related issues to support UL MU transmission in 11ax.
  AP initiates UL MU transmission by transmitting UL scheduling frame.
  AP needs information to schedule STAs in advance.
  11ax system needs to align the differences of time, frequency and power among STAs.
Next issues are
  TXOP protection based on RTS-CTS, L-SIG protection, etc.
  Processing time of UL data frame
    Need to check if the time is enough for STA to prepare data packet within SIFS after receiving UL MU scheduling frame which includes MU scheduling information (e.g., STAs’ ID, assigned MU channel, TXOP, etc.).
  Channel access and retransmission rule
  And verification of system-level gain of UL MU transmission

## Slide 10: Reference
[1] 11-13-1388, “Uplink multi-user transmission”
[2] 11-09-1036, “Uplink MU-MIMO Sensitivity to Power Differences and Synchronization Errors”
[3] 11-14-0621-03, “Simulation scenarios”