## Slide 1: Envisioning 11ax PHY Structure - Part I
Date: 2014-07-14
Authors:

## Slide 2: Introduction
11ax PAR [1] defines
  In Scope of the project
    Support “improvement in the average throughput per station”
    Support “coexistence with legacy IEEE 802.11 devices”
  In Additional Explanatory Notes
    Increase “robustness in outdoor propagation environments”
Design on 11ax PHY structure should reflect above requirements
  In terms of OFDM numerology
    Increase of available tones for Tput, longer CP for outdoor
  In terms of frame structure
    Legacy coexistence, minimized preamble overhead
In this contribution, we discuss how to design 11ax PHY structure focusing on OFDM numerology

## Slide 3: Proposed 11ax PHY structure (1/5) : Goal & approach
Goals for 11ax OFDM numerology design
  Average throughput enhancement by CP ratio reduction
  Outdoor robustness by longer CP length
Based on the goals in the above, out proposal on 11ax OFDM numerology is to “Increase FFT size (longer symbol) in 11ax”
Key questions (KQ)
  KQ 1. How many times FFT size will be increased?
  KQ 2: Which CP length(s) is the best by considering both of the goals?

## Slide 4: Proposed 11ax PHY structure (2/5) : FFT size
KQ-1: How many times FFT size will be increased? |  |  | 
FFT size | Frequency & Time structure | Benefit* (from CP ratio reduction) | Pros & cons
2-times FFT (156.25kHz SC) | F: 2-times more tone T: 2-times longer symbol | Get 11% throughput gain Conventional: 3.2μs + 0.8μs 2-times FFT: (6.4μs + 0.8μs) / 2 | Pros: lowest impact on CFO immunity Cons: smallest throughput gain
4-times FFT (78.125kHz SC) | F: 4-times more tone T: 4-times longer symbol | Get 17% throughput gain Conventional: 3.2μs + 0.8μs 4-times FFT: (12.8μs + 0.8μs) / 4 | Pros: higher tone gain (6% than 2-times) Cons: possibility of increased CFO impact with less subcarrier spacing => No critical issue (check: next slide)
8-times FFT (39.063kHz SC) | F: 8-times more tone T: 8-times longer symbol | Get 21% throughput gain Conventional: 3.2μs + 0.8μs 8-times FFT: (25.6μs + 0.8μs) / 8 | Pros: highest tone gain (4% than 4-times) Cons: Too much longer symbol (PPDU overhead) Highest impact on CFO immunity => performance degradation (check: next slide)
*: Assuming normal GI
4-times FFT extension as a good candidate for 11ax PHY structure

## Slide 5: Proposed 11ax PHY structure (3/5) : Feasibility check on KQ-1
4-times FFT: no critical impact on CFO aspect and even further gain in outdoor
  Additional gain from increased FFT because of longer symbol, especially in outdoor channel where channel delay can exceed CP length (refer Appendix)
8-times FFT: there is about 2dB performance loss than 4-times case
CP: 0.8μs. Performance ref.: [2]

## Slide 6: Proposed 11ax PHY structure (4/5) : CP size
KQ-2: Which CP length(s) is the best by considering both of the goals? |  |  |  | 
CP size | CP portion (assuming 4-times FFT) | Pros & cons | Aligned to goals | 
 |  |  | Tput | Outdoor
0.4μs | 1/32 | Pros: maximized throughput from CP (21% than 3.2μs case) Cons: vulnerable in outdoor environment |  | X
0.8μs | 1/16 | Pros: throughput enhancement from CP (17% than 3.2μs case) Cons: performance degraded in outdoor environment |  | 
1.6μs | 1/8 | Pros: better for outdoor channels Cons: less throughput enhancement from CP |  | 
3.2μs | 1/4 | Pros: best fit for outdoor channels Cons: No throughput enhancement from CP | X | 
One CP can not meet both goals of average throughput enhancement and outdoor robustness sufficiently
Two CPs as a good candidate for 11ax PHY structure
  {1/32 or 1/16}CP for average throughput enhancement and {1/8 or 1/4}CP for outdoor robustness (we already have multiple CPs in 11ac)
Performance ref. on outdoor: [2]

## Slide 7: Proposed 11ax PHY structure (5/5) : Frequency-time structure
PHY structure in frequency: 4-times larger FFT than 11ac
  Subcarrier spacing (SC) is 78.125kHz : 4-times more tones in frequency
  Number (/position) of pilots and guard subcarriers is TBD (figure is 11ac ref. for 80MHz)
: data subcarrier
: pilot subcarrier
-122
Subcarrier index
11ax 20MHz : 256FFT
PHY structure in time: 4-times longer IDFT/DFT period than 11ac
  IDFT/DFT length is 12.8μs: 4-times longer length in time
  Two CPs: Cyclic prefix (CP) is {1.6μs or 3.2μs}, short CP is {0.4μs or 0.8μs}
12.8μs
{1.6 or 3.2μs}
CP
IDFT/DFT length
12.8μs
Short CP
IDFT/DFT length
For outdoor robustness
For Tput enhancement
122
{0.4 or 0.8μs}

## Slide 8: Next steps for the 11ax PHY structure
Numerology details with larger FFT
  Frequency guard tones
    Whether to maintain portion of guard tones or utilize some of part as data tones?
  Pilots
    How to assign pilots and how may pilot portion required?
Frame structure design (considering PAR)
  11ax PPDU should be designed to coexist with 802.11 legacy devices
    E.g. include L-part in front of HE PPDU
  It is desirable to minimize preamble overhead as possible
    E.g. reuse L-part for timing/CFO compensation, exploit HE-preamble for advanced features (FFS)

## Slide 9: Conclusion
Beyond previous Wi-Fi systems, the purpose of 11ax system is to support a lot of use cases and different channel environments, so we should take into account
  Various options to be properly used in each environment
  Feasible solution to achieve the goals against challengeable environments (high-dense condition, outdoor propagation)
Based on the requirements, we analyzed OFDM numerology and proposed 11ax PHY structure
  4-times FFT extension
  Two CPs: {1/32 or 1/16} CP and {1/8 or 1/4} short CP
Further works will be accompanied later to look at the other aspect (frame structure) for 11ax PHY structure design

## Slide 10: Appendix: Benefit from longer symbol [3]
Conventional:
  Ps (signal power)
  = ((3.2 – 0.9 + 0.8) / 3.2)2 = 0.938
  Pi (interference power)
  = 1 - 0.938 = 0.062
TFFT is FFT period
CP is CP period
|αm|2 is power of m-th tap
τm is delay of m-th tap including OFDM symbol timing
E.g. τ = CP + 2 (0.8μs + 0.1μs = 0.9μs)
4-times FFT:
  Ps (signal power)
  = ((12.8 – 0.9 + 0.8) / 12.8)2 = 0.984
  Pi (interference power)
  = 1 - 0.984 = 0.016
Modeling on delay profile and CP length

## Slide 11: Reference
[1] 11-14-0165-01-0hew-802-11-hew-sg-proposed-par
[2] 11-14-0801-00-0ax-envisioning-11ax-phy-structure-part-ii
[3] 11-13-0536-00-0hew-hew-sg-phy-considerations-for-outdoor-environment