## Slide 1: RBIR-based PHY Abstraction with Channel Estimation Error
Date: 2014-07-xx
Authors:
Name | Affiliations | Address | Phone | email
Yakun Sun | Marvell Semiconductor | 5488 Marvell Ln, Santa Clara, CA 95054 | 1-408-222-3847 | yakunsun@marvell.com

## Slide 2: Introduction
    RBIR-based PHY abstraction has been evidently accurate in predicting PER for ideal channel estimation.
    How to model the channel estimation in PHY abstraction?
    We are proposing a simple method of incorporating channel estimation error in PHY abstraction.

## Slide 3: Scope of Study on Channel Estimation in SLS
An arbitrary channel estimation algorithm can be assumed by each company.
  For example, LS vs. MMSE vs. any other advanced CE.
One unified channel estimation algorithm is preferable.
  Using various algorithms leads to very different performance.
  Time consuming to verify/review the modeling for each algorithm.
LS CE provides baseline performance and is easy to analyze.
Proposal 1: LS-CE for SLS.

## Slide 4: LS Channel Estimation Error
Assume HT/VHT-LTF. The LS channel estimate is
  P- is the pseudo inverse of the spreading matrix.
The received signal is modeled with an effective noise.
  For Nss=NLTF, noise is 3dB higher;
  For Nss=3 and NLTF=4, the noise is 2.43dB higher.

## Slide 5: RBIR PHY Abstraction with CE
Step 1: For each tone/OFDM symbol, compute SINR with additional AWGN with variance Nss/NLTFσ2.
Step 2: Compute the effective SINR based RBIR mapping [1].
Step 3: Use PER table obtained from ideal channel estimation to predict PER.

## Slide 6: Performance of PER vs. Effective SNR
20MHz, 2.4GHz, 8000 bits per packet.
MIMO:
  No TxBF
  1x1, NLTF=1, Nss=1
  3x3, NLTF=4, Nss=3
Effective SNR mapping: RBIR-BICM
PER vs. effective SNR
  Ideal channel estimation for AWGN
  LS channel estimation for DNLOS/BLOS

## Slide 7: Performance of PER vs. Effective SNR (2)
PER vs. effective SNR curves with actual CE are within 1dB offset to that of AWGN with ideal CE.

## Slide 8: Performance of PER Prediction
100 independent (and fixed) DNLOS channel realizations.
  Each channel realization with 4000 noise realizations.
LS channel estimation is used.
PER is obtained for each SNR point in two ways [1]:
  Simulated: count by decoding errors
  Predicted: predict PER by PHY abstraction using PER table obtained from ideal CE.
Look at SNR offset @ PER = 10% for each channel realization.
PER is reliably predicted for each channel realization by using the proposed CE error modeling in PHY abstraction

## Slide 9: Simulation Results
1x1, Nss=1, NLTF=1
 | MCS | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
LDPC | Mean (dB) | 0.91 | 0.57 | 0.45 | 0.08 | 0.01 | -0.05 | -0.01 | 0.06 | 0.04 | 0.11
 | Var (dB) | 0.29 | 0.21 | 0.21 | 0.13 | 0.11 | 0.09 | 0.08 | 0.18 | 0.13 | 0.14
BCC | Mean (dB) | -0.34 | -0.43 | -0.57 | -0.34 | -0.41 | -0.19 | -0.15 | -0.40 | -0.05 | -0.15
 | Var (dB) | 0.38 | 0.40 | 0.58 | 0.37 | 0.53 | 0.47 | 0.51 | 0.76 | 0.47 | 0.56
 | MCS | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
LDPC | Mean (dB) | 0.66 | 0.29 | 0.06 | -0.03 | -0.29 | 0.29 | -0.14 | -0.31 | -0.02 | 0.44
 | Var (dB) | 0.27 | 0.19 | 0.20 | 0.13 | 0.21 | 0.25 | 0.25 | 0.19 | 0.37 | 0.27
BCC | Mean (dB) | -0.34 | -0.43 | -0.57 | -0.34 | -0.41 | -0.19 | -0.15 | -0.40 | -0.05 | -0.15
 | Var (dB) | 0.38 | 0.40 | 0.58 | 0.37 | 0.53 | 0.47 | 0.51 | 0.76 | 0.47 | 0.56
3x3, Nss=3, NLTF=4

## Slide 10: Conclusions
Proposal 1: assume LS channel estimation for SLS PHY abstraction
Proposal 2: LS channel estimation error in PHY abstraction is modeled as addition AWGN with variance of Nss/NLTF σ2.

## Slide 11: References
11-14-0581-00-00ax-further-discussion-on-phy-abstraction