## Slide 1: Coexistence Requirements of 802.11 WLAN and LTE in Unlicensed Spectrum
Date: 2014-07
Authors:

## Slide 2: Abstract
This presentation
  Provides results on the impact of LTE in unlicensed spectrum on the performance of 802.11 WLAN networks
  Proposes a requirement for TGax Functional Requirements document.

## Slide 3: Background
3GPP is considering extending the use of LTE into the unlicensed spectrum as a seamless approach to enable traffic offload. This new approach is dubbed LTE Unlicensed (LTE-U).
LTE-U, being a centralized scheduling system, will change the ecosystem in unlicensed spectrum.
LTE-U introduces new coexistence challenges for other technologies operating in the same unlicensed bands, particularly for legacy Wi-Fi.

## Slide 4: LTE Quiet Period
LTE is an “almost” continuously transmitting protocol.
A Wi-Fi device needs to wait for a “quiet” period, when LTE is not transmitting, before attempting to transmit.
Even when LTE is not transmitting data, it periodically transmits a variety of Control and Reference Signals.
  LTE “quiet” period depends on the periodicity of these signals.
For FDD LTE mode, the maximum quiet period is only 215 μsec (depicted here).
In the absence of data, or when subframes are intentionally muted, maximum LTE quiet period is 3 msec in TD-LTE mode.
DL Control and Reference Signals
(LTE FDD)
quiet period
It will be difficult for Wi-Fi to grab the channel from LTE, and it will be at the discretion of the eNodeB scheduler

## Slide 5: Lab Test Conditions
2.4 GHz Band
ISM Ch. 1 (2.412 GHz)
Conducted testing
LTE
20 MHz LTE FDD downlink frequency converted into the 2.4 GHz Band
LTE UE to setup the connection - no data passed
LTE had equal power at AP and client
Wi-Fi
1 AP and 1 Client
Wi-Fi Signal power -60 dBm (good average signal level)
DL/UL Loss was symmetrical
1 spatial stream, long guard interval (max MCS 4) or 39 Mbps
100 Mbps UDP traffic offered load
Reported throughput figures are average over 1 minute.

## Slide 6: 802.11n Wi-Fi vs. Rel. 8 Downlink LTE Co-Channel 20 MHz
Wi-Fi throughput diminishes as LTE transmission moves closer to Wi-Fi devices
eNodeB
Wi-Fi AP
Wi-Fi Client
Locations Fixed
Scenario Modeled in Lab Setup
Distance
LTE Interference Power vs. Wi-Fi Throughput*
*Shape of curve dependent on device tested, trend is key take away
With LTE power at Wi-Fi client energy detect threshold, throughput approaches zero
Chart: Interference Power (dBm)
| -50.0 | -55.0 | -60.0 | -65.0 | -70.0 | -75.0 | -80.0 | -90.0 | -100.0 | -110.0 | -120.0 | -130.0
Wi-Fi to Wi-Fi | 14.9 | 15.9 | 15.8 | 16.4 | 15.1 | 16.6 | 17.8 | 17.3 | 25 | 25
LTE to Wi-Fi | 0 | 0.2 | 2.4 | 4.5 | 6.9 | 14.9 | 14.9 | 21.1 | 25 | 25

## Slide 7: Coexistence with Duty Cycle LTE
One popular concept for spectrum sharing is Duty Cycling
  Allow LTE to occupy the channel for fixed (or semi dynamic) percentage of time for each period
Selection of the period (in milliseconds) is critical to the performance on Wi-Fi network
LTE On
LTE On
LTE Off
Duty Cycle Period
Duty Cycle:
% of cycle LTE is active
time
Wi-Fi access gaps
when LTE is off

## Slide 8: Duty Cycle Approach- Wi-Fi Throughput
Wi-Fi throughput is consistent across LTE higher cycle periods
Wi-Fi gets <1Mbps for 10ms / 70% case
  Same as TD-LTE w/ 3 ms quiet period configuration

## Slide 9: Duty Cycle Approach- Wi-Fi Delay
Light load Wi-Fi 95th percentile delay shows the real impact of duty cycle period
  Delay increases 20x, 40x, 60x or more
Mean delay follows same trend

## Slide 10: Coexistence Requirements
We propose following requirements to be added to the 802.11ax FR document:
  The TGax amendment shall define a mechanism or mechanisms to ensure “minimum performance levels” for TGax devices when coexisting with non-listen-before-talk compliant devices in the same unlicensed band.
    The minimum performance levels is TBD after group discussion.

## Slide 11: Straw Poll
Do you support adding following requirment to the TGax Functional Requirements document?
  The TGax amendment shall define a mechanism or mechanisms to ensure minimum performance levels (TBD) for TGax devices when coexisting with non-listen-before-talk compliant devices in the same unlicensed band.
  Yes
  No
  Abstain

## Slide 12: References
A. Babaei, J. Andreoli-Fang and B. Hamzeh, “On the Impact of LTE-U on Wi-Fi Performance,” To appear in Proceedings of IEEE PIMRC 2014.