## Slide 1: Energy Efficiency Evaluation Methodology
Date: 2014-07-14
Authors:

## Slide 2
Authors:

## Slide 3: Outline
Proposed energy efficiency metrics
Power model
Power states and power state transitions
802.11 power save mechanisms
Proposal for modifications to 802.11ax simulation scenarios
Calibrating power models
Setting the bar for energy efficiency
Evaluating energy efficiency
Conclusion

## Slide 4: Proposed Energy Efficiency Metrics
Metric | Units | Definition
Per-STA energy per TX bit | Joules/bit | Total energy consumed by a STA divided by the total number of successful data bits transmitted by the STA
Per-STA energy per RX bit | Joules/bit | Total energy consumed by a STA divided by the total number of successful data bits received by the STA

## Slide 5: Power Model
For evaluating of power efficiency, a power model is defined in this contribution with these 3 components:
  Power states
  Power state transitions
  Power save mechanism

## Slide 6: Power States and Power Consumption Levels
A STA operates in one of 5 power states when exchanging frames with other STAs, or sleeping to conserve power and prolong battery life
  The states are Transmit, Receive, Listen, Shallow Sleep and Deep Sleep
  Deep Sleep, compared to Shallow Sleep, is the state with the lowest consumption power; a STA takes a much longer time to transition into and out of Deep Sleep to Awake
Power consumed in each power state depends on the number of spatial streams, channel bandwidth, transmit power, and frequency bands in Awake states (i.e. Transmit, Receive, Listen)
  Note MCS and coding schemes affects power consumption for Transmit and Receive states; however, we make the assumption that the effects from these two factors are negligible
Clock inaccuracy means STA has to wake up early to catch the Beacon; however, this effect is assumed to be negligible
  E.g. STA with 100ppm, and waking up every 3 Beacon Intervals of 100 TUs would experience a clock drift of ±30us
A power table, enumerating power states and power consumption levels, is design and implementation dependent
  Nevertheless, a reference power table is needed for calibrating power models across System simulators and evaluating power save proposal(s)

## Slide 7: Example of Power States and Power Consumption Levels
Power State | Average Power Consumption (mW) Bandwidth = 40 MHz, Band = 5 GHz TX power per antenna[4] = 18 dBm (STA), 15 dBm (P2P) |  | 
NSS | 1 | 2 | 3
Transmit | 1280 | 1990 | 2100
Receive | 940 | 1270 | 1600
Listen | 820 | 1130 | 1450
Shallow Sleep | 100 | 100 | 100
Deep Sleep | - | - | -
Source: D. Halperin et al, “Demystifying 802.11n Power Consumption,” Proceedings of the 2010 International Conference on Power Aware Computing and System, 2010

## Slide 8: Power State Transitions and Consumption Levels
When a STA switches from one power state to another, there is a non-zero cost for this transition
  Cost is added latency, or extra power consumed
The reference power state transition table is used for power model calibration across System simulators
We make the assumption that these power state transitions are independent of MCS, channel bandwidth, frequency bands, etc.
Refer to Slide 19 in Appendix for table for power state transition
Transmit
Receive
Listen
Shallow Sleep
Deep Sleep

## Slide 9: 802.11 Power Save Mechanisms
Propose to adopt 3 existing power save mechanisms in 802.11-2012 as baseline for power efficiency evaluation
  Power save mode (PSM)
  Power save polling (PSP)
  Unscheduled automatic power save delivery (U-APSD)

## Slide 10: Example of Power States and Power State Transitions during Power Save Polling Operation
AP buffers this frame since this STA is in Power Save
AP
STA
ACK
PS-Poll
Beacon
DATA
Beacon
STA starts CCA for PS-Poll
STA Power State and State Transition
TX→SS
DATA
RX
RX
RX
TX
TX
LI
LI
LI
SS
AP starts CCA for downlink DATA
Shallow Sleep (SS)
DS
Transmit (TX)
Receive (RX)
Deep Sleep (DS)
Assume DTIM=3
TX→LI→RX
RX→TX
ACK
LI
SS→LI
SS/DS
Listen (LI)
Power State Transition
Assuming there no other traffic in medium

## Slide 11: Proposal for Modifications to 802.11ax Simulation Scenarios
Scenario | Topology | Traffic Model | Proposed Power Model
Residential (1) | Type A - Multi-floor building, 5 floors (each floor is 3m high), 2x10 apartments per floor, apartment size 10m x 10m x 3m, M APs per floor, N STAs per apartment | Buffered video streaming | PSM
Enterprise (2) | Type B - Office floor, 8 offices, 64 cubicles per office, 4 STAs per cubicle (laptop, monitor, smartphone/tablet, harddisk) | Local file transfer, lightly internet streaming video/audio, VoIP | PSP, U-APSD
Indoor Small BSS Hotspot (3) | Type C - BSSs in regular and symmetric grid with frequency reuse 3 or 7, AP in center and STAs randomly placed in hexagon, N (40) STAs per BSS | Highly compressed video (streaming), web browsing, local file transfer, multicast video streaming | PSM, PSP
Outdoor Large BSS Hotspot (4a) | Type D - 19 hexagonal grid with inter cell distance at 130m, N (50) STAs per BSS | Highly compressed video (streaming), web browsing, local file transfer | PSM, PSP
Outdoor Large BSS Hotspot + Residential (4b) | Type D + Type A - 7 hexagonal cells with inter cell distance (ICD) at 130m, one residential building per BSS with center placed in a random uniform position within a radius of ICD/2 around AP | Type D + Type A | PSM, PSP
Source: IEEE 802.11-14-0621r3

## Slide 12: Calibrating Power Models
Adopt power tables in slides 18-19 in System simulators
Implement the baseline power save mechanisms, i.e. PSM, PSP, U-APSD
Verify implementation of baseline power save mechanisms across System simulators
  For each simulation scenario, along with the power save mechanism, check that the throughput metric is comparable across System simulators
Verify implementation of power efficiency metrics across System simulators
  For each simulation scenario, along with the traffic and power models, check that both throughput and power efficiency metrics are comparable across System simulators

## Slide 13: Setting the Bar for Energy Efficiency
Propose Energy Efficiency Rating
  Defined as the ratio of energy consumed for one bit of data successfully exchanged between STAs using any new proposed power save mechanism over the baseline power save mechanism, i.e.
Any new proposed mechanisms should meet the following 3 requirements
  4 times average Per-STA throughput improvement [1]
  Transmission latency constraints requirements (TBD; see [3])
  Maintain or reduce energy per successful information bit, i.e. energy efficiency rating of at least one or less
Specifically, any proposed power save mechanism should have an energy efficiency rating less than one

## Slide 14: Evaluating Energy Efficiency
Required metrics to evaluate power save mechanisms
  As already defined in the simulation scenario document [3] [4]
    Per-STA and/or Per-BSS throughput
    Packet loss
    Transmission latency
  In addition to the above, the following needs to be added
    Per-STA energy per TX bit
    Per-STA energy per RX bit
Power save mechanisms proposed in 802.11ax should be benchmarked using the above mentioned metrics against:
  Other power save mechanisms proposed in 802.11ax
  Baseline power save mechanisms in the simulation scenarios (refer to slide 11)

## Slide 15: Conclusion
This contribution proposes a systems approach (covering both PHY and MAC) to evaluate energy efficiency for 802.11ax; this is similar to how throughput performance is evaluated for previous 802.11 amendments
Change the simulation scenario document [4] as follows:
  Add definitions for energy efficiency metrics in Slide 4
  Add power tables in Slides 18-19
  Adopt 3 baseline power save mechanisms, i.e.
    Power save mode (PSM)
    Power save polling (PSP)
    Unscheduled automatic power save delivery (U-APSD)
  Add power save mechanism to each simulation scenario (and associated traffic models)
Incorporate proposed power model to the evaluation methodology document [3]
  Add definition for Energy Efficiency Rating

## Slide 16: References
http://www.ieee802.org/11/PARs/P802.11ax.pdf
IEEE 802.11-2012
R. Porat et al, “11ax Evaluation Methodology,” IEEE11-14-571r2
S. Merlin et al, “TGax Simulation Scenarios,” IEEE 11-14-621r4
G. Park et al, “Discussion on power save mode for real time traffic,” IEEE 11-14-352r0
D. Halperin et al, “Demystifying 802.11n Power Consumption,” Proceedings of the 2010 International Conference on Power Aware Computing and System, 2010

## Slide 17: Appendix

## Slide 18: Power States and Power Consumption Levels
Power State | Average Power Consumption (mW) Bandwidth = { 20 MHz, 40 MHz, 80 MHz, 160 MHz }, Band = { 2.4 GHz, 5 GHz } TX power per antenna [4] = 18 dBm (STA), 15 dBm (P2P) |  |  |  |  |  |  | 
NSS | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Transmit |  |  |  |  |  |  |  | 
Receive |  |  |  |  |  |  |  | 
Listen |  |  |  |  |  |  |  | 
Shallow Sleep |  |  |  |  |  |  |  | 
Deep Sleep |  |  |  |  |  |  |  | 

## Slide 19: Power State Transitions and Consumption Levels
State Transitions | Transition Time (ms) | Average Power Consumption (mW)
Transmit ⬄ Listen | (0 , 0) | (0 , 0)
Receive ⬄ Listen | (0 , 0) | (0 , 0)
Receive➭ Transmit | TRT (e.g. SIFS of 16us) | PRT
Transmit ➭ Shallow Sleep | TTS | PTS
Receive ➭ Shallow Sleep | TRS | PRS
Listen ⬄ Shallow Sleep | (TLS , TSL) | (PLS , PSL)
Deep Sleep ⬄ Shallow Sleep | (TDS , TSD) | (PDS , PSD)