## Slide 1: Residential Scenario Sensitivity and Transmit Power Control Simulation Results
Date: 2014-07-14
Authors:

## Slide 2: Abstract
In this submission, we report MAC simulation results with varying transmit power level and sensitivity level for IEEE 802.11 networks in a scenario of dense residential apartments.
Data throughput and packet delay are compared for different settings of transmit power, sensitivity and frequency reuse.

## Slide 3: Simulation Scenario and Assumptions
The scenario of residential apartment buildings [1]
  Five floors, two rows per floor, ten rooms per row
  Minor modifications
    APs are centered in the apartment
    Floor/wall penetration loss [4, 5], [2, Table3]
  Uplink, 802.11n MAC
    Full buffer traffic, 100% FTP over TCP; packet size 1500 bytes
    Eighty (80) seconds runtime after a warm-up period
    Link adaptation scheme: Adaptive Auto Rate Fallback (AARF)
  20 MHz band @ 5 GHz, 2x2 MIMO, TGnB path loss, no fading/shadowing
  Further simulation details shown in the appendix

## Slide 4: Three Simulation Cases
What does the simulation do?
  Maintain a fixed level of sensitivity (CCA) and transmit power for all uplink transmitters
  Sweep different level of sensitivity and transmit power and record system performance (throughput and packet delay)
We provide updated simulation results for the following
  Case 1: Frequency reuse 1 with only one entire floor of rooms active
    20 rooms active in one channel
  Case 2: Frequency reuse 1 with all five floor rooms active
    100 rooms active in one channel
  Case 3: Frequency reuse 3 with 1/3 of all five floor rooms active
    33 rooms (randomly selected on different floors) active in one channel
    More details in the appendix

## Slide 5: Performance Metrics
Normalized (per-BSS) Average Throughput
  Number of bits successfully received across the entire network divided by the entire runtime and by the number of rooms with active nodes (Mbps per active room)
  Interchangeable with area throughput (Mbps /m2)
  Averaged over 10 drops
Average Packet Delay
  Average end to end delay of all data packets at the MAC layer
  Averaged over the entire runtime over 10 drops
More details in the appendix

## Slide 6: Performance Comparisons: One Floor, Reuse 1
Throughput increases with CCA first, then decreases with CCA
Delay decreases with CCA first, then increases with CCA
Usually, throughput changes hand-in-hand with delay, after inversion
Optimal CCA level is not fixed (depending on transmit power)
CCA
Tx Pwr
Normalized (per BSS) Average Throughput (Mbps) |  |  |  |  | 
 | -90 dBm | -80 dBm | -70 dBm | -60 dBm | -50 dBm
11 dBm | 18.3 | 36.2 | 25.0 | 28.1 | 28.1
14 dBm | 17.5 | 33.3 | 30.9 | 28.6 | 28.2
17 dBm | 17.8 | 23.2 | 36.2 | 27.8 | 27.9
Average Packet Delay (msec) |  |  |  |  | 
 | -90 dBm | -80 dBm | -70 dBm | -60 dBm | -50 dBm
11 dBm | 9.5 | 6.9 | 13.3 | 12.1 | 12.3
14 dBm | 10.3 | 7.4 | 9.0 | 10.5 | 12.2
17 dBm | 10.8 | 8.7 | 7.2 | 10.5 | 11.6

## Slide 7: Performance Comparisons: Five Floors, Reuse 1
CCA
Tx Pwr
Similar trend as one floor case
Optimal CCA level is not fixed (depending on transmit power)
Normalized throughput generally reduces compared to the one floor case
More severely interference limited
Normalized (per BSS) Average Throughput (Mbps) |  |  |  |  | 
 | -90 dBm | -80 dBm | -70 dBm | -60 dBm | -50 dBm
11 dBm | 9.1 | 19.2 | 22.3 | 21.0 | 19.2
14 dBm | 7.9 | 17.1 | 22.2 | 22.7 | 19.7
17 dBm | 6.6 | 12.4 | 22.6 | 22.7 | 20.4
Average Delay (msec) |  |  |  |  | 
 | -90 dBm | -80 dBm | -70 dBm | -60 dBm | -50 dBm
11 dBm | 15.7 | 10.2 | 8.5 | 11.1 | 14.8
14 dBm | 16.0 | 11.0 | 9.5 | 8.5 | 15.4
17 dBm | 17.5 | 12.0 | 10.2 | 8.2 | 12.8

## Slide 8: Performance Comparisons: Five Floor, Reuse 3
CCA
Tx Pwr
Normalized (per BSS) Average Throughput (Mbps) |  |  |  |  | 
 | -90 dBm | -80 dBm | -70 dBm | -60 dBm | -50 dBm
11 dBm | 23.6 | 39.7 | 40.8 | 40.5 | 38.5
14 dBm | 21.2 | 36.0 | 41.4 | 42.7 | 39.5
17 dBm | 18.4 | 29.7 | 42.4 | 42.0 | 40.9
Average Delay (msec) |  |  |  |  | 
 | -90 dBm | -80 dBm | -70 dBm | -60 dBm | -50 dBm
11 dBm | 8.1 | 6.1 | 7.4 | 8.6 | 10.4
14 dBm | 8.4 | 6.3 | 7.2 | 7.1 | 11.1
17 dBm | 9.5 | 6.7 | 6.5 | 7.0 | 9.7
Similar trend as one floor case
Optimal CCA level is not fixed (depending on transmit power)
There is almost a plateau near the optimal CCA level (left figure)
Normalized throughput generally improves compared to the previous two cases
Reduced interference thanks to frequency reuse (unmanaged)

## Slide 9: Transmit Power Control
  Transmit power control:
  With conservative CCA strategy (e.g. -90/-80 dBm), reducing transmit power may be able to improve the area throughput
    When not many people try to talk at the same time, it may be better that everybody speaks more quietly
  With medium CCA strategy (e.g. -70 dBm), increasing transmit power may be able to improve the area throughput
    When many people try to talk at the same time, it may be better that everybody speaks louder
  With aggressive CCA strategy (e.g. -60/-50 dBm), increasing transmit power may not have a great impact on area throughput
    When too many people try to talk at the same time, it may not help at all that everybody speaks louder

## Slide 10: Frequency Reuse and Sensitivity Control
Unmanaged frequency reuse 3
  As expected, frequency reuse improves the area throughput
  Depending on the settings of sensitivity control and transmit power, we may have different factors of area throughput improvement
    Median improvement factor 2.0 is observed
Sensitivity control
  Increasing CCA level is able to improve area throughput in the beginning
  Further increasing CCA level beyond a certain level negatively impacts the area throughput
  The same trend holds for different transmit power settings, and when we have different frequency reuse
    Increasing CCA level properly almost always helps
    Optimal CCA level exists but may not be fixed values

## Slide 11: Conclusions
Transmit power control has a potential to improve system performance
  Reduced transmit power may help in certain cases
Frequency reuse, even unmanaged, improves system performance
  Improvement factor generally smaller than the frequency reuse factor
Sensitivity control improves system performance
  Higher sensitivity level, up to a certain point, helps
  Optimal CCA level is not fixed in general
Overall, transmit power control, frequency reuse, and sensitivity control may be evaluated together

## Slide 12: References
IEEE 802.11-13/1001r8, HEW SG Simulation Scenarios, Qualcomm, et.al., March 2014.
ITU-R P1238-7, Propagation data and prediction methods for the planning of indoor radio communication systems and radio local area networks in the frequency range 900 MHz to 100 GHz, 02/2012.
IEEE 802.11-13/1487r1, Dense Apartment Complex Capacity Improvements with Channel selection and Dynamic Sensitivity Control, DSP Group, December 2013.
IEEE 802.11-14/0082r0, Improved Spatial Reuse Feasibility – Part I, Broadcom, January 2014.
IEEE 802.11-14/0083r0, Improved Spatial Reuse Feasibility – Part II, Broadcom, January 2014.
IEEE 802.11-14/0523r0, MAC simulation results for Dynamic sensitivity control (DSC - CCA adaptation) and transmit power control (TPC), Orange, April 2014.
IEEE 802.11-13/1359r1, HEW Evaluation Methodology, Broadcom, et.al., March 2014.

## Slide 13: Appendix

## Slide 14: Simulation Assumptions (1 / 2)
 | Scenario Name | Topology | Management | Channel Model | Homogeneity | ~Traffic Model
1 | Residential | A - Apartment bldg. e.g. ~10m x 10m apts in a multi-floor bldg; ~10s of STAs/AP, P2P pairs | Unmanaged | Indoor | Flat | Home
Modified 11-13/1001r8 Assumptions (Modifications shown in red)
Parameter | Value
Topology | Multi-floor building: 5 floors, 3 m height in each floor; 2x10 rooms in each floor; Apartment size: 10m x 10m x 3m.
APs location | One AP per apartment at a center xy-locations at 1.5m above the floor level.
AP Type | 802.11n, 20 MHz BW nodes. All nodes in each apartment are associated with the apartment’s AP. All BSS use the same channel, i.e. reuse = 1 and 3, both with 1 channel.
STAs location | In each apartment, place 5 STAs in random xy-locations (uniform distribution) at 1.5m above the floor level (no minimum distance from the AP)
Channel model | TGn channel model B path loss; No shadow fading; No multipath fading; GF Wall penetration loss = 13 dB, Floor penetration loss = 13 dB; No interior walls; Penetration loss expression below (11-14/0083r0); Penetration loss values (ITU-R P1238-7 (2012) Table 3) with = 13 dB
Parameter | Value
Topology | Multi-floor building: 5 floors, 3 m height in each floor; 2x10 rooms in each floor; Apartment size: 10m x 10m x 3m.
APs location | One AP per apartment at a center xy-locations at 1.5m above the floor level.
AP Type | 802.11n, 20 MHz BW nodes. All nodes in each apartment are associated with the apartment’s AP. All BSS use the same channel, i.e. reuse = 1 and 3, both with 1 channel.
STAs location | In each apartment, place 5 STAs in random xy-locations (uniform distribution) at 1.5m above the floor level (no minimum distance from the AP)
Channel model | 

## Slide 15: Simulation Assumptions (2 / 2)
Parameter | Value
PHY parameters | 
Center freq and BW | All BSSs at 5GHz, using 20 MHz BW
MCS | 802.11n MCS 8– 15 using Adaptive Auto-Rate Fallback (AARF) Link Adaptation
GI | 800 ns
Data Preamble | 802.11n
STA TX power | 17 dBm; 14 dBm; 11 dBm;
AP TX Power | 23 dBm; 20 dBm; 17 dBm;
AP # of antennas | 2 for 802.11n (Nss = 2), 0 dBi antenna
STA #of antennas | 2 for 802.11n (Nss = 2), 0 dBi antenna
CCA Threshold | -90 dBm; -80 dBm; -70 dBm; -60 dBm; -50 dBm
Noise Figure | 5 dB
MAC parameters | 
Access protocol | EDCA with default parameters for 802.11n
Primary channels | All BSS use one 20 MHz channel.
Aggregation | Max transmitted A-MSDU size = 7935 B; Max acceptable A-MPDU size = 65535 B
Max # of retries | Maximum retries = 4
RTS/CTS Threshold | None
Frag. Threshold | None
Rate adaptation | Adaptive Auto-Rate Fallback (AARF)
Association | 100% of STAs in an apartment are associated to the AP in the same apartment
Management frames | Periodic, 100 msec Beacons; No probing or association messaging
FAP ACKs | included

## Slide 16: Additional Simulation Details (1 / 2)
Normalized (per-BSS) Average Throughput
  Number of bits successfully received across the entire network divided by the entire runtime and by the number of rooms with active nodes; Averaged over 10 drops
  Proportional to area throughput
  Represents the average data traffic in bits/sec successfully received and forwarded to higher layers for each BSS
  Does not include the data frames that are
    unicast frames addressed to another MAC,
    duplicates of previously received frames, and
    incomplete, meaning that not all the fragments of the frame were received within a certain time, so that the received fragments had to be discarded without fully reassembling the higher layer packet.

## Slide 17: Additional Simulation Details (2 / 2)
Average packet delay
  Average end to end delay of all data packets at the MAC layer
  Averaged over the entire runtime over 10 drops
  Represents the average end to end delay of all the data packets that are successfully received by the wireless LAN MACs of all WLAN nodes in the network and forwarded to higher layers.
  Includes medium access delay at the source MAC, reception of all the fragments individually (if any), and transfer of the frames via AP, if the source and destination MACs are non-AP MACs of the same infrastructure BSS. The medium access delay at the source MAC - includes queuing and medium access delays.

## Slide 18: Simulation Settings: Case 3
511 | 512 | 513 | 514 | 515 | 516 | 517 | 518 | 519 | 520
501 | 502 | 503 | 504 | 505 | 506 | 507 | 508 | 509 | 510
5th Floor
411 | 412 | 413 | 414 | 415 | 416 | 417 | 418 | 419 | 420
401 | 402 | 403 | 404 | 405 | 406 | 407 | 408 | 409 | 410
4th Floor
311 | 312 | 313 | 314 | 315 | 316 | 317 | 318 | 319 | 320
301 | 302 | 303 | 304 | 305 | 306 | 307 | 308 | 309 | 310
3rd Floor
211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220
201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210
2nd Floor
111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120
101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110
1st Floor
10m
10m
3m
3m
3m
3m
Active
Co-channel apartments
(Reuse 3)
Frequency reuse 3 with 1/3 of all rooms active
    33 rooms (randomly selected) active in one channel