## Slide 1: Further Considerations on Enhanced CCA for 11ax
Date: 2014-07-15
Authors:

## Slide 2: Introduction
In [1], we provided performance measurement results of increased CCA threshold in OBSS environment.
Also there have been many contributions on Enhanced CCA for 11ax, which propose to increase CCA threshold for better spatial reuse.
In this contribution, we analyze several Enhanced CCA options while utilizing 11ah’s BSS color feature with legacy consideration.

## Slide 3: CCA & Enhanced CCA
PHY layer CCA (Clear Channel Assessment)
  SD(Signal Detection): sensing 802.11 preamble
  ED(Energy Detection): sensing the signal’s energy
Enhanced CCA for 11ax [1]~[7]
  Increasing the CCA-SD(Signal Detection) threshold higher than -82dBm for better spatial reuse.
  In [2][3], authors proposed simulation results of increased CCA level considering 802.11ah’s BSS color feature
  We analyze how to incorporate 11ah’s BSS color feature for 11ax’s Enhanced CCA

## Slide 4: BSS Color
11ah’s BSS color [8]
  Motivation: If the received frame is sent by another STA/AP in MYBSS, then spatial re-use is not possible
  Sender STA/AP: In each frame, insert BSS color information (Color bits/PBSSID) that STA/AP is associated with (in PHY SIG field)
  Receiver STA/AP: For each incoming frame, inspect BSS color information,
    if MYBSS frame, it is protected regardless of the signal level
    if OBSS frame, it is protected only if the signal level is above the CCA threshold
    (note that the time required to complete CCA increases from BSS color inspection)
Enhanced CCA for 11ax (w/ BSS color)
  Operates same as above, except that
    the CCA threshold applied to OBSS frame can be increased for better spatial reuse
    there are legacy (11a/n/ac) STAs having the lower CCA threshold (-82dBm) and the shorter CCA timing (4us)

## Slide 5: Current CCA Threshold levels
Any Signal | 
OBSS | MYBSS
OBSS | MYBSS
RX
Sensitivity
CCA-SD
CCA-ED
X
frame from X is protected
frame from X is NOT protected (for spatial reuse)
X
802.11ah AP/STA
received frame’s
RSSI
Any Signal
Any BSS
Any BSS
RX
Sensitivity
CCA-SD (-82dBm)
CCA-ED (-62dBm)
802.11 AP/STA
1) Having the lower RX Sensitivity (~-90dBm) than the CCA-SD is common but implementation specific.

## Slide 6: Enhanced CCA for 11ax – Option 1
Any Signal
ANYBSS
ANYBSS
RX
Sensitivity
CCA-SD(ax)
CCA-ED1)
11ax AP/STA
Increased CCA
  11ax AP/STA applies increased CCA-SD(ax) level on any received frame
Problems
  Spatial reuse on MYBSS frame
  Reduction of DL/UL coverage from the increased CCA
  Unfair to legacy STAs
  It’s not trivial to find the optimal CCA-SD(ax) level that satisfies all scenarios.
1) CCA-ED also needs to be increased according to CCA-SD(ax). Not described here for simplicity.

## Slide 7: Enhanced CCA for 11ax – Option 2
11ax AP/STA
Increased CCA + BSS color
  A frame received under CCA-SD(ax) level is BSS-color-inspected, and OBSS frame is NOT protected
Problems
  Works only when there are no legacy STAs
    11ax STA will require longer time to inspect received frame’s BSS color while legacy STA will finish normal CCA in much shorter time on the same frame (disadvantageous to 11ax STA)
    OBSS(legacy) STA is unfair
Any Signal | 
OBSS | MYBSS
OBSS | MYBSS
CCA-ED
CCA-SD(ax)
RX
Sensitivity

## Slide 8: Enhanced CCA for 11ax – Option 3
11ax AP/STA
Increased CCA + BSS color + legacy consider
  A frame received bet’n CCA-SD(legacy) and CCA-SD(ax) is BSS-color-inspected, OBSS(ax) frame is NOT protected
  A frame received below CCA-SD(legacy) is NOT protected
Problems
  Seeing no significant problems !
    No MYBSS frame is sacrificed
    No legacy STA is unfairly treated
    No UL/DL coverage reduction
    Obtain spatial reuse on OBSS(ax) frames only
Issues for further enhancement
  How to protect MYBSS frames received under CCA-SD(legacy)? Is it required?
Any Signal |  |  | 
OBSS |  | MYBSS | 
OBSS (ax) | OBSS (legacy) | MYBSS (legacy) | MYBSS (ax)
OBSS (ax) | OBSS (legacy) | MYBSS (legacy) | MYBSS (ax)
CCA-ED
CCA-SD(ax)
RX
Sensitivity
CCA-SD(legacy)
* RX procedure
(see next slide)

## Slide 9: * RX Procedure (Option 3)
frame is protected regardless of the signal level
AIFS
DATA
Preamble
BSS
Color
DATA
backoff
AIFS
ACK
ACK
Case2) RX frame’s BSS color is MYBSS
frame is protected if RSSI is above CCA-SD(legacy)
AIFS
DATA
Preamble
No
Color
DATA
backoff
AIFS
backoff
(resumed)
ACK
ACK
My TX
DATA
Case1) RX frame does not have BSS color (legacy frame)
backoff
(resumed)
My TX
DATA
When RX frame’s signal level is bet’n CCA-SD(legacy) and CCA-SD(ax), there are three Cases as follows
5
4
3
2
1
5
4
3
2
1

## Slide 10: * RX Procedure (Option 3) – cont’d
DATA
Preamble
BSS
Color
ACK
DATA
My TX DATA
frame is NOT protected if RSSI is below CCA-SD(ax)
AIFS
backoff
ACK
AIFS
Case3) RX frame’s BSS color is OBSS
backoff
(resumed)
Issues
  During the resumed backoff period, STA requires preamble detection-based CCA on top of the on-going OBSS frame
    In order to detect start of any frame transmission from MYBSS or any third BSSs
  The higher we increase CCA-SD(ax), the more challenge to the preamble detection
5
4
3
2
1

## Slide 11: Summary
We summarized several options for utilizing Enhanced CCA for 11ax.
Many previous contributions seem to have tried to find the optimal CCA level within the Enhanced CCA – Option 1.
We provided detailed design of Enhanced CCA – Option 3, that utilizes 11ah’s BSS color feature and consideration of legacy devices.
  No MYBSS frame is sacrificed
  No legacy STA is unfairly treated
  No UL/DL coverage reduction
  Obtain spatial reuse on OBSS(ax) frames only
  Still it requires careful evaluation for the optimal CCA-SD(ax) level selection
Also there are several problems [6] to solve, common for all Enhanced CCA methods
Two identified issues on Enhanced CCA-Option 3 are
  How to protect MYBSS frames received under CCA-SD(legacy) ?
  The higher we increase CCA-SD(ax), the more challenge to the preamble detection during OBSS frame

## Slide 12: References
[1] 11-14/0629r0 Measurements on CCA Thresholds in OBSS Environments
[2] 11-14/0082r0 Improved Spatial Reuse – Part I
[3] 11-14/0372r2 System level simulations on increased spatial reuse
[4] 11-14/0523r0 MAC simulation results for DSC and TPC
[5] 11-14/0578r0 Residential Scenario CCA/TPC Simulation Discussion
[6] 11-14/0637r0 Spatial Reuse and Coexistence with Legacy Devices
[7] 11-14/0779r0 DSC Practical Usage
[8] 11-13/1207r1 CID 205 BSSID Color Bits