## Slide 1: Techniques for Short Downlink Frames
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco |  | brianh@cisco.com
Sean Coffey | Realtek |  | coffey@realtek.com
Leif Wilhelmsson | Ericsson AB |  | leif.wilhelmsson@ericsson.com
Kåre Agardh | Sony Mobile |  | kare.agardh@sonymobile.com
Sigurd Schelstraete | Quantenna |  | sschelstraete@quantenna.com

## Slide 2: Overview
Situation:
  Whether or not a user is running obvious network applications (browsing, video streaming, etc), their 802.11 client continually receives (and transmits) short packets, at a low duty cycle [1-7]
    Uplink: NBNS, LDAP, LLMNR, BJNP, ARP, DNS
    Downlink unicast: NBNS, LDAP, ARP, DNS
    Downlink multicast/broadcast: LLMNR, BJNP, ICMPv6, IGMPv2
    60-120 octets is typical of these frames
  Problem tackled in this presentation:
  It is difficult to aggregate such downlink traffic; recent channel sounding is not available for such traffic
  Networks with many users per channel experience poor throughput due to preamble overheads
  Solution:
  Study different MU/aggregation schemes, and if a new technique is found that outperforms existing 802.11 techniques, then add a short frame requirement to the 802.11ax SFD

## Slide 3: Transmission duration comparison
Technique ID | Technique | Medium time (see notes)
0 | Aggregation with other traffic to the same RA | Disallowed due to traffic pattern
1 | Explicit sounding + DL-MU-MIMO Data + polled BAs | >= 846 us
2 | 4 * Data+Ack | 456 us
3a | PSMP (SIFS) | 462 us
3b | PSMP (RIFS) | 350 us
4 | DL-OFDMA Data + UL-MU-MIMO Ack | 142 us
5 | DL-OFDMA Data + UL-OFDMA Ack | 114 us
  What is the best way to send 4 downlink frame to 4 clients, in an 80 MHz BSS, where each frame carries 90 octets?
  Large available gains!
Notes: Assumptions:
Downlink traffic
80 MHz 
Intermittent traffic – not suitable for aggregation, no recent sounding 
AP density is high, AP antenna count is high (i.e. highest MCS is always available for Data) 
No collisions, no retries 
Clients have 1 antenna only 
24 Mbps 11ag control frames 
No RTS/CTS 
No overheads to point clients ot the correct subchannel with OFDMA 
Preamble duration for UL-MU-MIMO with 4SStot is same as VHT preamble length for 4SStot
VHT Data frames for MU-MIMO, else shortest 11ag/HT_MM/VHT Data frames (BCC) 
Count DIFS after Ack as overhead (not backoff times, which are shared) 
PSMP uses SIFS
Slot = 9us [A], SIFS = 16us [B], RIFS = 2us [B2], DIFS = B+2*A=34us [C]
Precalculations
TXTIME of 90 octet frame at maximum MCS
11ag: 20us + 4us*ceil((22+90*8)/(54e6*4e-6)) = 36us [D]
HT40-1SS: 36us + 4us*ceil(3.6/4*ceil((22+90*8)/(150e6*3.6e-6))) = 44us [E]
VHT80-1SS: 40us + 4us*ceil(3.6/4*ceil((22+90*8)/(433.3e6*3.6e-6))) = 44us [F]
G = min(D,E,F) = D = 36us
VHT80-(1+1+1+1)SS: 52us + 4us6*ceil(3.6/4*ceil((22+90*8)/(433.3e6*3.6e-6))) = 56us [H]
TXTIME of Ack frame at 24 Mbps
11ag: 20us + 4us*ceil((22+14*8)/(24e6*4e-6)) = 28us [I]
Uplink MU80-(1+1+1+1)SS: 52us + 4us*ceil(3.6/4*ceil((22+14*8)/(433.3e6*3.6e-6))) = 56us [J]
TXTIME of PSMP frame at 24 Mbps
11ag: 20us + 4us*ceil((22+64*8)/(24e6*4e-6)) = 44us [K]
TXTIME of VHT NDP Announcement frame at 24 Mbps
11ag: 20us + 4us*ceil((22+29*8)/(24e6*4e-6)) = 44us [L]
TXTIME of VHT NDP PPDU
VHT->=4SS: >=52us [M]
TXTIME of Beamforming Report frame at 24 Mbps (>=332 octets)
VHT80-1SS: 40us + 4us*ceil(3.6/4*ceil((22+332*8)/(433.3e6*3.6e-6))) or >=48us [N]
TXTIME of Beamforming Report Poll frame at 24 Mbps
11ag: 20us + 4us*ceil((22+21*8)/(24e6*4e-6)) = 28us [O]
TXTIME of BAR frame at 24 Mbps
11ag: 20us + 4us*ceil((22+24*8)/(24e6*4e-6)) = 32us [P]
TXTIME of BA frame at 24 Mbps
11ag: 20us + 4us*ceil((22+32*8)/(24e6*4e-6)) = 32us [Q]
Technique 1
L+B+M+B+N+3*(B+O+N) + B+H+B+Q+3*(B+P+Q)+C or >=846 us
Technique 2
4*(G+B+I+C) = 456 us
Technique 3a
K+4*(B+G)+4*(B+I)+C = 462 us
Technique 3b
K+4*(B2+G)+4*(B2+I)+C = 350 us
Technique 4
G+B+J+C = 142 us
Technique 5
G+B+I+C = 114 us

## Slide 4: Socializing the following (no strawpoll yet)
Add to the SFD:
“The 802.11ax amendment shall require a solution that provides significantly increased efficiency for short MSDUs (<250 octets) intermittently transmitted to different non-AP STAs”

## Slide 5: Short Frame/Packet References
[1] Bill Carney et al, 11-13-0728-01-0hew-network-optimization-for-expected-traffic-patterns.pptx
[2] Jim Lansford, 11-14-0546-01-00ax-packet-traffic-measurements-around-boulder-colorado.ppt
[3] Phillip Barber et al, 11-13-1438-00-0hew-traffic-observation-and-study-on-virtual-desktop-infrastructure.pptx
[4] Bill Carney et al, 11-13-1305-00-0hew-traffic-simulation-simplifications.pptx
[5] Ericsson measurement, 2012/Q4, smartphone-dominated mature LTE/HSPA/2G network
[6] A. Doufexi, S. Armour, P. Karlsson, M. Butler, A. Nix, D. Bull, J. McGeehan, “A Comparison of the HIPERLAN/2 and IEEE 802.11a Wireless LAN Standards,” IEEE Communications Magazine, May 2002, Vol. 40, No. 5
[7] ChaoChun Wang et al, 11-13-1407-00-0hew-simulation-based-study-of-qoe.pptx