## Slide 1: Evaluating Dynamic CCA/Receiver Sensitivity Algorithms
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Reza Hedayat | Cisco Systems |  | rehedaya@cisco.com
Sigurd Schelstraete | Quantenna |  | sschelstraete@quantenna.com
Tomo Adachi | Toshiba Corp. |  | tomo.adachi@toshiba.co.jp
Sean Coffey | Realtek |  | coffey@realtek.com

## Slide 2: Overview
Situation:
  802.11 “just works”. By virtual of the MAC’s use of physical/virtual carrier sense, back-off and MAC protection, 802.11 can tolerate odd AP deployments and unusual propagation.
  The 802.11 MAC is not perfect (hidden nodes, exposed nodes)
  In 802.11ax we have many proposals for optimizing CCA thresholds and/or receiver sensitivities
  Problem:
  A poorly chosen dynamic CCA or receiver sensitivity control algorithm may degrade the “it just works” property of 802.11 in important scenarios (for instance, Service Provider Wi-Fi)
  Solution:
  In simulations and presentations, give primary weight to simulation scenarios where dynamic CCA/receiver sensitivity proposals might fail, and secondary weight to simulation scenarios where dynamic CCA/receiver sensitivity proposals are likely to succeed. Accordingly focus on algorithms that are both
    As robust as the status quo in non-ideal deployments
    More efficient in ideal deployments

## Slide 3: Service Provider Wi-Fi Case That Should Be Checked
Multi-tenant office/mall or apartment building
  The Home AP and client are very close.
    If they can select a degraded CCA threshold, they can transmit over the top of the SP AP’s transmissions and impair the SP downlink.
    If they can select a degraded receiver sensitivity, they can ignore frames (including RTS/CTS) from the SP AP, transmit over the top of the SP AP’s transmissions and impair the SP downlink.
  The large coverage of the SP AP overlaps with many home APs (so channel selection cannot help)
  Very similar case arises with multiple small Wi-Fi Direct BSSs and a larger infrastructure BSS
Service Provider AP (“Outdoor hotspot”)
Tenant2
Client
Tenant1
Client
Home AP

## Slide 4: Summary
It is easy to design dynamic CCA or dynamic receiver sensitivity algorithms that work well in a network of similarly sized / relatively non-overlapping BSSs
To preserve Wi-Fi’s “it just works” property, we need something better – something that works even in overlapping BSSs with very different sizes and geometries
This is not a pipe-dream – such ideas are available