## Slide 1
PHY SIG Frame Structure for IEEE 802.11aj (45GHz)
Authors/contributors:
Date: 2014-09-09
Presenter: Haiming Wang

## Slide 2
Shiwen He, Haiming Wang
Slide 2
Abstract
The submission presents the physical layer (PHY) SIG frame structure to enable downlink multi-user MIMO WLAN communications for IEEE 802.11aj (45GHz).
This submission is an update version of IEEE 802.11-14/0883r0 which was presented in July 2014 plenary session.
Notes: 2

## Slide 3
Shiwen He, Haiming Wang
Slide 3
Background
Challenges of future WLAN
  Limited spectrum resources
  Requirement for very high data rate
Features of future WLAN
  Large bandwidth
  Multiple channel mode
  Multi-user
  Multi-stream
  Beyond 10 Gbps throughput
Notes: 3

## Slide 4
Shiwen He, Haiming Wang
Slide 4
Technology Objects
Technical goal:
  Dynamic BW
  Multi-user & Multi-stream
  Energy efficiency
  Scrambler
  Single-Carrier & OFDM
Dynamic BW
  Dynamic channel BW selection for 1080 MHz BSS to enhance the adaptability in different channel environments and improve spectral efficiency.
Notes: 4

## Slide 5
Shiwen He, Haiming Wang
Slide 5
Technology Objects
Multi-user & Multi-stream
  Achieve a multi-user multi-stream control to obtain the multiplexing gain.
Energy efficient communication
  Achieve energy efficient communication, i.e., allow non-AP STAs in TXOP power save mode to enter Doze state during a TXOP.
Scrambler
  Scrambling effectively reduces the PAPR in OFDM system .
Single carrier & OFDM
  Switch between SC and OFDM.
Notes: 5

## Slide 6
Shiwen He, Haiming Wang
Slide 6
SIG-A structure
The SIG-A field carries information required to interpret PPDUs.
To support more MCSs, the number of the bits in the MCS field is increased to 4 from 3.
To track the change of CSI, a midamble field is added to indicate the transmission style of the training field in SC PHY.
The researches in [1] have revealed that CRC 0x83=x8+x2+x+1 is enough to check the SIG-A fields.
Notes: 6

## Slide 7
Shiwen He, Haiming Wang
Slide 7
Explanation of each field in SIG-A
Scrambler
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7 | SC/OFDM | 1 | Set to 0 if SC transmission is adopted for PPDU, set to 1 if OFDM transmission is adopted for PPDU.
B8 | BW | 1 | Set to 0 for 540MHz, set to 1 for 1080MHz.
B9 | Dynamic Bandwidth | 1 | If BW=1 and Duplicate=1: set Dynamic Bandwidth to 1 for allowing dynamic bandwidth; set to 0 for non allowing dynamic bandwidth. Otherwise set to 0; (Reserved)
B10-B11 | Sub-Band | 2 | Bitmap (B10-B11): If Dynamic Bandwidth=1, set to 10 for using the primary 540MHz channel, set to 01 for using the secondary 540MHz channel; set to 11 for using 1080MHz channel; Otherwise set to 00 (reserved).
Notes: 7

## Slide 8
Shiwen He, Haiming Wang
Slide 8
Explanation of each field in SIG-A
SC-PHY & OFDM-PHY
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7 | SC/OFDM | 1 | Set to 0 if SC transmission is adopted for PPDU, set to 1 if OFDM transmission is adopted for PPDU.
B8 | BW | 1 | Set to 0 for 540MHz, set to 1 for 1080MHz.
B9 | Dynamic Bandwidth | 1 | If BW=1 and Duplicate=1: set Dynamic Bandwidth to 1 for allowing dynamic bandwidth; set to 0 for non allowing dynamic bandwidth. Otherwise set to 0; (Reserved)
B10-B11 | Sub-Band | 2 | Bitmap (B10-B11): If Dynamic Bandwidth=1, set to 10 for using the primary 540MHz channel, set to 01 for using the secondary 540MHz channel; set to 11 for using 1080MHz channel; Otherwise set to 00 (reserved).
Notes: 8

## Slide 9
Shiwen He, Haiming Wang
Slide 9
Explanation of each field in SIG-A
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7 | SC/OFDM | 1 | Set to 0 if SC transmission is adopted for PPDU, set to 1 if OFDM transmission is adopted for PPDU.
B8 | BW | 1 | Set to 0 for 540MHz, set to 1 for 1080MHz.
B9 | Dynamic Bandwidth | 1 | If BW=1 and Duplicate=1: set Dynamic Bandwidth to 1 for allowing dynamic bandwidth; set to 0 for non allowing dynamic bandwidth. Otherwise set to 0; (Reserved)
B10-B11 | Sub-Band | 2 | Bitmap (B10-B11): If Dynamic Bandwidth=1, set to 10 for using the primary 540MHz channel, set to 01 for using the secondary 540MHz channel; set to 11 for using 1080MHz channel; Otherwise set to 00 (reserved).
Dynamic bandwidth
Notes: 9

## Slide 10
Shiwen He, Haiming Wang
Slide 10
Explanation of each field in SIG-A
Multi-user & Multi-stream
Bit | Fields | Number of Bits | Description
B12-B29 | Length | 18 | SU：Number of data octets in the PSDU, Range 1-162143; MU：Maximum number of data octets in the PSDU of all users, Range 1-162143.
B30 | STBC | 1 | For an SU PPDU: set to 1 if space time block coding is used and set to 0 otherwise. For a MU PPDU: set to 0.
B31-B36 | GroupID | 6 | Set to the value of the TXVECTOR parameter GROUP_ID. A value of 0 or 63 indicates a SU PPDU; otherwise, indicates a MU PPDU.
B37 | Aggregation | 1 | Set to 1 indicate that the PPDU in the data portion of the packet contains an A-MPDU; otherwise, set to 0.
Notes: 10

## Slide 11
Shiwen He, Haiming Wang
Slide 11
Explanation of each field in SIG-A
Multi-user & Multi-stream
Bit | Fields | Number of Bits | Description
B38-B40 | Midamble | 3 | For SC transmission, transmit a SC-BTF block every a specified data blocks ; For OFDM transmission, this field is undefined.
B41-B51 | NSTS/Partial AID | 11 | For a MU PPDU: NSTS is divided into 4 user positions of 2 bits each. User position , where , uses bits B(38+) to B(39+). The number of space time streams for user are indicated at user position =USER position[ ], where….,NUM-USERS-1, and the notation A[b] denotes the value of array A at index b. Zero space-time streams are indicated at positions not listed in the USER_POSITION array. Each user position is set as follows: Set to 0 for 0 space-time streams Set to 1 for 1 space-time stream Set to 2 for 2 space-time streams B46-B48：set to zero, reserved For a SU PPDU: B38-B39 Set to 0 for 1 space-time stream Set to 1 for 2 space-time streams Set to 2 for 3 space-time streams Set to 3 for 4 space-time streams B40-B48 Partial AID: Set to the value of the TXVECTOR parameter PARTIAL_AID. Partial AID provides an abbreviated indication of the intended recipient(s) of the PSDU.
Notes: 11

## Slide 12
Shiwen He, Haiming Wang
Slide 12
Explanation of each field in SIG-A
Multi-user & Multi-stream
Bit | Fields | Number of Bits | Description
B52-B55 | SU MCS | 4 | For a SU PPDU: MCS index For a MU PPDU: reserved
B56 | Precoded | 1 | For a SU PPDU: Set to 1 if a Beam-forming steering matrix is applied to the waveform in an SU transmission as described in TBD, set to 0 otherwise. For a MU PPDU: Reserved and set to 1
B57-B64 | CRC | 8 | SIG-A check sequence. Definition of this field calculation is in TBD.
B65-B71 | Reserved | 7 | Reserved
Notes: 12

## Slide 13
Shiwen He, Haiming Wang
Slide 13
Transmitter Block Diagram for SIG-A fields Using SC Transmission
The SIG-A field carries information required to interpret PPDUs transmission. And the SIG-A field is transmitted with SC transmission.
Notes: 13

## Slide 14
Shiwen He, Haiming Wang
Slide 14
SIG-B structure
Bit | Fields | Number of Bits | Description
B0-B6 | Scrambler Initialization | 7 | The initial scrambler state.
B7-B9 | MCS | 3 | MCS index.
B10-B27 | Length | 18 | Number of data octets in the PSDU, Rang 1-162143.
B28-B31 | Reserved | 4 | Reserved.
B32-B47 | CRC | 16 | SIG-B check sequence. Definition of this field calculation is in TBD.
The SIG-B field carries information required to interpret PPDUs in MU transmission case.
Notes: 14

## Slide 15
Shiwen He, Haiming Wang
Slide 15
Transmitter Block Diagram for SIG-B fields Using OFDM MU PPDU Transmission
The SIG-B field carries information required to interpret PPDUs in MU transmission case. In other word, the SIG-B field is only transmitted for the MU case.
Notes: 15

## Slide 16
Shiwen He, Haiming Wang
Slide 16
Reference
[1] P. Koopman,T. Chakravarty, Cyclic Redundancy Code (CRC) Polynomial Selection For Embedded Networks, The International Conference on Dependable Systems and Networks, DSN-2004.
[2] PHY SIG Frame Structure for IEEE 802.11aj (45GHz), IEEE 802.11-14/0883r0
Notes: 16

## Slide 17
Shiwen He, Haiming Wang
Slide 17
Thanks for Your Attention.
Notes: 17

## Slide 18
Shiwen He, Haiming Wang
Slide 18
What is the motivation for the design of our SIG?
  The main role of our SIG is to carry information which is required to interpret the physical protocol data unit (PPDU).
  The basic required information to carry is listed as:
    Dynamic bandwidth
    Multi-user & Multi-stream
    Energy efficiency
    Scrambler initialization
    Single & Multi-carrier
Questions & Replies
Notes: 18

## Slide 19
Shiwen He, Haiming Wang
Slide 19
What is the difference between VHT-SIG and our SIG?
  The scrambler initialization field is included in our SIG, which is located in the service field that is removed in IEEE 802.11ac, due to the motivation of further enhancement of reducing the PAPR of SIG and reducing the SIG transmission overhead, such as the transmission of SIG-B in single user transmission for IEEE 802.11aj (45GHz).
  The indication of the dynamic bandwidth is also included in the SIG field.
  A subfield which indicates the modulated model is added in the SIG field.
Questions & Replies
Notes: 19

## Slide 20
Shiwen He, Haiming Wang
Slide 20
What are the key features of the SIG?
  The key features of the SIG are listed as follows:
    Scrambler initialization: reducing the PAPR.
    Dynamic bandwidth: improving the spectral efficiency.
    Multi-user & Multi-stream: enhancing the system capacity.
    Energy efficiency: reducing the power consumption.
    SC & OFDM: considering the PAPR and the power amplifier efficiency due to the fact that, in some cases, the power efficiency is more important than the spectral efficiency in the mmWave WLAN systems.
Questions & Replies
Notes: 20

## Slide 21
Shiwen He, Haiming Wang
Slide 21
How to support more MCSs?
To support more MCSs, the number of the bits in the MCS field is increased to 4 from 3. Combining with SC/OFDM field, IEEE 802.11aj(45GHz) can support 32 MCSs.
Questions & Replies
Notes: 21