## Slide 1: Security and Privacy Enhancements for 802.11
Date: 2014-07-15
Authors:

## Slide 2: Security and Privacy

## Slide 3: Wireless Threats for 802.11 Communications
The location and capabilities of an attacker in the network is a useful way to categorize vulnerabilities.

## Slide 4: 802.11 Security – What Could be Improved
Wireless security is hard to setup and use in consumer devices
Passwords are still the dominate way consumer products setup 802.11 security
  Why are
Open, WEP and TKIP are still being used
  WEP and TKIP should be removed from 802.11
  Opportunistic Security could eliminate Open
802.11 lacks adequate support for peer-to-peer authentication

## Slide 5: Opportunistic Security
“In contrast to the established approach of delivering strong protection some of the time, opportunistic security strives to deliver at least some protection most of the time. The primary goal is therefore broad interoperability, with security policy tailored to the capabilities of peer systems.”
http://datatracker.ietf.org/doc/draft-dukhovni-opportunistic-security

## Slide 6: Strong Device-to-Device Authentication
IEEE 802.11 does not have a “good” solution for device-to-device authentication
Preshared keys are problematic:
  Difficult to install
  Poor authentication (can be reshared)
EAP based methods are designed to use a remote server
  Difficult to configure
  Few APs have built in server (one approach for perr-to-peer)

## Slide 7: Device-to-Device Authentication Possible Use Cases and Benefits
Simplified secure device discovery
  All devices have an provable identity
  Enables good peer-to-peer security
Easy device enrollment and installation
  Provable identity greatly simplifies installation process
  Simplified installation of headless devices (sensors, etc)
Cost and complexity reduced for systems needing centralized authorization

## Slide 8: Peer-to-Peer Identity Framework
Every device has a public / private key
  hash of public key is used as identity
  True peer-to-peer (either side can initiate)
  Preassociation key exchange
  based on well defined cryptographic standards (ECDH, etc.)
  Used to simplify user experience for device enrollment

## Slide 9: Examples of Hash Based Cryptographic Identifiers
Bitcoin
  e.g. 1HB5XMLmzFVj8ALj6mfBsbifRoD4miY36v
IPv6 and HIP (RFC 5201)

## Slide 10: Simple Device Enrollment
Devices have a identity out-of-the box
  Self generated key pair
  Binding of wireless authentication to a specific device
    Label based on public key (truncated readable hash)
    Remote enrollment based on knowing identity
    Enrollment authentication may be facilitated by
      QR code, NFC, Bluetooth
      Human label validation

## Slide 11: Scalable Access Authorization
Can I2 enter network?
K1
K2
Access control servers do NOT need to hold any secrets
I1
I2
Ki is device unique public key
Ii is device unique identifier from hash of Ki, Cipher Suite

## Slide 12: Communication privacy is not a new issue.
Privacy was an important selling point for dial based phones (1912) since they did not require an operator.
http://en.wikipedia.org/wiki/Privacy

## Slide 13: Wi-Fi Privacy Concerns
Seattle Police Deactivate Wi-Fi Spy Grid After Privacy Outcry (Nov 2013)
  A DHS and Seattle police network collecting location information
CreepyDOL WiFi surveillance project debuts at Blackhat/DEFCON (Aug 2013)
  DIY surveillance with low-cost Wi-Fi based sensors that capture MAC addresses
Wi-Fi Trashcans Now Silently Tracking Your Smartphone Data (Aug 2013)
  ... the company boasted that the cans, which included LCD advertising screens, "provide an unparalleled insight into the past behavior of unique devices"—and hence of the people who carry them around
"Technopanic" mounts over Google's Wi-Fi Privacy violations (Mar 2013)
  A DHS and Seattle police network collecting location information

## Slide 14: But wait – Wi-Fi “location” is also a service!
Location-based Wi-Fi services can add immediate value to Wi-Fi deployments (Oct 2013)
  “Knowing where someone is can be important because you are then in a better position to do something for or with them.”
In-Location Alliance (Nov 2013)
  “There are countless uses for accurate indoor positioning ...”
Renew - Wi-Fi based market information (Nov 2013)
  The Renew Network extends to over three million professionals in the City of London everyday. Our units have been strategically placed to achieve optimum viewing time, enabling our clients to receive a constant and continuous space to accommodate commercial campaigns.

## Slide 15: Privacy Threats
Source of Threats:
  Hackers, private investigators, stalkers, paparazzi
  Marketing firms and retail outlets
  Police, Government Agencies
Non-threats:
  Marketing firms and retail outlets (with user approval)
  Personal home automation (of home user)
  ... Etc.
It is very important to identify ways to enable tracking when it is a “service”, but prevent unauthorized tracking

## Slide 16: What we should avoid as a 802.11 privacy solution
From one system vendor:
“Participation in Wi-Fi location services is completely up to the customer or visitor - they can opt out simply by turning off their Wi-Fi signal.”

## Slide 17: Privacy versus other Security Services in 802.11
Privacy protection is provided by encryption and authentication
  But this just protects the disclosure “data”
  Good security (e.g. RSN) is a first step and is not the subject of this analysis and is assumed as a starting point
Privacy of identity and location must consider other information in 802.11 frames that can be used to track a device
  the MAC address
  Active probing and SSIDs

## Slide 18: Where can 802.11 privacy be improved?
MAC Addresses are unique per device
  Enable detailed tracking by passive capture
  MAC addresses may be used in IPv6 addresses and carried beyond the WLAN and will directly identify the connecting device
SSIDs are sometimes unique
  Enable tracking when used in probe requests and indicate a devices commonly used APs
  The profile of multiple SSIDs used in probing are a good fingerprint of a users identity
802.11u is unprotected and may indicate user interests
Others?

## Slide 19: Passive Scanning and Monitor APs
The primary scenarios to consider that are a “threat” and not “services” are passive monitoring and APs used for monitoring

## Slide 20: Possible Technical Solutions for Privacy
Ephemeral MAC Addresses
  use local addresses that change occasionally
Limit active scanning
Define alternate ways to discover “services” and Aps
Capability bits to indicate “willingness to be tracked”
Others?

## Slide 21: Ephemeral MAC Addresses
Virtual STAs could be defined that allow a device to have a different MAC address for each BSSID
What happens to DHCP allocation and routing tables?
  Rapid changes are a problem, occasional changes are enough to prevent correlation of a device to a human
Not easy to change with an active association
  But could only change on new connections
Roaming and fast handoff might be impacted
  But MAC addresses could remain the same for roaming and only change when not actively associated
Careful use of Ephemeral MAC Addresses would provide significant improvements in 802.11 address privacy!

## Slide 22: A few Proposals for 802.11 Privacy Enhancements
2002 - Temporary MAC Addresses for Anonymity
2004 - Anonymous MAC Addresses
2008 - SlyFi-Enhancing_80211_Privacy
2013 - Service Discovery Proposal
2013 - 802.11 Privacy
2014 - random-macs-for-privacy
2014 - Privacy Enhanced Wireless
IEEE 802.11-14/0367r2 Privacy Enhanced Wireless
  “When a STA is not a member of a BSS it should periodically change its MAC address to a random value. “
IEEE 802.11 should adopt 802.11-14/0367r2