## Slide 1: Calibration of MAC simulator with OBSS Network Scenario
Date: 2014-07-14
Authors:

## Slide 2: Summary
14/0621 r4 lists five MAC simulator calibration scenarios
  All five cases measure the throughput of 20MHz channel with one or two BSSs
11ax network will consists of 11ax STAs and legacy 11b/g/n/ac STAs
  The simulation will have to address the cases that there are STAs and BSSs operating with different channel bandwidth
It is beneficial for MAC Calibration to include one or more cases to evaluate the performance of BSSs operate with different channel bandwidth

## Slide 3: Proposal
Same MAC and PHY Parameters are specified in 14/0621 r4
The two BSSs has different channel bandwidth, one is 20MHz and another one is 40 MHz

## Slide 4: Deferral test for network of different channel bandwidth
The set up and configuration is the same as test case 2a
The first BSS operates in 40 MHz channel
The second BSS operates in a 20MHz channel which is the secondary channel of the first BSS
Measuring the results throughput and PER of each BSS
AP1
AP2
STA2
STA1
BSS_2
BSS_1

## Slide 5: Deferral test for network of different channel bandwidth
The set up and configuration is the same as test case 2b
The first BSS operates in 40 MHz channel
The second BSS operates in a 20MHz channel which is the secondary channel of the first BSS
Measuring the results throughput and PER of each BSS
AP1
AP2
STA2
STA1
BSS_2
BSS_1

## Slide 6: Straw Poll
Do you agree to include the proposed test cases in the simulation calibration scenario?
  Y
  N
  Abs