## Slide 1: Calibration of MAC simulator with OBSS Network Scenario
Date: 2014-07-14
Authors:

## Slide 2: Summary
14/0621 r4 lists five MAC simulator calibration scenarios
  All five cases measure the throughput of 20MHz channel with one or two BSSs
11ax network will consists of 11ax STAs and legacy 11b/g/n/ac STAs
  The simulation will have to address the cases that there are STAs and BSSs operating with different channel bandwidth
It is beneficial for MAC Calibration to include cases to evaluate the performance of BSSs operate with different channel bandwidth

## Slide 3: Proposal
Same MAC and PHY Parameters are specified in 14/0621 r4
The two BSSs has different channel bandwidth, one is 20MHz and another one is 40 MHz
  The goal is verified that simulators have the same baseline MAC behavior and throughput.
The metrics for evaluation may include but not limit to check points, throughput

## Slide 4: Deferral test for network of different channel bandwidth
The set up and configuration is the same as test case 2a
  If packets collide, the both transmission fail
The first BSS operates in 40 MHz channel
The second BSS operates in a 20MHz channel which is the secondary channel of the first BSS
  With no channel model, the collision detection is determined by time domain information
    Any overlapping MPDU is considered a failure
  The secondary channel is consider free if there is no transmission on the secondary channel for PIFS
The 40MHz BSS is running full buffer.
The 20MHz BSS traffic is based on the Weibull distribution
  2Mbps traffic, lamda = 695, k=0.8099
The results other than throughput and PER of each BSS also include
  The percentage of time the 40MHz BSS running in 40 and 20 MHz mode.
AP1
AP2
STA2
STA1
BSS_2
BSS_1

## Slide 5: Straw Poll
Do you agree to include the proposed test case on page 4 in the simulation calibration scenario document?
  Y
  N
  Abs