## Slide 1: EPD, Mixed BSSes, and Group RAs
Date: 2014-07-17
Authors:

## Slide 2: Abstract
This presentation describes one way to resolve a number of intertwined 802.11ak (GLK) questions.

## Slide 3: Capabilities
GLK stations indicate they are GLK by including a GLK Information Element in Beacons, Probe Requests, Probe Responses, DMG Beacons, Mesh Peering Opens, and Mesh Peering Confirms.
Capabilities/Options are indicated by bits/fields within the GLK IE, except that
  Support of EPD is indicated by Capability Information Field bit 13 and DMG Capability Information Field bit 62.

## Slide 4: Pairwise STA Communications
IBSS, PBSS, Direct Link, Mesh Peer, and Individually Addressed AP ↔︎ non-AP MSDUs are
  EPD if both stations support EPD and
  LPD otherwise.

## Slide 5: Mixed BSSes
An AP may permit association of non-AP STAs regardless of their GLK or EPD support.
  Such AP policy is indicated by two BSS membership selector values, indicating that support is required, one for GLK and one for EPD. Non-APs STAs attempting to associate in violation of the policy are rejected.
  We should consider renaming the “Supported Rates” IE to be the “Supported Rates and BSS Membership Selectors” IE.

## Slide 6: Group Addressed RAs
An AP uses LPD for MPDUs with Group Addressed RAs unless it requires associating non-AP STAs to support EPD, in which case it uses EPD.
A GLK AP transmitting an MPDU with Group Addressed RA shall use an RA constructed as shown on the following slide.

## Slide 7: GLK Group RA
GLK APs send MPDUs with a Group Addressed RA only using an RA constructed with a new TBD OUI. The lower 24 bits have additional information, including subsetting. Optionally, there could be support for a larger amount of subsetting information later in the frame.
GLK non-AP STAs ignore MPDUs with a Group Addressed RA not formed as above.
01-TB-D0
bits