## Slide 1: Parameters for Power Save Mechanisms
Date: 2014-09-15
Authors:

## Slide 2: Outline
Baseline power save mechanisms
Summary of parameters for power save mechanisms
Calibration test for MAC simulator
Conclusion

## Slide 3: Baseline Power Save Mechanisms
The contribution 11-14/827r3 [1] proposed to adopt 3 existing power save mechanisms in 802.11-2012 [2] as baseline for energy efficiency evaluation
  Power save mode (PSM)
  Power save polling (PSP)
  Unscheduled automatic power save delivery (U-APSD)
This is a follow up contribution discussing:
  Parameters associated with each baseline power save mechanism
  Calibration of the MAC simulator for power save mechanisms

## Slide 4: Summary of Parameters for Power Save Mechanisms
Mechanism | Parameter | Definition/Values | Suggested Simulation Values
Power save mode (PSM) | Beacon Interval (BI) | 100 TU | 100 TU
 | DTIM | Integer in unit of BI | { 1, 3 }
 | PSM timeout [5] | Length of time before STA goes to sleep | { 50, 100, 200 } ms
Power save polling (PSP) | Beacon Interval | 100 TU | 100 TU
 | DTIM | Integer in unit of BI | { 1, 3 }
Unscheduled automatic power save delivery (U-APSD) | Beacon Interval | 100 TU | 100 TU
 | DTIM | Integer in unit of BI | { 1, 3 }
 | Max SP Length | Indicate the maximum number of buffered MSDUs, A-MSDUs, and MMPDUs that AP may deliver per SP | { 2, 4, 6, ∞ }
 | AC | Access Category | { VI, VO, BE, BK }

## Slide 5: Example of PSM Operation
AP buffers this frame since this STA is in power save mode
AP
STA
ACK
Beacon
A-MPDU
STA starts CCA for QOS frame with PM=0
DATA
AP starts CCA
BA
STA return to Doze, and AP resumes buffering traffic for this STA
STA exits power save mode and is Awake for Beacon, i.e. DtimCount=0
PM=0
PM=0
A-MPDU
BA
AP is aware STA is out of PM mode, and no longer buffers traffic for this STA
MPDU
ACK
ACK
PM=1
PM=1
PSM Timeout
STA starts CCA
DtimCount=0

## Slide 6: Example of PSP Operation
AP buffers this frame since this STA is in power save mode
AP
STA
ACK
PS-Poll
Beacon
MPDU
Beacon
STA starts CCA for PS-Poll
DATA
AP starts CCA for downlink one MPDU
ACK
Since DTIM=3, STA continues in Doze state during this Beacon
STA exits power save mode and is Awake for Beacon, i.e. DtimCount=0
STA return to Doze, and AP resumes buffering traffic for this STA
DtimCount=0
DtimCount=2

## Slide 7: Example of U-APSD Operation
AP buffers this frame since this STA is in power save mode
AP
STA
Beacon
A-MPDU
STA starts CCA for trigger frame, i.e. QoS (Null) frame
DATA
BA
STA return to Doze, and AP resumes buffering traffic for this STA
STA exits power save mode and is Awake for Beacon, i.e. DtimCount=0
AP is aware STA is Awake, starts CCA, and send frames to STA until there are no more data frames for this AC or AP has reached Max SP Length
A-MPDU
BA
EOSP=1
Service Period
MPDU
ACK
Beacon
EOSP=0
DtimCount=0
DtimCount=2

## Slide 8: Calibration Test for MAC Simulator
Goal
  This test case is intended to verify the baseline power save mechanism implemented in MAC system simulator
Assumptions
  PER = 0
Common Parameters
  Long GI, 11ac preamble, 20MHz
  Aggregation A-MPDU
  Fixed MCS
  Transport protocol: UDP
  EDCA parameters: BE (CWmin = 15), VI (CWmin = 7)
AP
STA
Power Save Test Parameters
  Traffic model: Voice (40% UL, 40% DL, 20% idle) and full buffer web-browsing
  MSDU length: [120 bytes (assuming 24 kbps codec, once every 40 ms), 1500 bytes ]
  RTS/CTS [ OFF ]
  MCS = [ 0 ]
  Power model = [ PSM, PSP, U-APSD ]
  DTIM = [ 3 ]
  Max SP Length = [ 4 ]
  PSM timeout = [ 100 ] ms
Output
  MAC throughput
  Per STA energy per TX bit
  Per STA energy per RX bit
  Pie chart (breakdown) of time spent in each power state [1] during the course of the simulation

## Slide 9: Conclusion
This contribution discusses parameters associated to each baseline power save mechanism, and proposed a MAC simulator calibration test for each power save mechanism

## Slide 10: Straw Poll 1
Do you agree to define parameters associated with each power save mechanism to the simulation scenario document (11-14/980r2)?
  Yes
  No
  Abstain

## Slide 11: Straw Poll 2
Do you agree to add a test for power save mechanisms to the simulation scenario document (11-14/980r2) in the “Scenarios for calibration of MAC simulator” section?
  Yes
  No
  Abstain

## Slide 12: References
E. Wong et al, “Energy Efficiency Evaluation Methodology,” IEEE 11-14-827r3
IEEE 802.11-2012
S. Merlin et al, “TGax Simulation Scenarios,” IEEE 11-14-980r2
R. Porat et al, “11ax Evaluation Methodology,” IEEE 11-14-571r2
Y. Xiao et al, “Modeling Energy Consumption of Data Transmission over Wi-Fi,” IEEE Transactions on Mobile Computing, 2014