## Slide 1: Energy Efficiency Evaluation Methodology Follow Up
Date: 2014-09-15
Authors:

## Slide 2: Outline
Energy efficiency evaluation recap
Feedback and discussions
Conclusion

## Slide 3: Energy Efficiency Evaluation Recap
The previous contribution (11-14/827r3) proposes a systems approach (covering both PHY and MAC) to evaluate energy efficiency for 802.11ax; this is similar to how throughput performance is evaluated for previous 802.11 amendments
Change the simulation scenario [2] and evaluation methodology [3] documents as follows:
  Add definitions for energy efficiency metrics in Slide 4 of [1]
  Add power tables in Slides 18-19 of [1]
  Adopt 3 baseline power save mechanisms, i.e.
    Power save mode (PSM)
    Power save polling (PSP)
    Unscheduled automatic power save delivery (U-APSD)
  Add power save mechanism to each simulation scenario (and associated traffic models)
Incorporate proposed power model to the evaluation methodology document
  Add definition for Energy Efficiency Rating

## Slide 4: Energy Efficiency Rating
According to the PAR, the 802.11ax protocol should meet the following 3 requirements
  4 times average Per-STA throughput improvement [1]
  Transmission latency constraints requirements (TBD; see [3])
  Maintain or reduce energy per successful information bit, i.e. energy efficiency rating of at least one or less
To verify the 3rd requirement, we propose to use Energy Efficiency Rating
  Energy Efficiency Rating is defined as the ratio of average energy consumed for one bit of data successfully exchanged between STAs using any new proposed power save mechanism over the baseline power save mechanism, i.e.
  Average energy per bit is calculated based on the same time interval used for computing average throughput
Proposed power save mechanisms should have an EER ≤ 1

## Slide 5: Feedback and Discussions
Is every “complete proposal” subjected to power save requirement?
  Yes, there has to be at least one mode that clearly demonstrate power save of EER ≤ 1
  Partial proposals are not subjected to this
Is power save calibration across different system simulators required?
  For simulators that implement one or more of the existing power save mechanisms, a basic power save calibration is recommended
  Suggested power save calibration scenarios are going to be defined in [4]
How are the different power save mechanisms mapped into scenarios and traffic models? (Slide 11 of [1])
  We suggest to use a basic set of three baseline power save mechanisms (i.e. PSM, PSP and U-APSD) for all simulation scenarios
  We are suggesting a power save mechanism for each scenario and associated traffic model; for a given simulation there can be flexibility in the mapping of the power save mechanism to the traffic model – as long as it is stated which is used

## Slide 6: Conclusion
This a follow up contribution to energy efficiency evaluation methodology 11-14/827r3 that provides
  An update on the Energy Efficiency Rating
  Discussed feedback received from 11-14/827r3

## Slide 7: Straw Poll 1.1
Do you agree, in principle, to add metrics corresponding to energy efficiency to the evaluation methodology document (11-14/571r3)?
  Yes
  No
  Abstain

## Slide 8: Straw Poll 1.2
Do you support adding the following definition for Energy Efficiency Ratio (EER) to the evaluation methodology document (11-14/571r3)?
  Energy efficiency ratio is defined as the ratio of average energy consumed for one bit of data successfully exchanged between STAs using any new proposed power save mechanism over the baseline power save mechanism
  Yes
  No
  Abstain

## Slide 9: Straw Poll 1.3
Do you support adding these metrics to the evaluation methodology document (11-14/571r3)?
  Yes
  No
  Abstain
Metric | Units | Definition
Per-STA energy per TX bit | Joules/bit | Total energy consumed by a STA divided by the total number of successful data bits transmitted by the STA
Per-STA energy per RX bit | Joules/bit | Total energy consumed by a STA divided by the total number of successful data bits received by the STA

## Slide 10: Straw Poll 2.1
Do you support adding standardized power tables for purposes of computing energy consumption to the simulation scenario document (11-14/980r2)?
  Yes
  No
  Abstain

## Slide 11: Straw Poll 2.2
Do you support adding the following power table (whose entries are TBD) to the simulation scenario document (11-14/980r2)?
  Yes
  No
  Abstain
Power State | Average Power Consumption (mW) Bandwidth = { 20 MHz }, Band = { 2.4 GHz, 5 GHz }, NSS = { 1 }, Number of TX/RX antennas = { 1 }, TX power per antenna = { 15 dBm }
Transmit | 
Receive | 
Listen | 
Sleep | 

## Slide 12: Straw Poll 2.3
Do you support adding the following power transition table (whose entries are TBD) to the simulation scenario document (11-14/980r2)?
  Yes
  No
  Abstain
State Transitions | Transition Time (ms) | Average Power Consumption (mW)
Transmit ⬄ Listen | 0 | 0
Receive ⬄ Listen | 0 | 0
Receive➭ Transmit | TRT (e.g. SIFS of 16us) | PRT
Transmit ➭ Sleep | TTS | PTS
Receive ➭ Sleep | TRS | PRS
Listen ⬄ Sleep | TLS | PLS

## Slide 13: Straw Poll 3.1
Do you support adding a baseline power save mechanism to each scenario and associated traffic modes, in reference traffic profile in Annex 1 to the simulation scenario document (11-14/980r2)?
  Yes
  No
  Abstain

## Slide 14: Straw Poll 3.2
The baseline power save mechanism may include one of the following 3 power save mechanisms defined in [4]?
  Power save mode (PSM)
  Power save polling (PSP)
  Unscheduled automatic power save delivery (U-APSD)
  Yes
  No
  Abstain

## Slide 15: References
E. Wong et al, “Energy Efficiency Evaluation Methodology,” IEEE 11-14-827r3
S. Merlin et al, “TGax Simulation Scenarios,” IEEE 11-14-980r2
R. Porat et al, “11ax Evaluation Methodology,” IEEE 11-14-571r2
E. Wong et al, “Parameters on Power Save Mechanisms,” IEEE 11-14-1161r0