## Slide 1: TGax Functional Requirement Discussion
Date: 2014-09
Authors:
Name | Affiliation | Address | Email
Yonggang Fang | ZTE |  | yfang@ztetx.com
Bo Sun | ZTE |  | sun.bo1@zte.com.cn
Ke Yao | ZTE |  | ke.yao@zte.com.cn
Kaiying Lv | ZTE |  | lv.kaiying@zte.com.cn
Zhendong Luo | CATR |  | luozhendong@catr.cn
Meng Yang | CATR |  | yangmeng1@catr.cn
Jiadong Du | CATR |  | dujiadong@catr.cn

## Slide 2: Background
TGax PAR [1] and CSD [2] have defined the scope of amendment of 802.11, focusing on
  WLAN deployments with dense stations and dense access points where interference from neighboring devices is an issue affecting the perceived user experience.
  Improving system level performance and utilization of the spectrum resources as well as interference mitigation and management between neighboring OBSS.
The contribution discusses functional requirements of TGax amendment based on TGax scopes.

## Slide 3: Efficiency Requirement Discussion (1)
Efficiency Improvement in PAR
  TGax is the amendment of IEEE 802.11 mainly for High Efficiency WLAN:
    Operating in 2.4 GHz and 5 GHz frequency bands
    In indoor and outdoor dense deployment scenario
    Working environment like
      wireless corporate office, outdoor hotspot, dense residential apartments, and stadiums.
  TGax PAR [1] requires to
    make more efficient use of spectrum resources in scenarios with a high density of STAs per BSS.
    significantly increase spectral frequency reuse and manage interference between neighboring overlapping BSS (OBSS) in scenarios with a high density of both STAs and BSSs.

## Slide 4: Efficiency Requirement Discussion (2)
Efficiency Issues
  MAC Efficiency issue
    WLAN is expected to deploy in the high dense environment, like hotspots, stadium, offices, conference rooms etc.
    Contributions [3] [4] [5] pointed out that the current MAC of 802.11 is not efficient for the high dense deployment. When the density of STAs reaches a certain level, the collision possibility of using current EDCA mechanism for medium access is very high. In such high dense deployment cases, most of medium time would be wasted for control and management frames or re-transmission due to collisions.
    [6] indicated that the current 802.11 MAC is not efficient to handle short frame transmission.
  Spectral Efficiency
    The current primary and secondary channel assessment mechanism is not permitted to fully use of available channel bandwidth and causes the waste of spectrum.

## Slide 5: Efficiency Requirement Discussion (3)
Efficiency Definitions
  Wikipedia (http://en.wikipedia.org/wiki/Spectral_efficiency) defines :
    “The spectrum efficiency refers to the information rate that can be transmitted over a given bandwidth in a specific communication system. It is a measure of how efficiently a limited frequency spectrum is utilized by the physical layer protocol, and sometimes by the media access control (the channel access protocol).”
  The spectrum efficiency includes
    the link spectrum efficiency, measured in (bit/s)/Hz;
      It is the net bit rate or maximum throughput divided by the bandwidth in hertz of a communication channel or a data link.
    system spectrum efficiency or area spectrum efficiency measured in (bit/s)/Hz per unit area or cell.
      That is based on the link spectrum efficiency and considering interference from neighbor cells and frequency reuse factor.

## Slide 6: Efficiency Requirement Discussion (4)
Proposed Efficiency Requirement in FRD
  The 802.11ax amendment shall provide a mechanism to improve spectral efficiency including the link spectrum efficiency and system spectrum efficiency, in scenarios of high density deployment of 802.11ax STAs with and without the presence of legacy STAs.

## Slide 7: Packet Delay Requirement Discussion (1)
Packet Delay in PAR
  In TGax PAR [1], it clearly mentions that this amendment is different from the previous versions of amendment which focused on improving aggregated throughput.
  Instead, TGax is to focus on improving user experience such as the average per-STA throughput and 5th percentile of the per station throughput distribution in a given area, along with the satisfaction of the packet delay and the packet error ratio (PER) requirements of applications.
  The user experience could be measured in following aspects:
    Average per-STA throughput
    Transmission latency which is especially important to real-time applications, like gaming, video streaming, etc.
    PER

## Slide 8: Packet Delay Requirement Discussion (2)
Proposed Latency Requirement in FRD
  TGAx Rn: The 802.11ax amendment shall quantify and bring latency to a desirable level to meet QoS requirements in high dense deployment scenario. define a mechanism to improve the average transmission latency, compared to the existing IEEE 802.11 standard and its amendments operating in the same dense deployment scenario.

## Slide 9: Robustness Requirement Discussion (1)
Robustness in PAR
  TGax PAR [1] requires to increase robustness in outdoor propagation environments and uplink transmissions.
  This PAR amendment requirement indicates the issue of successful transmission ratio due to loss of packets and would like to reduce the number of retransmissions especially in the dense deployment scenario.
  Improving transmission robustness will in turn to help improving the efficiency and saving battery power.

## Slide 10: Robustness Requirement Discussion (2)
Proposed Robustness Requirement in FRD
  TGAx Rn: The 802.11ax amendment shall bring PER to a desirable level to make the link robust in high dense deployment scenario. increase the probability of successful frame transmissions (i.e. reduce packet error rate (PER), compared to the existing IEEE 802.11 standard and its amendments operating in the same dense deployment scenarios

## Slide 11: Straw Polls
SP1: Do you support to add the efficiency requirement in page 6 to the FRD?
  Yes/No/Abstain
SP2: Do you support to add the latency requirement in page 8 to FRD?
  Yes/No/Abstain
SP3: Do you support to add the robustness requirement of page 10 to the FRD?
  Yes/No/Abstain

## Slide 12: Motion-1
Move to add the following text to the TGax Functional Requirement document 11-14-1009-01-00ax-proposed-802-11ax-functional-requirements:
2.x Latency Requirements
  TGAx Rn: The 802.11ax amendment shall quantify and bring latency to a desirable level to meet QoS requirements in high dense deployment scenario.
  Move: Second:
  Yes/No/Abstain

## Slide 13: Motion-2
Move to add the following text to the TGax Functional Requirement document 11-14-1009-01-00ax-proposed-802-11ax-functional-requirements :
2.x Robustness Requirements
  TGAx Rn: The 802.11ax amendment shall bring PER to a desirable level to make the link robust in high dense deployment scenario.
  Move: Second:
  Yes/No/Abstain

## Slide 14: References
11-14-0165-01-0hew-802-11-hew-sg-proposed-par
11-14-0169-01-0hew-ieee-802-11-hew-sg-proposed-csd
11-13-0505-00-0hew-mac-efficiecy-analysis-for-hew-sg
11-11-1512-04-00ah-mac-considerations-for-802-11ah
Hai. Vu and Taka Sakurai, “Collision Probability in Saturated IEEE 802.11 Networks”; http://caia.swin.edu.au/pubs/ATNAC06/Vum.pdf
11-14-0855-00-00ax-techniques-for-short-downlink-frames