## Slide 1: DL-FDMA considerations
Date: 2014-09-12
Authors:

## Slide 2: Abstract
This contribution considered Down Link FDMA (DL-FDMA) as a candidate technique for access efficiency improvement for 11ax.

## Slide 3: Conceptions
AP
  20MHzBW * 4CH frequency division multiplex transmission (in case of 80MHzBW totally)
  Up to 4 data streams to 4 STAs are available
  4 concurrent ACKs on different 4 * 20MHz CH
STAs
  Data streams on 4 channels will be received and demodulated in parallel
  Target data streams are recognized by destination address in MAC header
  STA will reply ACK using channels which included the data stream to the STA

## Slide 4: Figure of Conceptions DL-FDMA: AP  4 STAs
t
t
t
t
AP
STA-1
AP
STA-2
AP
STA-3
AP
STA-4
CCA
DIFS
+ CW
CCA
CCA
CCA
Data to STA-1
Data to STA-2
Data to STA-3
Data to STA-4
ACK
ACK
ACK
ACK
SIFS
CH36
CH40
CH44
CH48
Ex.

## Slide 5: Sequence by the current standards
AP
STA1
STA2
STA3
STA4
DIFS
+CW
SIFS
ACK
DIFS
+CW
SIFS
DIFS
+CW
SIFS
DIFS
+CW
SIFS
Medium time for a set of data deliveries to 4 STAs
ACK
ACK
ACK
Data
Data
Data
Data

## Slide 6: Sequence by this proposal (DL-FDMA)
AP
STA1
STA2
STA3
STA4
DIFS
+CW
SIFS
ACK
Simultaneous 4 ACKs are responded on different 4 frequency channels.
Medium time for a set of data deliveries to 4 STAs
Data1
Data2
Data3
Data4
ACK
ACK
ACK

## Slide 7: Medium Time Comparison (Data delivery to 4 STAs)
Medium Time (us)
MPDU size (byte)
Chart: 
| 0.0 | 100.0 | 200.0 | 300.0 | 400.0 | 500.0 | 600.0 | 700.0 | 800.0 | 900.0 | 1000.0 | 1100.0 | 1200.0 | 1300.0 | 1400.0 | 1500.0
11ac@MCS0 (80MHz) | 932 | 1028 | 1140 | 1252 | 1364 | 1476 | 1588 | 1684 | 1796 | 1908 | 2020 | 2132 | 2244 | 2340 | 2452
11ac@MCS8 (80MHz) | 804 | 820 | 820 | 836 | 836 | 852 | 868 | 868 | 884 | 884 | 900 | 900 | 916 | 916 | 932
Proposal@MCS0 (20MHz*4) | 345 | 469 | 593 | 713 | 837 | 961 | 1085 | 1205 | 1329 | 1453 | 1577 | 1701 | 1821 | 1945 | 2069
Proposal@MCS8 (20MHz*4) | 209 | 221 | 229 | 241 | 249 | 261 | 273 | 281 | 293 | 301 | 313 | 321 | 333 | 341 | 353
MPDU size (byte) | 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500
11ac@MCS0 (80MHz) |  | 932 | 1028 | 1140 | 1252 | 1364 | 1476 | 1588 | 1684 | 1796 | 1908 | 2020 | 2132 | 2244 | 2340 | 2452
11ac@MCS8 (80MHz) |  | 804 | 820 | 820 | 836 | 836 | 852 | 868 | 868 | 884 | 884 | 900 | 900 | 916 | 916 | 932
Proposal@MCS0 (20MHz*4) |  | 345 | 469 | 593 | 713 | 837 | 961 | 1085 | 1205 | 1329 | 1453 | 1577 | 1701 | 1821 | 1945 | 2069
Proposal@MCS8 (20MHz*4) |  | 209 | 221 | 229 | 241 | 249 | 261 | 273 | 281 | 293 | 301 | 313 | 321 | 333 | 341 | 353
Medium time usage is reduced.
Refer to Slide-12 for details.

## Slide 8: DL Throughput per a STA without considerations on upper layer protocols
Chart: 
| 0.0 | 100.0 | 200.0 | 300.0 | 400.0 | 500.0 | 600.0 | 700.0 | 800.0 | 900.0 | 1000.0 | 1100.0 | 1200.0 | 1300.0 | 1400.0 | 1500.0
11ac@MCS0 (80MHz) | 0.85837 | 1.5564 | 2.1053 | 2.5559 | 2.9326 | 3.252 | 3.5264 | 3.8005 | 4.0089 | 4.1929 | 4.3564 | 4.5028 | 4.6346 | 4.7863 | 4.894
11ac@MCS8 (80MHz) | 0.99502 | 1.9512 | 2.9268 | 3.8278 | 4.7847 | 5.6338 | 6.4516 | 7.3733 | 8.1448 | 9.0498 | 9.7778 | 10.6667 | 11.3537 | 12.2271 | 12.8755
Proposal@MCS0 (20MHz*4) | 2.3188 | 3.4115 | 4.0472 | 4.4881 | 4.779 | 4.9948 | 5.1613 | 5.3112 | 5.4176 | 5.5058 | 5.5802 | 5.6437 | 5.7111 | 5.7584 | 5.7999
Proposal@MCS8 (20MHz*4) | 3.8278 | 7.2398 | 10.4803 | 13.278 | 16.0643 | 18.3908 | 20.5128 | 22.7758 | 24.5734 | 26.5781 | 28.115 | 29.9065 | 31.2312 | 32.8446 | 33.9943
Throughput (Mbps)
MPDU size (byte)
MPDU size (byte) | 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500
11ac@MCS0 (80MHz) |  | 0.86 | 1.56 | 2.11 | 2.56 | 2.93 | 3.25 | 3.53 | 3.80 | 4.01 | 4.19 | 4.36 | 4.50 | 4.63 | 4.79 | 4.89
11ac@MCS8 (80MHz) |  | 1.00 | 1.95 | 2.93 | 3.83 | 4.78 | 5.63 | 6.45 | 7.37 | 8.14 | 9.05 | 9.78 | 10.67 | 11.35 | 12.23 | 12.88
Proposal@MCS0 (20MHz*4) |  | 2.32 | 3.41 | 4.05 | 4.49 | 4.78 | 4.99 | 5.16 | 5.31 | 5.42 | 5.51 | 5.58 | 5.64 | 5.71 | 5.76 | 5.80
Proposal@MCS8 (20MHz*4) |  | 3.83 | 7.24 | 10.48 | 13.28 | 16.06 | 18.39 | 20.51 | 22.78 | 24.57 | 26.58 | 28.12 | 29.91 | 31.23 | 32.84 | 33.99

## Slide 9: Available Bandwidth
11ac
(80M*1)
Interference
FDMA
(20M*4)
FDMA may also have some advantages on available bandwidth in densely deployed environment.
36
40
44
48
CH
Primary 20M
Secondary 20M
Secondary 40M
80MHz
36
40
44
48
Primary 20M
Secondary 20M
40MHz
36
40
44
48
Primary 20M
20MHz
36
40
44
48
0MHz
36
40
44
48
CH
80MHz
36
40
44
48
60MHz
36
40
44
48
60MHz
36
40
44
48
60MHz

## Slide 10: Mixed Operation with Legacy STAs
FDMA
(20M*4)
This FDMA concept may be applicable for mixed operation with legacy STAs. The primary 20MHz channel would be used for a legacy STA on a priority basis and other channels for 11ax supported STAs. It might improve access efficiency of legacy STAs too.
36
40
44
48
CH
Primary 20M
for a legacy STA
for 11ax STAs

## Slide 11: Summary
FDMA may have some advantages in access efficiency on:
  Less medium time,
  Shorter latency,
  Wider available bandwidth in dense environment,
  Mixed operation with legacy STAs
Detailed considerations is needed for feasibility study.

## Slide 12: Straw poll
Do you support to study DL-FDMA as a possible technique for efficiency improvement for 11ax?
Y/N/A =

## Slide 13: Backup Medium Time of Frames
L-STF
L-LTF
L-SIG
VHT-SIG-A
VHT-
STF
VHT-
LTF
VHT-
SIG-B
Data
8us
8us
8us
4us
4us
4us
4us
40us
Data Frame [us]
40 + {(Service + MPDU + PHY pad + Tail) / NDBPS}* 4
= 40 + roundup{(16 + MPDU[byte]*8 + 6) / NDBPS}* 4
NDBPS: the number of data bits per OFDM symbol
ACK Frame [us]
40 + {(Service + MPDU(ACK frame) + PHY pad + Tail) / NDBPS}* 4
= 40 + roundup{(16 + 14*8 + 6) / NDBPS}* 4
MPDU includes MAC header (26 bytes).

## Slide 14: References
[1] Brian Hart et al, IEEE 11-14/855r0, “Techniques for Short Downlink Frames”