## Slide 1: DSC Simulation Results for Scenario 3
Date: 2014/9/15
Authors:

## Slide 2: Abstract
Performance improvement and impact on legacy STA of Dynamic Sensitivity Control (DSC) techniques are evaluated under Simulation Scenario 3
Condition to effectively obtain the DSC gain is also analyzed
  Some additional techniques to avoid loss of Rx opportunity should be used

## Slide 3: Introduction
Dynamic Sensitivity Control (DSC) is an attractive candidates against OBSS interference
Some contributions have shown the improvement and/or the impact to the performance of Legacy STA when DSC techniques are used [1-16]
We have also presented some results in very simplified scenario (2-cell, AMPDU disabled) [17]
In this contribution, simulation results are presented for defined sim. scenario 3 (19-cell, A-MPDU enabled)
  And also effects of some additional feature are evaluated
    DSC at recipient STA
      If DSC is used by only a transmitting STA and the recipient STA don’t use the DSC, how does it affect to gain?

## Slide 4: Simulation Conditions
Chart: 
| 10 | 5 | -5 | -10 | -5 | 5 | 10
BSS0 | 0 | 8.66 | 8.66 | 0 | -8.66 | -8.66 | 0
BSS1 | 0 | 8.66 | 8.66 | 0 | -8.66 | -8.66 | 0
BSS2 | 25.98 | 34.64 | 34.64 | 25.98 | 17.32 | 17.32 | 25.98
BSS3 | 25.98 | 34.64 | 34.64 | 25.98 | 17.32 | 17.32 | 25.98
BSS4 | 0 | 8.66 | 8.66 | 0 | -8.66 | -8.66 | 0
BSS5 | -25.98 | -34.64 | -34.64 | -25.98 | -17.32 | -17.32 | -25.98
BSS6 | -25.98 | -34.64 | -34.64 | -25.98 | -17.32 | -17.32 | -25.98
 | 0 | 8.66 | 8.66 | 0 | -8.66 | -8.66 | 0
 | 25.98 | 34.64 | 34.64 | 25.98 | 17.32 | 17.32 | 25.98
 | 51.96 | 60.62 | 60.62 | 51.96 | 43.3 | 43.3 | 51.96
 | 51.96 | 60.62 | 60.62 | 51.96 | 43.3 | 43.3 | 51.96
 | 51.96 | 60.62 | 60.62 | 51.96 | 43.3 | 43.3 | 51.96
Scenario-3
  19-cell model with wrap-around (R=10m, Reuse=3)
Traffic model
  10 uplink UDP Flows/BSS (Full-buffer condition)
  No downlink traffic
MCS selection
  Goodput maximizing MCS based on SINR by training[18]
Sensitivity control algorithm
  Beacon RSSI based algorithm[1]
Parameters
  Preamble detection threshold
    -82dBm ~ -52dBm
See backup slide for details
ICD=30m
R
[NOTE] Definitions in this material
“Preamble detection threshold” means
Min level to be “CCA=busy” for 802.11 signals. (aka Rx sensitivity level)
“CCA threshold” means
Min level to be “CCA=busy” for any signals. (-82dBm + 20dB)

## Slide 5: Adopted DSC Algorithm
STA
  Beacon RSSI based algorithm
    Simplified algorithm of DSPG’s contribution [1]
    Toggle ON/OFF based on RSSI of most recent received Beacon from associated AP
    Compare the RSSI with “Trigger Threshold” and if exceed the threshold, toggle DSC to ON. Otherwise toggle DSC to OFF
      In this time Trigger Threshold is set to -41dBm
    Preamble detection threshold during DSC-OFF is fixed to -82dBm
    Preamble detection threshold during DSC-ON is a parameter (A dbm)
    CCA threshold is always -62dBm
AP
  Fixed
    AP’s preamble detection threshold is always set to A dBm.
    CCA threshold is always -62dBm
DSC=ON
STA
AP
Beacon
Beacon
DSC=OFF
Beacon
Beacon
-40dBm
-50dBm
-38dBm
DSC=ON
time
-40dBm

## Slide 6: Simulation Results (Scenario3)
BSS Total
per STA
CDF 5%
94%
Down
-System gain was confirmed in Scenario 3
-Degradation of Legacy STAs was also confirmed
per STA
Ave.
38%
Down
36%
Up
[NOTE] 11ax STA CDF5% TP is also degraded.
This can be due to algorithm of DSC. (See slide#5)
DSC of 11ax STA isn’t always enabled and
they behave as Legacy STA during DSC is disabled.

## Slide 7: Impact of DSC at Recipient STA
DSC has two aspects
  One is increasing opportunity of Tx
  Another one is avoiding undesired weak packet and increasing chance to Rx a stronger desired packet
If DSC is used by only transmitting STA of packets, system gain may be small
w/o DSC
at Recipient STA
Rx Interference Packet
Tx to AP
Detect ->
start Rx
Not detect due to DSC ->
can transmit simultaneously
ｘ
AP
(Recipient STA)
STA
(Transmitting STA)
Interference Packet from OBSS
Interference Packet from OBSS
Tx to AP
Rx desired Packet
Not detect due to DSC ->
can wait stronger packet
Cannot receive no matter how large the SINR is !
time
time
time
time
Not detect due to DSC ->
can transmit simultaneously
w/ DSC
at Recipient STA
AP
(Recipient STA)
STA
(Transmitting STA)

## Slide 8: Simulation Results (If Recipient STA does not use DSC)
BSS Total
per STA
Ave.
per STA
CDF 5%
42%
Down
-If DSC is used by only the transmitting STA and the Recipient STA (i.e. AP in this case) don’t use DSC, there is small system gain
(ref) Both 11axSTAs/AP uses DSC
- Scenario 3
- 10 Uplink Flows/BSS
- No Downlink Flow
- 8KB AMPDU
- No RTS
- AP doesn’t use DSC
(36%
Up)
(38%
Down)
24%
Down
6%
Up
(ref) Both 11axSTAs/AP uses DSC

## Slide 9: Summary
System gain and the impact for legacy devices of DSC are confirmed in Scenario 3
Some additional techniques to avoid loss of Rx opportunity should be used together to effectively obtain the DSC gain
  For example;
    Using DSC at recipient STA together
    Switching/overriding receiving packet when a stronger packet comes during reception

## Slide 10: Backup

## Slide 11: Simulation Results (AMPDU vs no-AMPDU)
BSS Total
per STA
CDF 5%
-When AMPDU isn’t used, the system gain of DSC is more than AMPDU enabled case.
-The impact for Legacy STA is also more than AMPDU case.
- Scenario 3
- 10 Uplink Flows/BSS
- No Downlink Flow
- No RTS
- No AMPDU
99%
Down
per STA
Ave.
(ref) 8KB AMPDU case
(ref) 8KB AMPDU case
(36%
Up)
(38%
Down)
148%
Up
87%
Down

## Slide 12: Simulation Setup details
Node | (AP x 1, STA x 10) x 19
Num of Drops [times] | 5
Traffic Model & Load | Uplink CBR UDP 30Mbps (from all STA -> Full Buffer condition)
Traffic Duration [sec] | 20
Access Category | AC_BE CWmin=15, CWmax=1023, AIFSN=3, TXOP limit=0
Tx Power [dBm] | AP:+20dBm(2 antennas), STA:+15dBm(1 antenna)
MCS Selection | Goodput maximizing MCS based on Training result (MCS0 ~ MCS7)
Packet Length [byte] | (MPDU, MSDU, APP)=(1030, 1000, 972) Fixed
L2 Retry | 10
Ack Rate | MCS0
RTS/CTS | Parameter (OFF)
Max Aggregation Size | (A-MPDU, A-MSDU)=(0 or 8KB, NA)
NF [dB] | 7
Channel | TGn Channel D (pathloss, shadowing, fading)
Preamble Detect Th. [dBm] | Parameter (-82 ~ -52: on 11ax-STAs & APs , -82 on Legacy-STAs)
CCA Th [dBm] | -62 (Fixed)
Channel Setting [MHz] | (CenterFreq, BW)=(2412, 20)
Det. Cancel on PLCP err | Enable
DSC algorithm | See slide #5
[NOTE] Definitions in this material
“Preamble detection threshold” means
Min level to be “CCA=busy” for 802.11 signals. (aka Rx sensitivity level)
“CCA threshold” means
Min level to be “CCA=busy” for any signals. (-82dBm + 20dB)

## Slide 13: Impact of RTS/CTS to DSC gain
Any difference on gain when it is enabled?
General effect of RTS/CTS protection
  (Pro) Reduce the probability of collision and reduce the wasted time of retransmit PPDU
    If PPDUs are longer, the benefit become larger
  (Con) Increase the overhead of frame exchange
  (Con) Sometimes force to honor NAV unnecessarily at many STAs in dense environment
DSC should reduce C), so it is expected that the performance can be improved

## Slide 14: Simulation Results (no-RTS vs RTS)
per STA
CDF 5%
98%
Down
(ref) no RTS case
-When RTS is used with DSC, the system gain is more remarkable than no-RTS case.
-But the absolute value of Tput never exceeded the no-RTS case.
BSS Total
- Scenario 3
- 10 Uplink Flows/BSS
- No Downlink Flow
- 8KB AMPDU
- with RTS
per STA
Ave.
(ref) no RTS case
(36%
Up)
(38%
Down)
44%
Down
231%
Up

## Slide 15: Consideration of DSC+RTS Sim. Result
General effect of RTS/CTS protection (again)
  (Pro) Reduce the probability of collision and reduce the wasted time of retransmit PPDU
    If PPDUs are longer, the benefit become larger
  (Con) Increase the overhead of frame exchange
  (Con) Sometimes force to honor NAV unnecessarily at many STAs in dense environment
The result was worse than no-RTS case
  In scenario-3 condition, the degradation of C) may outstrip the improvement of A) even if DSC is used

## Slide 16: References
Graham Smith, DSP Group, 11-13-1290-01 Dynamic Sensitivity Control for HEW
Graham Smith, DSP Group, 11-13-1487-02 Dense Apartment Complex Capacity Improvements with Channel selection and Dynamic Sensitivity Control
Graham Smith, DSP Group, 11-13-1489-05 Airport Capacity Analysis
Graham Smith, DSP Group, 11-14-0045-02 E-Education Analysis
Graham Smith, DSP Group, 11-14-0058-01 Pico Cell Use Case Analysis
Ron Porat, Broadcom, 11-14-0082-00 Improved Spatial Reuse Feasibility - Part I
Nihar Jindal, Broadcom, 11-14-0083-00 Improved Spatial Reuse Feasibility - Part II
Graham Smith, DSP Group, 11-14-0294-02 Dynamic Sensitivity Control Channel Selection and Legacy Sharing
Graham Smith, DSP Group, 11-14-0328-02 Dense Apartment Complex Throughput Calculations
Jinjing Jiang, Marvell, 11-14-0372-00 System level simulations on increased spatial reuse
Imad Jamil, Orange, 11-14-0523-00 Mac Simulation Results for DSC and TPC
Frank LaSita, InterDigital, 11-14-0578-00 Residential Scenario CCA/TPC Simulation Discussion
John Son, WILUS Institue/SK Telecom, 11-14-0628-00 Measurements on CCA Thresholds in OBSS Environment
Graham Smith, DSP Group, 11-14-0365-01 Dynamic Sensitivity Control Implementation
James Wang, MediaTek, 11-14-0637-00 Spatial Reuse and Coexistence with Legacy Devices
Graham Smith, DSP Group, 11-14-0779-00 Dynamic Sensitivity Control Practical Usage
William Carney, Sony, 11-14-0854-00 DSC and Legacy Coexistence
Gwen Barriac, Qualcomm, 11-14-0851-02-00ax-rate-control-for-mac-and-integrated-system-simulations