## Slide 1: Considerations for Partial Band Interference between WLAN Systems
Date: 2014-09-10
Authors:

## Slide 2: Abstract
In the OBSS area, WLAN throughput decrease depending on number of overlapped BSS due to the time sharing policy between WLAN systems.
There are two types of interferers between overlapped BSSs. One is full band interference from neighbor BSSs. Another is partial band interference.
In this presentation, we will discuss both partial band interference problems and possible solution.

## Slide 3: Introduction
Full band interference
  When two or more devices’ operation band are fully overlapped. This type of interference is called by Full band interference each others
  Both center frequency and bandwidth are exactly same
Partial band interference
  When two or more devices’ operation band are partially overlapped. This type of interference is called by Partial band interference each others
  Both center frequency and bandwidth are NOT exactly same

## Slide 4: Introduction
Full band vs Partial band interference example in 2.4GHz band

## Slide 5
Bandwidth Overlap Problems
Because of time sharing policy for coexistence between BSSs called CSMA/CA, bandwidth overlap yields performance degradation.
This performance degradation is an expected problem since WLAN was born.
However, this simple coexistence protocol is a good solution for bandwidth overlap between BSSs.
Solution of this problem will be supported by Functional Requirement of IEEE 802.11ax(TGax R7)[1]
  The 802.11ax amendment shall provide a mechanism to facilitate frequency reuse and manage interference between neighboring overlapping BSS (OBSS) in dense deployment scenarios with a high density of STAs per BSS or a high density of both STAs and BSSs

## Slide 6: Difference between Full and Partial Bandwidth Overlap
In full bandwidth overlap case, time division solution is available.
Whereas, in partial bandwidth overlap case, there are some clean frequency bands additionally.
These clean parts of bandwidth are a hiding resource of current WLAN networks.
So, if we can use those clean part of bandwidth, WLAN performance can be improved.

## Slide 7: Characteristics of Fully and Partially Overlapped Bandwidth
Fully overlapped bandwidth
  Possible : both physical layer detection and NAV information
Partially overlapped bandwidth
  Possible : physical layer detection and expected low signal strength
  Hard to decode NAV information
To detect partial overlap bandwidth accurately, we need modification of existing CCA procedure based on signal characteristics of partial overlap cases.

## Slide 8: What about 5GHz?
Similar situation in 5GHz band!

## Slide 9: Possible Solution for Bandwidth Overlap Problem
Non Overlap approach(Level 1)
  Higher Layer or User Management
    Government Guide Line for band selection
    Powerful for 2.4GHz and enterprise devices
  Providing intelligence initial bandwidth selection and updating mechanism
    How often?
    Automatically or User setting?
Overlap approach(Level 2)
  Full band overlap case
    Time Division Access
  Partial band overlap case
    Time and Frequency Division Access  OFDMA

## Slide 10: Summary
  IEEE 802.11ax will support various performance enhancement techniques
  There are unused resource in the frequency domain which is some clean bandwidth under partially overlapped OBSS situation
  Usage of these unused bands provides higher performance in IEEE 802.11ax standard

## Slide 11: References
[1]Lei Wang et. al.,11-14-0567-07-00ax-proposed-tgax-functional-requirements