## Slide 1: MAC calibration results
Date: 2014-09-10
Authors:

## Slide 2: Summary
Contributions [1][2] define the simulation scenarios and evaluation method for MAC system calibration
This contribution provides the MAC calibration results:
  Test 1: MAC overhead test
  Test 2: Deferral test
  Test 3: TXOP test
This contribution also discusses some of the parameter setting in [1] that need clarification for implementing the calibration. (underline Marked)

## Slide 3: Test 1a: MAC overhead w/out RTS/CTS -Simulation Parameter-
AP1
STA 1
AP1
Parameters:
  MSDU length:[0:500:2000Bytes]
  2 MPDU limit
  RTS/CTS off
  Data MCS = [0,8] ( to clarify, run a sweep over MSDU length once for MCS 0, and once for MCS 8.
  ACK MCS = 0
  AIFS=DIFS = 34us

## Slide 4: Test 1a: MAC overhead without RTS/CTS Calibration Results
Without RTS/CTS
Data Rate | Application Packet Size | MSDU Size | Expected Application Throughput | Simulation Application Throughput | Expected MAC Throughput | Simulation MAC Throughput
(MCS) | (Bytes) | (Bytes) | (Mbps) | (Mbps) | (Mbps) | (Mbps)
0 | 464 | 500 | 4.79 | 4.79 | 5.16 | 5.16
0 | 964 | 1000 | 5.55 | 5.55 | 5.76 | 5.76
0 | 1464 | 1500 | 5.84 | 5.84 | 5.99 | 5.99
0 | 1964 | 2000 | 6.00 | 6.00 | 6.11 | 6.10
8 | 464 | 500 | 22.00 | 21.98 | 23.70 | 23.68
8 | 964 | 1000 | 34.94 | 34.91 | 36.24 | 36.22
8 | 1464 | 1500 | 43.26 | 43.24 | 44.32 | 44.30
8 | 1964 | 2000 | 48.68 | 48.67 | 49.57 | 49.56

## Slide 5: Test 1a: MAC overhead without RTS/CTS Calibration Results-time/event trace
Time trace [usec] |  |  | MCS0 1500 bytes
 | –CP1 start of A-MPDU |  | 12174
 | –CP2 end of A-MPDU |  | 15998
 |  | •CP2-CP1 | 3824
 |  | •Expected time gap = A-MPDU duration | 3824
 | –CP3 start of ACK |  | 16014
 |  | •CP3-CP2 | 16
 |  | •Expected time gap = SIFS | 16
 | –CP4 end of ACK |  | 16082
 |  | •CP4-CP3 | 68
 |  | •Expected time gap = ACK duration | 68
 | –CP5 start of A-MPDU |  | 16242
 |  | •CP5-CP4 | 160
 |  | •Expected time gap = Defer&backoff duration | 34+14*9
Test Items | Check points | Standard definition | Matching?
A-MPDU duration | Tcp2-Tcp1= 3824 us | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | OK
SIFS | Tcp3-Tcp2=16 us | 16 us | OK
ACK duration | Tcp4-Tcp3= 68 us | ceil((ACKFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | OK
Defer & backoff duration | Tcp5-Tcp4= 160us | DIFS(34 us)+backoff (CWmin) =34us+14*9us | OK

## Slide 6: Test 1b: MAC overhead w RTS/CTS -Simulation Parameter-
AP1
STA 1
AP1
Assumptions:
  PER is 0
Parameters:
  MSDU length:[0:500:2000Bytes]
  2 MPDU limit
  RTS/CTS on
  Data MCS = [0,8] ( to clarify, run a sweep over MSDU length once for MCS 0, and once for MCS 8.
  ACK MCS = 0
  AIFS=DIFS = 34us

## Slide 7: Test 1b: MAC overhead with RTS/CTS Calibration Results
With RTS/CTS
Data Rate | Application Packet Size | MSDU Size | Expected Application Throughput | Simulation Application Throughput | Expected MAC Throughput | Simulation MAC Throughput
(MCS) | (Bytes) | (Bytes) | (Mbps) | (Mbps) | (Mbps) | (Mbps)
0 | 464 | 500 | 4.43 | 4.42 | 4.77 | 4.77
0 | 964 | 1000 | 5.31 | 5.31 | 5.51 | 5.51
0 | 1464 | 1500 | 5.66 | 5.66 | 5.80 | 5.80
0 | 1964 | 2000 | 5.85 | 5.85 | 5.96 | 5.96
8 | 464 | 500 | 15.95 | 15.94 | 17.19 | 17.17
8 | 964 | 1000 | 27.08 | 27.07 | 28.09 | 28.08
8 | 1464 | 1500 | 34.99 | 34.97 | 35.85 | 35.83
8 | 1964 | 2000 | 40.63 | 40.61 | 41.37 | 41.36

## Slide 8: Test 1b: MAC overhead with RTS/CTS Calibration Results-time/event trace
Time trace [usec] |  |  | MCS0 1500 bytes
 | –CP1 start of RTS |  | 12302
 | –CP2 end of RTS |  | 12354
 |  | •CP2-CP1 | 52
 |  | •Expected time gap = RTS duration | 52
 | –CP3 start of CTS |  | 12370
 | –CP4 end of CTS |  | 12414
 |  | •CP4-CP3 | 44
 |  | •Expected time gap = CTS duration | 44
 | –CP5 start of A-MPDU |  | 12430
 | –CP6 end of A-MPDU |  | 16254
 |  | •CP6-CP5 | 3824
 |  | •Expected time gap = Frame duration | 3824
Test Items | Check points | Standard definition | Matching?
RTS duration | Tcp2-Tcp1= 52 | ceil((RTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | OK
CTS duration | Tcp4-Tcp3= 44 | ceil((CTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | OK
Frame duration | Tcp6-Tcp5= 3824 | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | OK

## Slide 9: Test 2a: Deferral Test 1 -Simulation Parameters-
AP1
Assumptions:
  Devices are within energy detect range of each other.
  When AP1 and AP2 start to transmit on the same slot, both packets are lost (PER= 100%). Otherwise packets get through 100%. PER=0 %
Parameters:
  MSDU length:[0:500:2000Bytes]
  2 MPDU limit
  RTS/CTS on
  Data MCS = [0]
  ACK MCS = 0
  AIFS=DIFS = 34us
  Maximal number of Retries = 10
  CWmin=15
  CWmax=1023
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)

## Slide 10: Test 2a: Deferral Test 1 Calibration Result
MCS0
RTS/CTS | Application Packet Size | MSDU Size | PER | Simulation Application Throughput | Simulation MAC Throughput
 | (Bytes) | (Bytes) |  | (Mbps) | (Mbps)
Off | 464 | 500 | 0.11 | 4.56 | 4.92
Off | 964 | 1000 | 0.12 | 5.25 | 5.44
Off | 1464 | 1500 | 0.12 | 5.51 | 5.65
Off | 1964 | 2000 | 0.11 | 5.66 | 5.76
On | 464 | 500 | 0.00 | 4.46 | 4.81
On | 964 | 1000 | 0.00 | 5.33 | 5.53
On | 1464 | 1500 | 0.00 | 5.68 | 5.82
On | 1964 | 2000 | 0.00 | 5.87 | 5.98

## Slide 11: Test 2b: Deferral Test 2 -Simulation Assumptions-
AP1
STA 1
AP 2
AP1
STA 2
Assumptions:
  AP1 and AP2 can not hear each other. (ever)
    Interference Assumptions:
      If any part of an MPDU sees interference, that MPDU should fail
      If any part of a data preamble sees interference, all MPDUs should fail
      If an MPDU, or data premable sees no interference, it should pass
      If an ACK overlaps with the transmission of an OBSS AP, the PER on the ACK should be 0. (i.e. the ACK should pass)

## Slide 12: Test 2b: Deferral Test 2 -Simulation Assumptions-
AP1
Assumptions (Continue):
    Backoff
      If no ACK is received, the transmitter should double it’s CW.
      If an ACK is received, the transmitter should reset its CW
      If no MPDUs are decoded, no ACK should be sent.
      After 10 missing ACKS, the CW should be reset.
    PER definition
      PER= 1-Acked data MPDUs/Total data MPDUs sent
        ( TPUT can be computed from number of successfully ACKed MPDUs and the total time)
        ACKed data MPDUs are measured by the transmitters

## Slide 13: Test 2b: Deferral Test 2 -Simulation Parameters
Parameters:
  MSDU length:[1500Bytes]
  RTS/CTS [ OFF]
  MCS = [0,8]
  2 MPDU limit
  Data MCS = [0]
  ACK MCS = 0
  AIFS=DIFS = 34us
  Maximal number of Retries = 10
  CWmin=15
  CWmax=1023

## Slide 14: Test 2b: Deferral Test 2 Calibration Results
Without RTS/CTS
RTS/CTS | Data Rate | Application Packet Size | MSDU Size | PER | Simulation Application Throughput | Simulation MAC Throughput
 | (MCS) | (Bytes) | (Bytes) |  | (Mbps) | (Mbps)
Off | 0 | 1464 | 1500 | 88.37 | 1.01 | 1.04
Off | 8 | 1464 | 1500 | 29.14 | 34.75 | 35.60

## Slide 15: Test 3: Test 2b with RTS/CTS -Simulation Assumptions
AP1
STA 1
AP 2
AP1
STA 2
Assumptions:
  AP1 and AP2 can not hear each other. ( ever)
  If MPDUs from AP1 and AP2 overlap, they both fail with 100% probability
  If an MPDU from AP1/AP2 is interference free, it succeeds with 100% probability.

## Slide 16: Test 3: Deferral Test 2 -Simulation Parameters
Parameters:
  MSDU length:[1500Bytes]
  RTS/CTS [ ON]
  MCS = [0,8]
  2 MPDU limit
  Data MCS = [0]
  ACK MCS = 0
  DIFS = 34us
  Maximal number of Retries = 10
  CWmin=15
  CWmax=1023

## Slide 17: Test 3: NAV Deferral Calibration Results
With RTS/CTS
RTS/CTS | Data Rate | Application Packet Size | MSDU Size | PER | Simulation Application Throughput | Simulation MAC Throughput
 | (MCS) | (Bytes) | (Bytes) | (%) | (Mbps) | (Mbps)
On | 0 | 1464 | 1500 | 0.00 | 5.58 | 5.72
On | 8 | 1464 | 1500 | 0.00 | 34.05 | 34.88

## Slide 18: Reference
[1] 11-14-0980-02-00ax-simulation-scenarios
[2] 11-14-0571-03-00ax-evaluation-methodology

## Slide 19: Annex.1

## Slide 20: Annex.2 MPDU collision model
AP1
A A-MPDU subframe is correctly received if and only if its preamble and itself are not affected by interference