## Slide 1: MAC calibration results comparison
Date: 2014-09-10
Authors:

## Slide 3: Summary
This contribution provides result comparison of MAC calibration of test 1-3 from variety of companies [1][2]
This contribution also proposes a criteria for result alignment
There are some parameter setting in the simulation scenario document that may generate different interpretation, this contribution clarifies these parameter settings

## Slide 4: Status Overview
Status √: aligned, −: No need to provide
Calibration | Box 3 – MAC Calibration |  |  |  |  |  |  |  |  |  |  |  | 
Simulation Scenarios | Test 1a |  |  |  | Test 1b |  |  |  | Test 2a |  | Test 2b | Test 3 | Test 4
Scenario Names | MAC overhead w/out RTS/CTS |  |  |  | MAC overhead w RTS/CTS |  |  |  | Deferral Test 1 |  | Deferral Test 2 | NAV deferral | Deferral Test for 20 and 40MHz BSSs
Configurations | MCS = [0] | MCS = [0] | MCS = [8] | MCS = [8] | MCS = [0] | MCS = [0] | MCS = [8] | MCS = [8] | RTS/CTS [OFF] | RTS/CTS [ON] | RTS/CTS [OFF] | RTS/CTS [ON] | 
Metrics | MAC Tput | Check Points | MAC Tput | Check Points | MAC Tput | Check Points | MAC Tput | Check Points | MAC Tput | MAC Tput | MAC Tput | MAC Tput | 
LG | √ | √ | √ | − | √ | √ | √ | − | √ | √ | √ | √ | 
Huawei | √ | √ | √ | − | √ | √ | √ | − | √ | √ | √ | √ | 
Qualcomm | √ | √ |  | − | √ | √ |  | − | √ | √ | √ | √ | 
MediaTek | √ | √ | √ | − | √ | √ | √ | − |  | √ |  | √ | 
Intel | √ | √ | √ | − | √ | √ | √ | − | √ | √ |  | √ | 
Ericsson | √ |  | √ | − | √ |  | √ | − | √ | √ |  |  | 
Nokia | √ |  | √ | − | √ |  | √ | − | √ | √ |  |  | 
NTT | √ |  | √ | − | √ |  | √ | − | √ | √ | √ | √ | 
… |  |  |  |  |  |  |  |  |  |  |  |  | 
Criteria:
  Make average over most close three companies as the baseline to compare
  If the performance value intended for calibration is within 5% deviation, it is marked as aligned

## Slide 5: Test 1a
AP1
Configurations | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
Huawei | 4.79 | 5.55 | 5.84 | 6.00 | 21.98 | 34.91 | 43.24 | 48.67
LGE | 4.81 | 5.55 | 5.84 | 5.99 | 22.4 | 35.2 | 43.25 | 48.9
Qualcomm | 4.76 | 5.53 | 5.82 | 5.98 | 23.92 | 37.25 | 45.55 | 50.81
MediaTek | 4.76 | 5.53 | 5.82 | 5.98 | 21.71 | 34.65 | 42.71 | 48.15
Intel | 4.76 | 5.53 | 5.82 | 5.98 | 21.53 | 34.46 | 42.58 | 48.14
Ericsson | 4.75 | 5.52 | 5.82 | 5.97 | 21.53 | 34.47 | 42.57 | 48.09
Nokia | 4.76 | 5.52 | 5.83 | 5.97 | 21.19 | 34.22 | 41.93 | 47.74
NTT | 4.79 | 5.54 | 5.84 | 6.00 | 22.00 | 35.00 | 43.20 | 48.40

## Slide 6: Test 1b
AP1
Configurations | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
Huawei | 4.42 | 5.31 | 5.66 | 5.85 | 15.94 | 27.07 | 34.97 | 40.61
LGE | 4.45 | 5.31 | 5.66 | 5.86 | 16.2 | 27.3 | 35 | 40.8
Qualcomm | 4.4 | 5.29 | 5.64 | 5.84 | 18.64 | 30.75 | 38.94 | 44.51
MediaTek | 4.40 | 5.29 | 5.64 | 5.84 | 15.79 | 26.90 | 34.62 | 40.24
Intel | 4.4 | 5.29 | 5.64 | 5.84 | 15.7 | 26.8 | 34.55 | 40.26
Nokia | 4.40 | 5.28 | 5.64 | 5.83 | 15.52 | 26.66 | 34.12 | 39.96
NTT | 4.42 | 5.30 | 5.67 | 5.85 | 16.00 | 27.10 | 34.97 | 40.40

## Slide 7: Test 2a
AP1
Configurations | Without RTS/CTS |  |  |  | With RTS/CTS |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
Huawei | 4.56 | 5.25 | 5.51 | 5.66 | 4.46 | 5.33 | 5.68 | 5.87
LGE | 4.62 | 5.28 | 5.54 | 5.66 | 4.5 | 5.34 | 5.68 | 5.88
Qualcomm | 4.57 | 5.26 | 5.53 | 5.67 | 4.45 | 5.32 | 5.67 | 5.86
MediaTek | 4.71 | 5.48 | 5.78 | 5.94 | 4.35 | 5.24 | 5.62 | 5.81
Intel | 4.52 | 5.22 | 5.48 | 5.62 | 4.44 | 5.31 | 5.67 | 5.86
Ericsson | 4.53 | 5.21 | 5.48 | 5.63 |  |  |  | 
Nokia | 4.58 | 5.29 | 5.56 | 5.71 | 4.48 | 5.32 | 5.67 | 5.85
NTT | 4.58 | 5.25 | 5.45 | 5.66 | 4.49 | 5.35 | 5.70 | 5.88

## Slide 8: Test 2b results
L4 Tputs with MPDU Frame Aggregation (FA)
Scenarios | Huawei | LGE | Qualcomm | MediaTek | Intel | Nokia | NTT
test2b-noRTS-noFA-MCS0 | 1.62 | 1.7 |  |  |  |  | 
test2b-noRTS-FA-MCS0 | 1.01 | 1.02 | 0.98 | 0.03631 | 1.008 | 1.20 | 1.06
test2b-noRTS-noFA-MCS8 | 26.54 | 26.8 |  |  |  |  | 
test2b-noRTS-FA-MCS8 | 34.75 | 35.0 |  |  |  | 35.66 | 

## Slide 9: Test 3 results
L4 Tputs with MPDU Frame Aggregation (FA)
Scenarios | Huawei | LGE | Qualcomm | MediaTek | Intel | Nokia | NTT
test3-RTS-noFA-MCS0 | 5.15 | 5.14 |  |  |  |  | 
test3-RTS-FA-MCS0 | 5.58 | 5.58 | 5.55 | 5.63933 | 5.66 | 5.59 | 5.40
test3-RTS-noFA-MCS8 | 22.04 | 22.4 |  |  |  |  | 
test3-RTS-FA-MCS8 | 34.05 | 34.2 |  |  |  | 31.35 | 

## Slide 10: Proposed parameter setting modification
Test 1a
  Data MCS = [0,8] ( to clarify, run a sweep over MSDU length once for MCS 0, and once for MCS 8.
  ACK MCS = 0
  AIFS=DIFS = 34us
Test 1b
  Data MCS = [0,8] ( to clarify, run a sweep over MSDU length once for MCS 0, and once for MCS 8.
  ACK MCS = 0
  AIFS=DIFS = 34us
Test 2a
  Data MCS = [0]
  ACK MCS = 0
  AIFS=DIFS = 34us
  CWmax=1023
Test 2b
  2 MPDU limit
  Data MCS = [0]
  ACK MCS = 0
  AIFS=DIFS = 34us
  CWmax=1023
Test 3
  2 MPDU limit
  Data MCS = [0]
  ACK MCS = 0
  AIFS=DIFS = 34us
  CWmax=1023

## Slide 11: Straw poll
Do you support adopting the parameter settings listed in slide 9 into the simulation scenario document
  YES
  NO
  ABS

## Slide 12: Straw poll
Do you support adopting a link of this contribution into the simulation scenario document as an initial report of box 3 MAC calibration
  Instruct the editor to add the following paragraph before Annex 1
    Calibration results
      The initial calibration report is provided in contribution [].
  Instruct the editor to add reference of this contribution
    []11-14-1192-02-00ax-comparing-mac-calibration-results.pptx
    YES
    NO
    ABS

## Slide 13: Reference
[1]11-14-1230-00-00ax-mac-calibration-result.pptx
[2]11-14-1192-00-00ax-comparing-mac-calibration-results.pptx