## Slide 1: NG60 channel model
Date: 2014-09-16
Authors:

## Slide 2: Abstract
Channel bonding
MIMO in mmWave
Simulation Example
Channel model for MIMO @ NG60

## Slide 3: Channel bonding
Channel bonding is simple technique to multiply the transmission rate
Use of contiguous band is preferred for hardware. Less crowded than 2.4 or 5 GHz, interference and spectral mask issues less pivotal as in 5G
Spatial selectivity higher than in other bands, with higher scattering and diffractions e.g. 2.4G, 5G, hence less in-band interference
Today ADC technology allows implementation of 5.3Gsps 6 bits ADC/DAC with <70mW

## Slide 4: MIMO in mmWave
Each antenna can be either:
  A separated phased array subassembly
  Separated chain within same subassembly
Many MIMO options: SVD,ML,MMSE, etc.
60 GHz MIMO has unique features:
  Good separation between subassemblies (>>λ)
  Each subassembly is a configurable antenna array
  High bandwidth, moderate SNR: robustness to low power interference
  RX->TX basic feedback for multi-antenna already defined in the 802.11ad specification

## Slide 5: MIMO in mmWave
Consider a 4x4 MIMO in 60GHz system in the frequency domain
At receiver chain 2, the received signal is
Where:
: the subassembly configuration for RX-chain i,
: the subassembly configuration for TX-chain i
: the signal transmitted through TX-chain i
: the physical channel between each receive and transmit antenna element
#1
#2
#3
#4
#1
#2
#3
#4

## Slide 6: MIMO in mmWave
Phased arrays approximated SVD: The RF configurations approximate the singular vectors from the SVD of H
Each TX antenna subassembly sends 1 stream to one RX antenna subassembly Other options such as 1->2 or 2->1 are not effective for multiple antenna subassemblies due to the directivity
Feedback from RX to TX
  TX-SS is multiplied by # TX antenna subassemblies
  TX-SS extended feedback is multiplied by #TX antenna subassemblies
  TX-SS is followed by multiple 802.11ad MIDC
PHY Channel estimation done per stream
MCS/power per stream: TX power limit per subassembly
Notes: SS – Sector Sweep
MIDC – multiple sector identifier capture(11ad)

## Slide 7: Example: simulation
Double channel (3.5 GHz bandwidth)
Using approximated SVD, 4 sector IDs are returned to TX
Each antenna subassembly is made of 16 patch antennas arranged in two lines
4 subassemblies, each turning to different direction (as in the picture in the backup slide)
All rates up to 64QAM are used
Room of 4x5x2.8 [m] with a table of 3x1.2 [m] in the center and a monitor of 0.4x0.4 [m] on top of the table

## Slide 8: Example: simulation (cont)
TX remains fixed at the end of the table, RX moves around
3D Ray-tracing simulation, all reflections are considered up to the 2 order reflection, including from ceiling/floor
Simulator was calibrated to real-world measurements and current system parameters
Maximum SINR RF configuration is used. The BB in this example does not include any multi-stream spatial equalizer

## Slide 9: Example: simulation results – rate in bps

## Slide 10: Channel model for MIMO @ NG60
Use H’=Θr H Θt as the channel model
  compact matrix
  compresses the false degrees of freedom from H
  same approach as MIMO channel models in previous standards (802.11, 3GPP etc.).
Several environments:
  Living room, strong reflectors (low ceil, concrete walls)
  Cubical, weak reflectors (high ceil, fabric walls)
  Large conference room
  Outdoor

## Slide 11: Channel model for MIMO @ NG60
System options:
  Same subassembly, several chains (1,2,3,4)
  Several subassemblies with varying number of antennas (1,4,16,32)
  Basic array configuration options:
    SNR optimal: Just maximum SNR
    SINR-optimal: Takes inter chains interference into account
    Capacity-optimal: requires a lot of feedback
Will a full-duplex mode be of use ?
The channel model from 802.11ad should be modified for MIMO

## Slide 12: Backup

## Slide 13: Example: a tablet system

## Slide 14: ADC/DAC FOM
ADC/DAC: looking into the literature Figure of merit (FOM)
  Digitally assisted ADCs are common in the industry
  ADCs running in 5GHz BW, assuming 6 bits
  Power estimated is 32 mW

## Slide 15: ADC/DAC FOM
A/D Converter Trends: Power Dissipation, Scaling and Digitally Assisted Architectures, B. Murmann Stanford University, Stanford, CA, IEEE 2008 Custom Integrated Circuits Conference (CICC)
ADCsurvey_rev20130629a.xlsx http://www.scribd.com/doc/205265261/ADCsurvey-rev20130629a