## Slide 1
MAC considerations on 802.11ax OFDMA
Date: 2014-09-17
Authors:

## Slide 2: Introduction
In IEEE 802.11ax PAR [1], IEEE 802.11ax should provide methods for efficient use of spectrum resources in dense STAs per BSS.
  Make more efficient use of spectrum resources in scenarios with a high density of STAs per BSS.
  Significantly increase spectral frequency reuse and manage interference between neighboring overlapping BSS (OBSS) in scenarios with a high density of both STAs and BSSs.
OFDMA could be one of solutions to provide efficient spectrum resource utilization
  In IEEE 802.11-10/0317r1[2] DL-OFDMA increase AP utilization and throughput dramatically.
At the same time, OFDMA should be designed to provide interference management under a high density of both STAs and OBSSs.
Since dense wideband STAs and OBSSs scenarios may cause severe system degradation by contentions, OFDMA with guaranteed TXOP should be studied in 802.11ax

## Slide 3: OFDMA operation
OFDMA without RTS/CTS
  New Preamble is only way to support OFDMA without RTS/CTS except full scanning case
    Full scanning means STAs are always listening and decoding all the possible channels
  A parameter indicating group allocation is required (e.g., Group ID of MU-MIMO)
  Resource indicator for user-resource assignment is also required
  However, OFDMA w/o RTS/CTS suffers from severe interference due to a high density of STAs and OBSSs

## Slide 4: Considerations on OFDMA with RTS/CTS
Requirements for OFDMA operation with RTS/CTS
  Protection from interference caused by legacy devices as well as 802.11ax devices should be provided
    Collisions should be minimized
  Using legacy control frames is recommended
    Modification on control frames for OFDMA should be minimized
  Power consumption & complexity should be reduced
    Operational overhead should be minimized
  When OFDMA is unusable, 802.11ax devices should be able to act like non-OFDMA devices
    Procedure overhead for OFDMA transmission should be minimized

## Slide 5: OFDMA under high density of STAs and OBSSs (CTS-to-Self)
OFDMA CTS-to-Self

## Slide 6: OFDMA under high density of STAs and OBSSs (CTS-to-Self)
OFDMA CTS-to-Self[3]
  Disadvantage
    CTS-to-Self cannot solve Hidden terminal problem (severe interference)
  Advantage
    Primary channel based simple scanning

## Slide 7: OFDMA under high density of STAs and OBSSs (RTS/CTS)
OFDMA RTS/CTS

## Slide 8: OFDMA under high density of STAs and OBSSs (RTS/CTS)
Example protocol of Full Scanning OFDMA RTS/CTS
  Channel extended form of legacy RTS/CTS
  Each STAs are scanning all the possible channel always
  Large operational overhead but similar to ideal form
    Does not satisfy the requirement of operational overhead reduction

## Slide 9: OFDMA under high density of STAs and OBSSs (RTS/CTS)
OFDMA modified RTS/CTS
  All the transmitted modified RTS frames are exactly identical
  Legacy STAs recognize the modified RTS as a normal RTS (Same frame format as a legacy RTS frame, but different use of receiver address)
  User and channel assignment information is not included in RTS

## Slide 10: Summary
 |  | Pros | Cons
Without RTS/CTS | Full Scanning | Using Legacy procedure and frame | Large operational overhead
 | New Preambles | Minimizing operational overhead | Modification on preamble
With RTS/CTS | Full Scanning | Using Legacy procedure and control frame | Large operational overhead
 | CTS-to-Self | Using Legacy control frame | Hidden terminal problem
 | Modified RTS | Guarantee of TXOP with low operational overhead | Control frame modification

## Slide 11: Conclusion
Full scanning method makes OFDMA channel access protocol simple, however, it requires high operational overhead
OFDMA operation w/o RTS/CTS relies on preamble of its data frame
CTS-to-self technique requires small operational overhead, but cannot solve hidden terminal problem
Modified RTS does not cause hidden terminal problem
Since using OFDMA with RTS/CTS provides good performance in dense STAs and OBSS scenario, it is recommended to study more in 802.11ax

## Slide 12: References
[1] IEEE 802.11-14/0165r1 “802.11 HEW SG Proposed PAR”
[2] IEEE 802.11-10/0317r1 “DL-OFDMA for Mixed Clients”
[3] IEEE 802.11-09/0138r3 “OFDMA Related Issues in VHTL6”