## Slide 1: MAC Calibration Results for Tests 1 and 2
Date: 2014-09-14
Authors:

## Slide 2: Overview
Maintained assumptions from previous MAC Calibration
  If packets collide, both packets are lost
  If packets do not collide, receive both
New assumptions from 11-14/0967-05
  2 MPDUs per A-MPDU for all scenarios
  Block ACK is always received correctly if packets do not collide

## Slide 3: Test 1a: MAC overhead without RTS/CTS
Goal:
  Designed to verify whether the simulator can correctly handle the basic frame exchange procedure, including AIFS+backoff procedure and A-MPDU + SIFS + BA sequence.
  Also to make sure the overheads are computed correctly.
Assumptions:
  Assumption is that PER is 0
Parameters:
  MSDU length: [500, 1000, 1500, 2000] Bytes
  2 MPDUs per A-MPDU limit
  RTS/CTS off
  MCS = [0,8] ( to clarify, run a sweep over MSDU length once for MCS 0, and once for MCS 8.
STA 1
AP1

## Slide 4: Test 1a: MAC overhead without RTS/CTS
MCS | MSDU Length | DL Mean System T-Put (Mbps)
MCS 0 (BPSK ½) | 500 | 5.13
 | 1000 | 5.73
 | 1500 | 5.97
 | 2000 | 6.08
MCS 8 (256 QAM ¾) | 500 | 22.83
 | 1000 | 35.50
 | 1500 | 42.96
 | 2000 | 48.61

## Slide 5: Test 1b: MAC overhead with RTS/CTS
Goal:
  This test case is designed to further verify whether the simulator can correctly handle the frame exchange procedure with RTS/CTS protection based on test1a. It also tests whether the correct overhead computation with RTS /CTS.
Assumptions:
  Assumption is that PER is 0
Parameters:
  MSDU length: [500, 1000, 1500, 2000] Bytes
  2 MPDUs per A-MPDU limit
  RTS/CTS is always on
  MCS = [0,8] ( to clarify, run a sweep over MSDU length once for MCS 0, and once for MCS 8.
STA 1
AP1

## Slide 6: Test 1b: MAC overhead with RTS/CTS
MCS | Length | DL Mean System T-Put (Mbps)
MCS 0 (BPSK ½) | 500 | 4.74
 | 1000 | 5.48
 | 1500 | 5.78
 | 2000 | 5.94
MCS 8 (256 QAM ¾) | 500 | 16.72
 | 1000 | 27.66
 | 1500 | 34.96
 | 2000 | 40.69

## Slide 7: Test 2a: Deferral Test 1
Goal:
  This test case is designed to verify whether the simulator can correctly handle deferral procedure after collision happens without hidden nodes. It also checks whether deferral because of energy levels is happening correctly.
Assumptions:
  All devices are within energy detect range of each other.
  When AP1 and AP2 start to transmit on the same slot, both packets are lost (PER= 100%). Otherwise packets get through 100%. PER=0 %
Note:
  AP1 and AP2 should defer to each other.
  The only packet loss is due to collisions when backoffs end at same time
Parameters:
  MSDU length: [500, 1000, 1500, 2000] Bytes
  2 MPDUs per A-MPDU limit
  RTS/CTS [ OFF, ON]
  MCS = [0]
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)

## Slide 8: Test 2a: Deferral Test 1
RTS/CTS | Length | DL Mean System T-Put (Mbps)
Off | 500 | 4.94
 | 1000 | 5.49
 | 1500 | 5.70
 | 2000 | 5.81
On | 500 | 4.83
 | 1000 | 5.52
 | 1500 | 5.81
 | 2000 | 5.96

## Slide 9: Test 2b: Deferral Test 2
Goal:
  This test case is designed to verify whether the simulator can correctly handle deferral procedure after collision happens with the existing of hidden nodes.
Assumptions:
  AP1 and AP2 can not hear each other. ( ever)
  Interference Assumptions:
    If any part of an MPDU sees interference, that MPDU should fail
    If any part of a data preamble sees interference, all MPDUs should fail
    If an MPDU, or data premable sees no interference, it should pass
    If an ACK overlaps with the transmission of an OBSS AP, the PER on the ACK should be 0. (i.e. the ACK should pass)
  Backoff
    If no ACK is received, the transmitter should double it’s CW.
    If an ACK is received, the transmitter should reset its CW
    If no MPDUs are decoded, no ACK should be sent.
    After 10 missing ACKS, the CW should be reset.
  PER definition
    PER= 1-Acked data MPDUs/Total data MPDUs sent
    TPUT can be computed from number of successfully ACKed MPDUs and the total time
  ACKed data MPDUs are measured by the transmitters
Parameters:
  MSDU length:[1500Bytes]
  RTS/CTS [ OFF]
  MCS = [0]
STA 1
AP 2
AP1
STA 2

## Slide 10: Test 2b: Deferral Test 2
MCS | RTS/CTS | Length | DL Mean System T-Put (Mbps) | DL Data BLER [%]
MCS 0 (BPSK ½) | Off | 1500 | 1.23 | 82.74
 | On | 1500 | 5.73 | 0.81
MCS 8 (256 QAM ¾) | Off | 1500 | 36.54 | 18.40
 | On | 1500 | 32.12 | 6.24