## Slide 1: Doppler Effect Evaluation for 11ax
Date: 2014-09-12
Authors:

## Slide 2: Introduction
IEEE 802.11ax outdoor operation focus on pedestrian mobility, reflections from fast moving objects, such as cars, can cause higher Doppler. In [1], the following two Doppler modes should be supported in the outdoor spatial channel models.
  1. Speed up to 3kmph for all clusters for UMi and UMa models; (STA velocity = 3 kmph)
  2. The TBD cluster of UMi and UMa models assigned a speed of 60kmph and the rest of the clusters assigned 0 kmph

## Slide 3: Doppler Effect due to a Moving STA
In [2], a theoretical model is built where the change of phase due to a moving station (STA) between time t and t + Δt is given by
where θp is the incident angle of the pth propagation path into a received and vm is the moving velocity of station.

## Slide 4: Doppler Effect due to a Moving Cluster (Scatter)
In [2], a theoretical model is built where the change of phase due to a moving pth scatter (or cluster) between time t and t + Δt is given by
  Where αp is the angle between the direction of scatter (or cluster) movement,
  γp the direction orthogonal to the reflecting surface and the reflection angle and v is the moving velocity of the cluster.
  By proper selection of these angles different Doppler spectrums may be achieved.
  The model is also adopted for B5 – stationary feeder scenario in Winner II channel mode [3].

## Slide 5: Comments
We find out that if we assume Doppler on one cluster only, to assign a speed of 60kmph to cluster 2 or 3 has similar Doppler effect.
If we consider that there might be two fast moving objects (say, two cars running nearby), then the Doppler effect is much more severe.
To make our 11ax more robust in outdoor scenario, we might need to take care of more severe cases, so there are two options for us to consider.

## Slide 6: Options
Option 1: The 2nd cluster of UMi and UMa models assigned a speed of 60kmph and the rest of the clusters assigned 0/3 kmph.
Option 2: The 2nd and the 3rd clusters of UMi and UMa models assigned a speed of 60kmph and the rest of the clusters assigned 0/3 kmph.
Option 0 (for comparison): No moving cluster and the rest of the clusters assigned 0/3 kmph.

## Slide 7: Evaluation Setup
We obtain the autocorrelation of the channel impulse response over 10000 time samples in time domain.
We average the autocorrelation over 1000 channel realizations.
The time sample duration is set equal to be 1/(4*fD) ≈ 0.9 ms, where fD is the maximum Doppler frequency shift with velocity of 60 km/hr.
  For comparison, we only show the time scale from 0 to 100 msec.
  We also zoom out each result with time scale from 0 to 5 msec.

## Slide 8: STA velocity = 3 km/hr (NLoS)

## Slide 9: STA velocity = 3 km/hr (LoS)

## Slide 10: STA velocity = 0 km/hr (NLoS)

## Slide 11: STA velocity = 0 km/hr (LoS)

## Slide 12: Conclusions
When we consider the Doppler effects from both moving station and scatter,
  Long-term time scale (0 – 100 msec): the Doppler effect of moving STA dominates the performance.
  Short-term time scale (0 – 2 msec): the Doppler effect of moving scatters dominates the performance.
In turn, when we consider Doppler effects only from the movement of some scatters, the correlation coefficients will be degraded to be from 0.6 to 0.9 under NLoS scenario.
  However, under LoS scenario, the correlation coefficients will be degraded to be from 0.95 to 0.98.
It is natural to consider only one fast moving object or two fast moving objects cases:
  Option 1 (one fast moving object): The 2nd cluster of UMi and UMa models assigned a speed of 60 kmph and the rest of the clusters assigned 3 kmph.
  Option 2 (two fast moving objects): The 2nd and the 3rd clusters of UMi and UMa models assigned a speed of 60 kmph and the rest of the clusters assigned 3 kmph.

## Slide 13: Straw Poll #1
Do you support to add the following Doppler effect to IEEE 802.11ax channel model document
  The 2nd and the 3rd clusters of UMi and UMa models assigned a speed of 60 kmph and the rest of the clusters assigned 3 kmph.

## Slide 14: Reference
[1] “IEEE 802.11ax Channel Model Document”, IEEE 802.11-14/0882r3, Jianhan Liu, etc.
[2] Thoen, S.; Van der Perre, L.; Engels, M., "Modeling the channel time-variance for fixed wireless communications," Communications Letters, IEEE , vol.6, no.8, pp.331,333, Aug. 2002
[3] IST-WINNER D1.1.2 P. Kyösti, et al., "WINNER II Channel Models", ver 1.2, Apr. 2008.