## Slide 1: Link-Aware CCA
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco |  | brianh@cisco.com

## Slide 2: Overview
Situation:
  In 802.11ax we have many proposals for optimizing CCA thresholds and/or receiver sensitivities, including “Dynamic Sensitivity Control”
  Problem:
  For inter-BSS fairness, the Margin parameter in Dynamic Sensitivity Control must be carefully set to avoid unfairness in environments with a mixture of larger and smaller BSSs
    e.g. overlay SP network starve near an enterprise network
    e.g. enterprise network with underlay mobile networks
    But no testable proposal is made for selecting Margin
  Solution:
  Option 1: Sean Coffey’s 14/872 (per-PPDU CCA thresholds using PER)
  Option 2: (Presented here) CCA Do-Over – design CCA rules that really address the real problem

## Slide 3: Summary of DSC (1/2)
  Each non-AP STA measures the RSSI of the AP Beacon (R dBm)
  Each non-AP STA adds a margin to that, called M dB
  Each non-AP STA also sets an Upper Limit, L, to Beacon RSSI to cater for case where the non-AP STA is very close to its AP.
  i.e. Receiver sensitivity = min(R,U)-M
  E.g. R = -15 dBm, L = -30 dBm, M = 20 dB, then Receiver sensitivity = -50 dBm
  And, CCA-CS tracks the receiver sensitivity, as:
    CCA-CS = max(-82* dBm, Receiver sensitivity)
      *Assuming 20 MHz

## Slide 4: Summary of DSC (2/2)
Assumes AP doesn’t move; over-estimates installer’s access, etc
  Residential Service Provider
    Margin could be preset based upon simple check list
      Size/type of property (e.g. apartment/house? Rooms? Floors?)
    Or carrying out simple instructions
      Walk the (high data rate required) area; walk the extremes (for DSC AP)
    Settings could be learnt - room for clever learning algorithms
  Dumb User, residential
    DSC AP
      Learning algorithm?
        After say 1 week, AP ‘knows’ distribution of its STAs.
      May use DSC to ‘prioritize’, for example, its HD video STAs
      Use of internal Receive Sensitivity threshold probably ‘dangerous’
  DSC non-AP STA
    No real danger to assume a setting such as -40dBm and 20dB. High probability of avoiding OBSS and always ‘in range’ as STA moves away from AP (this is a the major feature of DSC versus a fixed, higher, CCA threshold).”
Battery powered non-AP STAs (and APs!) go everywhere; see next slide for one pathological case
Non-robust to building materials
“Selfish algorithms” - no mechanism for overlapping victim BSSs to be protected

## Slide 5: Unfairness from DSC
Multi-tenant office/mall or apartment building
Service Provider AP2 (“Outdoor hotspot”)
Tenant2
Client2
Tenant1
Client1
Home AP1
-45 dBm
-75 dBm
-80 dBm
  C1 in BSS1 operates DSC at -65 by design (default rule defined above)
    With DSC, PPDUs at -75 dBm from BSS2 do not trigger CCA-ED, CCA-CS, nor VCS
  DSC in BSS2 will not substantially change the CCA thresholds or receiver sensitivities of STAs in BSS2
    Thus, STAs in BSS2 do contend with STAs in BSS1 and BSS2 (unfairness)
  Worse, when AP2 transmits to C2, this PPDU and its Duration field is completely ignored by C1, so C1 will often transmit over the top of AP2. The SINR at C2 is negative so the AP retries with a higher backoff. If C1 is heavily loaded, the cycle repeats and we see that the BSS2 downlink throughout is very low (unfairness).

## Slide 6: CCA Do-Over: Who Are the Actors?
  Initiating STAs (called “ISTAs”) transmit PPDUs that contain unicast/groupcast frames desired by an responder STA (called “RSTA”)
  Other overlapped STAs (called “OSTAs”) want to transmit PPDUs at the same time as the desired PPDUs (e.g. to the blank STA or the RSTA).
  (By the way, ISTAs and OSTAs are not disjoint sets since: e.g. if the RSTA is an AP, then its clients are both ISTAs and potential OSTAs)
  Attempt to protect both an initiating PPDU and a response PPDU
ISTA
RSTA
OSTA

## Slide 7: CCA Do-Over: What Are We Trying to Achieve? Initiating PPDU
  The RSTA can successfully receive PPDUs from a ISTA if either a colliding PPDU from an OSTA is received at no greater than rssi(desiredPpdu,I⇒R) – Margin, or the OSTA doesn’t transmit. This requires the Initiating CCA rule:
    rssi(desiredPpdu,I⇒R) – Margin > omniEirp(txPpdu,O) – pathloss(R⇒O)
      Where: pathloss(R⇒O) = omniEirp(txPpdu,R) – rssi(snoopedPpdu,R⇒O)
    So: rssi(desiredPpdu,I⇒R) – Margin > omniEirp(txPpdu,O) – omniEirp(txPpdu,R) + rssi(snoopedPpdu,R⇒O)
    Margin is some agreed and standardized value (e.g. in the range of 15-30 dB).
    “omniEirp” = expected EIRP away from the beamformed target
    rssi(desiredPpdu,I⇒R) could be a maximum/mean over a recent window (e.g. 5 sec)
  pathloss(R⇒O)
ISTA
RSTA
OSTA
  rssi(desiredPpdu,I ⇒R)
  omniEirp(txPpdu,cR)
  cR
  rssi(snoopedPpdu,R⇒O)
  Initiating
  CCA rule
  omniEirp(txPpdu,O)

## Slide 8: CCA Do-Over: What Needs to be Advertised? Initiating PPDU
  For the OSTA to implement the Initiating CCA rule ,it needs:
    omniEirp(txPpdu,O) is already known to the OSTA
    The omniEirp(txPpdu,R) and rssi(snoopedPpdu,R ⇒O) parameters must come from the same PPDU, and be reasonably recent (e.g. within 5 sec)
      If not recently measured , the OSTA can fall back to conventional VHT CCA
      The EIRP and transmitter identity (= R) parameters in omniEirp(txPpdu,R) is snooped information, so must be carried in a SIG field of a PPDU from STA2. Thus, really we’re talking about a compressed omniEirp and a compressed TA in a HEW SIG field
    Both the RSSI and receiver identity (=R) parameters in rssi(desiredPpdu,I⇒R) must be advertised by RSTA and reach OSTA
      Here, both the RSSI and receiver identity information are snooped information, so must be carried in a SIG field.
      As well, the receiver identity is the same as transmitter identity above
    Partial summary: the SIG fields transmitted by the RSTA (or any other HEW STA) should contain:
      Compressed RSTA identity (cR) (5-10 bits)
      omniEirp(txPpdu,cR) (3-5 bits)
      rssi(desiredPpdu,cR) (4-6 bits)
    As well, implicitly, when ISTA transmits a PPDU to RSTA, the PPDU needs to include the compressed identity of RSTA (i.e. cR). Diagrammatically:
      Compressed RSTA identity (cR) (4-10 bits)
ISTA
RSTA
OSTA
  rssi(desiredPpdu,I ⇒R)
  cR
  rssi(desiredPppu,R)
  omniEirp(txPpdu,R)
  cR
  rssi(snoopedPpdu,R⇒O)
  Initiating
  CCA rule
  omniEirp(txPpdu,O)

## Slide 9: CCA Do-Over: What Are We Trying to Achieve? Responding PPDU
  The ISTA can successfully receive PPDUs from the RSTA if either a colliding PPDU from an OSTA is received at no greater than rssi(desiredPpdu,R⇒I) – Margin, or the OSTA doesn’t transmit. This requires the Responding CCA rule:
    rssi(desiredPpdu,R⇒I) – Margin > omniEirp(txPpdu,O) – pathloss(I⇒O)
      Where: pathloss(I⇒O) = omniEirp(txPpdu,I) – rssi(snoopedPpdu,I⇒O)
    So: rssi(desiredPpdu,R⇒I) – Margin > omniEirp(txPpdu,O) – omniEirp(txPpdu,I) + rssi(snoopedPpdu,I⇒O)
  pathloss(I⇒O)
ISTA
RSTA
OSTA
  rssi(desiredPpdu,R ⇒I)
  cR
  omniEirp(txPpdu,I)
  rssi(snoopedPpdu,I⇒O)
  Responding
  CCA rule
  omniEirp(txPpdu,O)

## Slide 10: CCA Do-Over: What Needs to be Advertised? Responding PPDU
  For the OSTA to implement the Responding CCA rule, it needs:
    omniEirp(txPpdu,O) is already known to the OSTA
    rssi(snoopedPpdu,I⇒O) can be directly measured by the OTA from the initiating PPDU. Meanwhile the omniEirp(txPpdu,I) must come from the same PPDU
    The rssi(desiredPpdu,R⇒I) must be advertised by ISTA also
    Final Summary (Initiating and Responding CCA Rules):
      the SIG field transmitted by the RSTA (or any other HEW STA) should contain:
        RSTA indication (1 bit)
        Compressed RSTA identity (cR) (5-10 bits)
        omniEirp(txPpdu,R) (3-5 bits)
        rssi(desiredPpdu,R) (4-6 bits)
      the SIG field transmitted by the ISTA should contain
        ISTA indication (1 bit)
        Compressed RSTA identity (cR) (5-10 bits)
        omniEirp(txPpdu,I) (3-5 bits)
        rssi(desiredPpdu, I) (4-6 bits)
ISTA
RSTA
OSTA
  cR
  rssi(desiredPppu,R⇒I)
  omniEirp(txPpdu,I)
  rssi(snoopedPpdu,I⇒O)
  Responding
  CCA rule
  omniEirp(txPpdu,O)
  rssi(desiredPpdu,R ⇒I)

## Slide 11: Bitwidth Considerations
  These fields consume SIG time, so terseness is vital
  As proposed, these fields consume 50%-100% of a whole SIG OFDM symbol (but, this might be more useful than the SU VHT-SIGB from 11ac)
  For the compressed R, too few bits implies station ambiguity. OSTAs would lump rssi(desiredPppu,I⇒cR) and omniEirp(txPpdu,cR) into the same bin for different stations. Since rssi(desiredPppu,I⇒cR) would be 10-20-30 dB different for two random STAs, this degrades the benefit of this enhanced CCA.
    As long as an OSTA hears all RTAs this is not fatal … for each bin, pick the maximum received over the past 5 sec, and at worst this system gracefully degrades back to the current fixed CCA today
    If two RSTAs, one near and one far, map to the same cR, and an OSTA has recent information about just the far RSTA, but the near RSTA transmits, then the OSTA could transmit and collide with the near RSTA. This motivates more bits for identity, to avoid ambiguity
    Say 10000 STAs in range across 10 channels, so then 10 bits of compressed identity would be “plenty good enough” to (mostly) uniquely ID STAs
  Note: a larger cR probably implies more storage at every OSTA: i.e. 2#bits * storage for rssi(desiredPppu,I⇒R) and omniEirp(txPpdu,R) … i.e. up to 11kbit

## Slide 12: What Can go Wrong?
  We don’t really know omniEirp and RSSI
    +-5dB measurement tolerance … but similar issue with CCA today
    omniEirp is an over simplification for non-isotopic antennas (including omnidirectionals) … will be set to conducted power + antenna efficiency. TBD impact when actual EIRP at an angle >> reported EIRP
  Reusing 5 sec old measurements may be OK – or not. Depends on device speed.
  Margin is a critical parameter to select. Optimal modulation to maximize system throughput is closer to QPSK with high spatial reuse than 256QAM with low spatial reuse. i.e. lower margin. This is a mor optimal direction for 11ax, but means 256QAM and higher only get usage in lightly loaded networks
  If multiple OSTAs transmit at the same time, they raise the interference floor (this analysis assumes a single OSTA). Readily mitigated by adding a few dB extra to Margin
  Mostly these rules are more relaxed than VHT CCA rules, but not always (e.g. protection of long-range links). We have some choices here.
  Bandwidth effects are not included in this presentation. Bandwidth can be easily accounted for if the advertised omniEirp and RSSI parameters report energy per 20 MHz
  System is most robust if the RSTA can be uniquely identified by its cR field.
  With OFDMA and MU-MIMO, it is hard to find enough SIG bits! And the parameters sent by the ISTA really need to be sent in a SIG field (since the ISTA will send at a higher MCS/NSS)
    Default to VHT CCA rules in this case?
  The parameters sent by the RSTA don’t really have to be sent in a SIG field (they could be fields in frames typically sent at low rate – RTS/CTS/Ack/BA frames).
  VHT CCA rules apply to legacy PPDUs
  Simulation results TBD – new kinds of topological unfairness are to be expected?

## Slide 13: Can this be Tested (or Gamed?)
  Reported parameters are internal estimates of omniEIRP and RSSI.
  While these are not exposed parameters, they can be easily compared against measurements made by RF test equipment using colocated antennas … i.e. this is testable
  In the field, an RSTA could over-report its desired RSSI by a few dB (or more) to ensure a lower noise-induced error rate.
    But, this will mean cause fewer free slots at the ISTA, so it is self-limiting
  An AP with desired clients intermittently probing/associating from long range might always report a very high rssi(desiredPpdu,cR)
    But this is not unreasonable behavior
  Certainly APs in high density environments are highly motivated to report low-and-correct rssi(desiredPpdu,cR) values