## Slide 1: Requirements Discussion
Date: 2014-09-15
Authors:

## Slide 2: Abstract
This contribution discusses the need for well defined requirements as part of the approved 802.11 TGax Selection Procedure (11-14/0938r04).
We contend that without meaningful and clearly defined requirements it is not possible to have an open and fair standards development process that adheres to the agreed Selection Procedure.

## Slide 3: Summary of 11-14/0938r4
The Procedure begins with the Functional Requirements.
Without agreed well defined requirements there is no criteria to judge the merit of the technical contributions.
Building of the SFD based on technical criteria is critical to the selection procedure.
Flow Chart from [1]

## Slide 4: Our understanding of what a requirement is
Requirements should bound the goals of the task group
  By setting a minimum required performance
  By setting a allowed range of performance
  By setting an allowed degradation in performance
Requirements should be clear to all task group participants
Requirements should be measurable
  By simulation or calculation
Requirements should expand and further define the goals/requirements stated in the PAR

## Slide 5: Example of Functional Requirements from TGn [2]
Name
Requirement

## Slide 6: TGac Selection Procedure [3] States:
“TGac shall adopt, through a 75% approval in the Taskgroup, a Functional Requirements document that must be met by the proposed specification, including System Level Performance Targets and Simulation Scenarios for those Targets” [bold emphasis added]

## Slide 7: Example of System Performance TGac [4]
2.1 System Performance
2.1.1 Multi-STA throughput measured at the MAC SAP to be at least 1 Gbps.
TGac R1 – The TGac amendment shall provide at least a mode of operation capable of achieving a maximum Multi-Station aggregate throughput of more than 1 Gbps as measured at the MAC data service access point (SAP), utilizing no more than 80 MHz of channel bandwidth in 5 GHz band.
2.1.2 Single-STA throughput measured at the MAC SAP to be at least 500 Mbps.
TGac R2 – The TGac amendment shall provide at least a mode of operation capable of achieving a maximum Single-Station throughput of more than 500 Mbps as measured at the MAC data service access point (SAP), utilizing no more than 80 MHz of channel bandwidth in 5GHz band.
Note: document also defines the scenarios for which each of the requirements should be met.

## Slide 8: Proposed Requirements
Scope: set by the P802.11ax PAR [5] and CSD [6], as well as by the TGax usage models [7]
Requirement areas referred to in the TGax PAR:
  System Performance
    Average Throughput
    5th percentile Throughput
    Area Throughput
  System Efficiency
    Spectrum resources
    Spectral frequency reuse and interference management
    Robustness in outdoor propagation environments/uplink transmissions
  Other Requirements:
    Power Efficiency
    Backward compatibility
    Coexistence with legacy 802.11
    Multiple simultaneous communications in the spatial and frequency domains

## Slide 9: Example Requirement R1 Average Throughput
The 802.11ax amendment shall provide at least one mode of operation capable of achieving at least four times improvement in the average throughput per station, compared to the existing IEEE 802.11 standard and its amendments in the following scenarios:
Scenario 3 (indoor small BSS hotspot)
  Baseline: 100% non-11ax APs and 100% non-11ax STAs.
  11ax: 100% 11ax APs and 50% 11ax STAs.
Scenario 2 (enterprise)
  Baseline: 100% non-11ax APs and 100% non-11ax STAs.
  11ax:100% 11ax APs and 50% 11ax STAs.

## Slide 10
The 802.11ax amendment shall provide a mechanism to improve by at least 10% the spectral frequency reuse in efficiency in 20 MHz and larger frequency channels in the following scenarios:
Scenario 2 (enterprise)
  Baseline: 100% non-11ax APs and 100% non-11ax STAs.
  11ax:100% 11ax APs and 50% 11ax STAs.
Proposed Requirement R2 Spectral frequency reuse

## Slide 11: Conclusion
Without agreed well defined requirements there is no criteria to judge the merit of the technical contributions.
We have provided a set of reasonable meaningful functional requirements in 11-14/xxxxr1
Without criteria to judge the technical merit of contributions we do not see how the current 802.11ax process will be able to move forward in an open and fair manner.

## Slide 12: References
11-14/0938r4, 802.11ax Selection Procedure, Rolf de Vegt (Qualcomm), 17 Jul 2014
11-08/1392r0, Inputs for a VHT Selection Procedure, Rolf de Vegt (Qualcomm), 12 Nov 2008
11-09/0059r4, 802.11ac Proposed Selection Procedure, Rolf de Vegt (Qualcomm), 11 Mar 2009
11-09/0541r16, TGac Functional Requirements and Evaluation Methodology, Peter Loc (Ralink Technology) Minho Cheong (ETRI) 19 Jan 2011
11-14-0165-01-0hew-802-11-hew-sg-proposed-par
11-14-0169-01-0hew-ieee-802-11-hew-sg-proposed-csd
11-13-0657-06-0hew-hew-sg-usage-models-and-requirements-liaison-with-wfa