## Slide 1: Backhaul Support in NG 60
Authors:
Date: 2014-09-15

## Slide 2: Abstract
This contribution outlines some of the requirements for supporting backhaul in NG 60.

## Slide 3: Recap of Backhaul Usage Model
Small cells are becoming increasingly important for cellular and Wi-Fi [1].
Requirements:
  ~ 2 Gbps peak per small-cell data rate
  100 m – 150 m cell size
  Latency: ~ 5 ms, one way, end-to-end.
  Support for bursty traffic
mmW backhaul enabled by 802.11ad/NG60:
  Leverage availability of low-cost chipsets, driven by volume (ABI Research: 1.5 billion chipsets by 2018)

## Slide 4: What does backhaul need from NG 60?
Multi-hop capability.
  Existing 802.11ad specification may not be sufficient for extended range applications.
Enhanced QoS guarantees:
  Beyond current 802.11ad specification.
Higher data rate
  Will be addressed by planned high-data rate enhancements (MIMO, channel bonding, etc.). MU-MIMO may be beneficial as well.
Enhanced discovery methods for longer range
  Discovery range = Communication range.

## Slide 5: Use cases enabled
Solutions that meet the backhaul requirements will also provide benefits to other use cases of interest:
  High-data-rate indoor applications [2], such as video streaming, would benefit from extended range.
  Deployment of infrastructure NG60 APs would benefit from the possibility of self-backhaul, leading to lower-cost.

## Slide 6: Conclusions
Support for backhaul in NG60 may require MAC only or PHY/MAC enhancements to current 802.11ad.
Support for backhaul in NG60 will enable new deployment and use scenarios that may not be fully served by 802.11ad.
Support for backhaul is complementary to high-rate enhancements such as MIMO, higher-order constellation, channel bonding etc.

## Slide 7: References
[1] 11-14/0579r1, A Backhaul Use Case For NG 11ad, Joseph Levy et al, May 2014.
[2] 11-14/0606r0, Next Generation 802.11ad: 30+ Gbps WLAN, Carlos Cordeiro et al, May 2014.