## Slide 1: MAC Calibration Results
Date: 9/10/2014
Authors:
Name | Affiliations | Address | Phone | Email
Igor Kim | ETRI | Korea | +82-42-860-5525 | ikim@etri.re.kr
Gwangzeen Ko | ETRI | Korea | +82-42-860-4862 | gogogo@etri.re.kr
Hyunduk Kang | ETRI | Korea | +82-42-860-1074 | henry@etri.re.kr
Myung-Sun Song | ETRI | Korea | +82-42-860-5046 | mssong@etri.re.kr

## Slide 2: Summary
In [1], [2] simulation scenarios and evaluation methods for MAC simulator are described
Some MAC calibrations are described in [3] – [8]
In [9] comparison of each company’s MAC calibration for scenarios 1 – 3 is done
This document provides results of MAC simulator for
  MAC overhead (test 1a (w/o RTS) and 1b (w/ RTS))
  Deferral tests (tests 2a (w/o hidden node) and 2b (w/ hidden node))
  NAV deferral (test 3)
Compare MAC simulator results by company

## Slide 3: Test 1a. MAC Overhead w/o RTS/CTS
Simulation Parameters
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s) and MCS8 (78 Mbit/s)
  RTS/CTS: off
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 500, 1000, 1500, 2000 bytes
  Application data size: 464, 964, 1464, 1964 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP1

## Slide 4: Test 1a. Check Points
Test Items | Check points | Standard definition | Matching?
A-MPDU duration | Tcp2 - Tcp1 = 3824 us | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES
SIFS | Tcp3 - Tcp2 = 16 us | 16 us | YES
ACK duration | Tcp4 - Tcp3 = 68 us | ceil((ACKFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES
Defer & backoff duration | Tcp5 - Tcp4 = 101.5 us | DIFS(34 us)+backoff (CWmin) =34us+n*9/2us | YES
MSDU size = 1500 bytes, MCS0

## Slide 5: Test 1a. Simulation Time Trace
CP1 start of A-MPDU, [sec] |  | 34.618888503164
CP2 end of A-MPDU, [sec] |  | 34.62271251983
 | CP2-CP1, [us] | 3824.016666
 | Expected A-MPDU duration, [us] | 3824
 | Difference, [us] – signal propagation delay | 0.016666
CP3 start of BA, [sec] |  | 34.62272851983
 | CP3-CP2, [us] | 16
 | Expected SIFS duration, [us] | 16
CP4 end of BA, [sec] |  | 34.622796536497
 | CP4-CP3, [us] | 68.016666
 | Expected ACK duration, [us] | 68
 | Difference, [us] – signal propagation delay | 0.016666
CP5 start of new A-MPDU, [sec] |  | 34.622839536497
 | CP5-CP4, [us] | 43
 | Expected DIFS + backoff duration, [us] | [34, 169]

## Slide 6: Test 1a. Throughput Results
MCS index | Application data size, [Bytes] | MSDU size, [Bytes] | Numerical L4 Throughput, [Mbit/s] | Simulated L4 Throughput, [Mbit/s] | Numerical MAC Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
0 | 464 | 500 | 4.79112 | 4.79111 | 5.16284 | 5.16284
0 | 964 | 1000 | 5.55313 | 5.55293 | 5.76051 | 5.76030
0 | 1464 | 1500 | 5.84208 | 5.84192 | 5.98573 | 5.98558
0 | 1964 | 2000 | 5.99519 | 5.99482 | 6.10508 | 6.10471
8 | 464 | 500 | 21.99486 | 21.99063 | 23.70136 | 23.69680
8 | 964 | 1000 | 34.93281 | 34.94223 | 36.23735 | 36.24714
8 | 1464 | 1500 | 43.25496 | 43.26557 | 44.31860 | 44.32949
8 | 1964 | 2000 | 48.67913 | 48.68493 | 49.57141 | 49.57733

## Slide 7: Test 1b. MAC Overhead with RTS/CTS
Simulation Parameters
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s) and MCS8 (78 Mbit/s)
  RTS/CTS: on
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 500, 1000, 1500, 2000 bytes
  Application data size: 464, 964, 1464, 1964 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP1

## Slide 8: Test 1b. Check Points
MSDU size = 1500 bytes, MCS0
Test Items | Check points | Standard definition | Matching?
RTS duration | Tcp2 - Tcp1 = 52 us | ceil((RTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES
CTS duration | Tcp4 - Tcp3 = 44 us | ceil((CTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES
Frame duration | Tcp6 - Tcp5 = 3824 us | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES

## Slide 9: Test 1b. Simulation Time Trace
CP1 start of RTS, [sec] |  | 34.329152003165
CP2 end of RTS, [sec] |  | 34.329204019832
 | CP2-CP1, [us] | 52.016667
 | Expected RTS duration, [us] | 52.0
 | Difference, [us] – signal propagation delay | 0. 016667
CP3 start of CTS, [sec] |  | 34.329220019832
 | CP3-CP2, [us] | 16
 | Expected SIFS duration, [us] | 16
CP4 end of CTS, [sec] |  | 34.329264036498
 | CP4-CP3, [us] | 44.016667
 | Expected CTS duration, [us] | 44.0
 | Difference, [us] – signal propagation delay | 0. 016667
CP5 start of A-MPDU, [sec] |  | 34.329280036498
 | CP5-CP4, [us] | 16
 | Expected SIFS duration, [us] | 16
CP6 end of A-MPDU, [sec] |  | 34.333104053165
 | CP6-CP5, [us] | 3824.016667
 | Expected A-MPDU duration, [us] | 3824
 | Difference, [us] – signal propagation delay | 0.016667

## Slide 10: Test 1b. Throughput Results
MCS index | Application data size, [Bytes] | MSDU size, [Bytes] | Numerical L4 Throughput, [Mbit/s] | Simulated L4 Throughput, [Mbit/s] | Numerical MAC Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
0 | 464 | 500 | 4.42555 | 4.42499 | 4.76891 | 4.76830
0 | 964 | 1000 | 5.30849 | 5.30908 | 5.50673 | 5.50734
0 | 1464 | 1500 | 5.66134 | 5.66016 | 5.80056 | 5.79935
0 | 1964 | 2000 | 5.85228 | 5.85183 | 5.95955 | 5.95910
8 | 464 | 500 | 15.94730 | 15.94436 | 17.18459 | 17.18142
8 | 964 | 1000 | 27.08182 | 26.96925 | 28.09317 | 27.97640
8 | 1464 | 1500 | 34.98556 | 34.98834 | 35.84586 | 35.84872
8 | 1964 | 2000 | 40.62398 | 40.62964 | 41.36861 | 41.37439

## Slide 11: Test 2a. Deferral Test1
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s)
  RTS/CTS: [OFF, ON]
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 500, 1000, 1500, 2000 bytes
  Application data size: 464, 964, 1464, 1964 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)

## Slide 12: Test 2a. Throughput and PER Results
RTS/CTS | Application data size, [Bytes] | MSDU size, [Bytes] | PER | Simulated L4 Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
No | 464 | 500 | 0.10934 | 4.59254 | 4.94887
No | 964 | 1000 | 0.111242 | 5.28223 | 5.47949
No | 1464 | 1500 | 0.112979 | 5.54912 | 5.68559
No | 1964 | 2000 | 0.108886 | 5.68078 | 5.78491
Yes | 464 | 500 | 0.0 | 4.46549 | 4.81195
Yes | 964 | 1000 | 0.0 | 5.30999 | 5.50829
Yes | 1464 | 1500 | 0.0 | 5.65486 | 5.79393
Yes | 1964 | 2000 | 0.0 | 5.86833 | 5.97590

## Slide 13: Test 2b. Deferral Test2
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU, OFF
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s) and MCS8 (78 Mbit/s)
  RTS/CTS: [OFF]
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 1500 bytes
  Application data size: 1464 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP 2
AP1
STA 2

## Slide 14: Test 2b. Throughput and PER Results
FA – frame aggregation
FA | MCS index | Application data size, [Bytes] | MSDU size, [Bytes] | PER | Simulated L4 Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
Yes | 0 | 1464 | 1500 | 0.877915 | 0.950949 | 0.974342
Yes | 8 | 1464 | 1500 | 0.152984 | 33.960896 | 34.796107
No | 0 | 1464 | 1500 | 0.732127 | 1.62026 | 1.66012
No | 8 | 1464 | 1500 | 0.197594 | 28.84498 | 29.55438

## Slide 15: Test 3. NAV Deferral
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU, OFF
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s) and MCS8 (78 Mbit/s)
  RTS/CTS: [ON]
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 1500 bytes
  Application data size: 1464 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP 2
AP1
STA 2

## Slide 16: Test 3. Throughput and PER Results
FA – frame aggregation
FA | MCS index | Application data size, [Bytes] | MSDU size, [Bytes] | PER | Simulated L4 Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
Yes | 0 | 1464 | 1500 | 0.0 | 5.610717 | 5.748704
Yes | 8 | 1464 | 1500 | 0.0 | 33.816448 | 34.64802
No | 0 | 1464 | 1500 | 0.0 | 5.194439 | 5.32219
No | 8 | 1464 | 1500 | 0.0 | 21.635812 | 22.167891

## Slide 17: Test 1a. Results Comparison
Configurations | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
ETRI | 4.79111 | 5.55293 | 5.84192 | 5.99482 | 21.9906 | 34.9422 | 43.2656 | 48.6849
Huawei | 4.79 | 5.55 | 5.84 | 6.00 | 21.98 | 34.91 | 43.24 | 48.67
LGE | 4.81 | 5.55 | 5.84 | 5.99 | 22.4 | 35.2 | 43.25 | 48.9
Qualcomm | 4.76 | 5.53 | 5.82 | 5.98 | 23.92 | 37.25 | 45.55 | 50.81
MediaTek | 4.76 | 5.53 | 5.82 | 5.98 | 21.71 | 34.65 | 42.71 | 48.15
Intel | 4.76 | 5.53 | 5.82 | 5.98 | 21.53 | 34.46 | 42.58 | 48.14
Ericsson | 4.75 | 5.52 | 5.82 | 5.97 | 21.53 | 34.47 | 42.57 | 48.09
Nokia | 4.76 | 5.52 | 5.83 | 5.97 | 21.19 | 34.22 | 41.93 | 47.74
NTT | 4.79 | 5.54 | 5.84 | 6.00 | 22.00 | 35.00 | 43.20 | 48.40
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
ETRI | 4.7911 | 5.5529 | 5.8419 | 5.9948
Huawei | 4.79 | 5.55 | 5.84 | 6
LGE | 4.81 | 5.55 | 5.84 | 5.99
Qualcomm | 4.76 | 5.53 | 5.82 | 5.98
MediaTek | 4.76 | 5.53 | 5.82 | 5.98
Intel | 4.76 | 5.53 | 5.82 | 5.98
Ericsson | 4.75 | 5.52 | 5.82 | 5.97
Nokia | 4.76 | 5.52 | 5.83 | 5.97
NTT | 4.79 | 5.54 | 5.84 | 6
MCS0
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
ETRI | 21.9906 | 34.9422 | 43.2656 | 48.6849
Huawei | 21.98 | 34.91 | 43.24 | 48.67
LGE | 22.4 | 35.2 | 43.25 | 48.9
Qualcomm | 23.92 | 37.25 | 45.55 | 50.81
MediaTek | 21.71 | 34.65 | 42.71 | 48.15
Intel | 21.53 | 34.46 | 42.58 | 48.14
Ericsson | 21.53 | 34.47 | 42.57 | 48.09
Nokia | 21.19 | 34.22 | 41.93 | 47.74
NTT | 22 | 35 | 43.2 | 48.4
MCS8

## Slide 18: Test 1b. Results Comparison
Configurations | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
ETRI | 4.42499 | 5.30908 | 5.66016 | 5.85183 | 15.9444 | 26.9693 | 34.9883 | 40.6296
Huawei | 4.42 | 5.31 | 5.66 | 5.85 | 15.94 | 27.07 | 34.97 | 40.61
LGE | 4.45 | 5.31 | 5.66 | 5.86 | 16.2 | 27.3 | 35 | 40.8
Qualcomm | 4.4 | 5.29 | 5.64 | 5.84 | 18.64 | 30.75 | 38.94 | 44.51
MediaTek | 4.40 | 5.29 | 5.64 | 5.84 | 15.79 | 26.90 | 34.62 | 40.24
Intel | 4.4 | 5.29 | 5.64 | 5.84 | 15.7 | 26.8 | 34.55 | 40.26
Nokia | 4.40 | 5.28 | 5.64 | 5.83 | 15.52 | 26.66 | 34.12 | 39.96
NTT | 4.42 | 5.30 | 5.67 | 5.85 | 16.00 | 27.10 | 34.97 | 40.40
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
ETRI | 4.425 | 5.3091 | 5.6602 | 5.8518
Huawei | 4.42 | 5.31 | 5.66 | 5.85
LGE | 4.45 | 5.31 | 5.66 | 5.86
Qualcomm | 4.4 | 5.29 | 5.64 | 5.84
MediaTek | 4.4 | 5.29 | 5.64 | 5.84
Intel | 4.4 | 5.29 | 5.64 | 5.84
Nokia | 4.4 | 5.28 | 5.64 | 5.83
NTT | 4.42 | 5.3 | 5.67 | 5.85
MCS0
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
ETRI | 15.9444 | 26.9693 | 34.9883 | 40.6296
Huawei | 15.94 | 27.07 | 34.97 | 40.61
LGE | 16.2 | 27.3 | 35 | 40.8
Qualcomm | 18.64 | 30.75 | 38.94 | 44.51
MediaTek | 15.79 | 26.9 | 34.62 | 40.24
Intel | 15.7 | 26.8 | 34.55 | 40.26
Nokia | 15.52 | 26.66 | 34.12 | 39.96
NTT | 16 | 27.1 | 34.97 | 40.4
MCS8

## Slide 19: Test 2a. Results Comparison
Configurations | Without RTS/CTS |  |  |  | With RTS/CTS |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
ETRI | 4.59254 | 5.28223 | 5.54912 | 5.68078 | 4.46549 | 5.30999 | 5.65486 | 5.86833
Huawei | 4.56 | 5.25 | 5.51 | 5.66 | 4.46 | 5.33 | 5.68 | 5.87
LGE | 4.62 | 5.28 | 5.54 | 5.66 | 4.5 | 5.34 | 5.68 | 5.88
Qualcomm | 4.57 | 5.26 | 5.53 | 5.67 | 4.45 | 5.32 | 5.67 | 5.86
MediaTek | 4.71 | 5.48 | 5.78 | 5.94 | 4.35 | 5.24 | 5.62 | 5.81
Intel | 4.52 | 5.22 | 5.48 | 5.62 | 4.44 | 5.31 | 5.67 | 5.86
Ericsson | 4.53 | 5.21 | 5.48 | 5.63 |  |  |  | 
Nokia | 4.58 | 5.29 | 5.56 | 5.71 | 4.48 | 5.32 | 5.67 | 5.85
NTT | 4.58 | 5.25 | 5.45 | 5.66 | 4.49 | 5.35 | 5.70 | 5.88
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
ETRI | 4.5925 | 5.2822 | 5.5491 | 5.6808
Huawei | 4.56 | 5.25 | 5.51 | 5.66
LGE | 4.62 | 5.28 | 5.54 | 5.66
Qualcomm | 4.57 | 5.26 | 5.53 | 5.67
MediaTek | 4.71 | 5.48 | 5.78 | 5.94
Intel | 4.52 | 5.22 | 5.48 | 5.62
Ericsson | 4.53 | 5.21 | 5.48 | 5.63
Nokia | 4.58 | 5.29 | 5.56 | 5.71
NTT | 4.58 | 5.25 | 5.45 | 5.66
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
ETRI | 4.4655 | 5.31 | 5.6549 | 5.8683
Huawei | 4.46 | 5.33 | 5.68 | 5.87
LGE | 4.5 | 5.34 | 5.68 | 5.88
Qualcomm | 4.45 | 5.32 | 5.67 | 5.86
MediaTek | 4.35 | 5.24 | 5.62 | 5.81
Intel | 4.44 | 5.31 | 5.67 | 5.86
Nokia | 4.48 | 5.32 | 5.67 | 5.85
NTT | 4.49 | 5.35 | 5.7 | 5.88
w/o RTS/CTS
w/ RTS/CTS

## Slide 20: Test 2b. Results Comparison
Scenarios | ETRI | Huawei | LGE | Qualcomm | MediaTek | Intel | Nokia | NTT
No FA, MCS0 | 1.62026 | 1.62 | 1.7 |  |  |  |  | 
FA, MCS0 | 0.95095 | 1.01 | 1.02 | 0.98 | 0.03631 | 1.008 | 1.20 | 1.06
No FA, MCS8 | 28.845 | 26.54 | 26.8 |  |  |  |  | 
FA, MCS8 | 33.9609 | 34.75 | 35.0 |  |  |  | 35.66 | 
Chart: L4 Throughput, Mbits/s
| FA, MCS0 | FA, MCS8
ETRI | 0.95095 | 33.9609
Huawei | 1.01 | 34.75
LGE | 1.02 | 35
Qualcomm | 0.98
MediaTek | 0.03631
Intel | 1.008
Nokia | 1.2 | 35.66
NTT | 1.06

## Slide 21: Test 3. Results Comparison
Scenarios | ETRI | Huawei | LGE | Qualcomm | MediaTek | Intel | Nokia | NTT
No FA, MCS0 | 5.19444 | 5.15 | 5.14 |  |  |  |  | 
FA, MCS0 | 5.61072 | 5.58 | 5.58 | 5.55 | 5.63933 | 5.66 | 5.59 | 5.40
No FA, MCS8 | 21.6358 | 22.04 | 22.4 |  |  |  |  | 
FA, MCS8 | 33.8164 | 34.05 | 34.2 |  |  |  | 31.35 | 
Chart: L4 Throughput, Mbits/s
| FA, MCS0 | FA, MCS8
ETRI | 5.6107 | 33.8164
Huawei | 5.58 | 34.05
LGE | 5.58 | 34.2
Qualcomm | 5.55
MediaTek | 5.6393
Intel | 5.66
Nokia | 5.59 | 31.35
NTT | 5.4

## Slide 22: Clarification Issues (1)
Defer & Backoff duration formula in Test 1a
  Correct formula and value
    DIFS(34 us)+backoff (CWmin)/2=34us+n*9/2us = 101.5us
    n = 15
Signal propagation delay
  Signal propagation delay Tprop = d/c
    d – distance between transmitter and receiver
    c – speed of light in vacuum (3*108 m/s)
  A distance of 100m adds 0.333 us propagation delay
  Do we need to consider it?

## Slide 23: Clarification Issues (2)
A-MPDU Tx time estimation
  According to the 802.11-2012 standard: “Except when an A-MPDU subframe is the last one in an A-MPDU, padding octets are appended to make each A-MPDU subframe a multiple of 4 octets in length”
  A-MPDU size = (MSDU + MAC header + delimiter)*2*8 + padding + service + tail = (1500 + 30 + 4)*2*8 + 16 + 16 + 6 = 24582 bits
  A-MPDU duration = ceil((FrameLength*8) /rate /OFDMsymbolduration) * OFDMsymbolduration + PHY Header = ceil(24582/6.5/4) * 4 + 40 = 3824 us

## Slide 24: Conclusion
MAC calibration results
  Performed simulations for Tests 1 – 3
  Simulation results show similar trend with other companies results

## Slide 25: Reference
[1] 11-14-0980-04-00ax-simulation-scenarios
[2] 11-14-0571-05-00ax-evaluation-methodology
[3] 11-14-1175-01-00ax-mac-calibration-results
[4] 11-14-0600-00-00ax-mac-simulator-calibration
[5] 11-14-1230-00-00ax-mac-calibration-result
[6] 11-14-1217-00-00ax-mac-calibration-results-for-test-1-and-2
[7] 11-14-1191-00-00ax-mac-calibration-huawei-results
[8] 11-14-1147-00-00ax-mac-simulator-calibration-results
[9] 11-14-1192-03-00ax-comparing-mac-calibration-results