## Slide 1: MAC Calibration Results
Date: 01/11/2014
Authors:
Name | Affiliations | Address | Phone | Email
Igor Kim | ETRI | Korea | +82-42-860-5525 | ikim@etri.re.kr
Gwangzeen Ko | ETRI | Korea | +82-42-860-4862 | gogogo@etri.re.kr
Hyunduk Kang | ETRI | Korea | +82-42-860-1074 | henry@etri.re.kr
Myung-Sun Song | ETRI | Korea | +82-42-860-5046 | mssong@etri.re.kr

## Slide 2: Summary
In [1], [2] simulation scenarios and evaluation methods for MAC simulator are described
Some MAC calibrations are described in [3] – [8]
In [9] comparison of each company’s MAC calibration for scenarios 1 – 3 is done
This document provides results of MAC simulator for
  MAC overhead (test 1a (w/o RTS) and 1b (w/ RTS))
  Deferral tests (tests 2a (w/o hidden node) and 2b (w/ hidden node))
  NAV deferral (test 3)
Compare MAC simulator results by company

## Slide 3: Test 1a. MAC Overhead w/o RTS/CTS
Simulation Parameters
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s) and MCS8 (78 Mbit/s)
  RTS/CTS: off
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 500, 1000, 1500, 2000 bytes
  Application data size: 464, 964, 1464, 1964 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP1

## Slide 4: Test 1a. Check Points
Test Items | Check points | Standard definition | Matching?
A-MPDU duration | Tcp2 - Tcp1 = 3824 us | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES
SIFS | Tcp3 - Tcp2 = 16 us | 16 us | YES
ACK duration | Tcp4 - Tcp3 = 68 us | ceil((ACKFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES
Defer & backoff duration | Tcp5 - Tcp4 = 101.5 us | DIFS(34 us)+backoff (CWmin) =34us+n*9/2us | YES
MSDU size = 1500 bytes, MCS0

## Slide 5: Test 1a. Simulation Time Trace
CP1 start of A-MPDU, [sec] |  | 34.618888503164
CP2 end of A-MPDU, [sec] |  | 34.62271251983
 | CP2-CP1, [us] | 3824.016666
 | Expected A-MPDU duration, [us] | 3824
 | Difference, [us] – signal propagation delay | 0.016666
CP3 start of BA, [sec] |  | 34.62272851983
 | CP3-CP2, [us] | 16
 | Expected SIFS duration, [us] | 16
CP4 end of BA, [sec] |  | 34.622796536497
 | CP4-CP3, [us] | 68.016666
 | Expected ACK duration, [us] | 68
 | Difference, [us] – signal propagation delay | 0.016666
CP5 start of new A-MPDU, [sec] |  | 34.622839536497
 | CP5-CP4, [us] | 43
 | Expected DIFS + backoff duration, [us] | [34, 169]

## Slide 6: Test 1a. Throughput Results
MCS index | Application data size, [Bytes] | MSDU size, [Bytes] | Numerical L4 Throughput, [Mbit/s] | Simulated L4 Throughput, [Mbit/s] | Numerical MAC Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
0 | 464 | 500 | 4.79112 | 4.79111 | 5.16284 | 5.16284
0 | 964 | 1000 | 5.55313 | 5.55293 | 5.76051 | 5.76030
0 | 1464 | 1500 | 5.84208 | 5.84192 | 5.98573 | 5.98558
0 | 1964 | 2000 | 5.99519 | 5.99482 | 6.10508 | 6.10471
8 | 464 | 500 | 21.99486 | 21.99063 | 23.70136 | 23.69680
8 | 964 | 1000 | 34.93281 | 34.94223 | 36.23735 | 36.24714
8 | 1464 | 1500 | 43.25496 | 43.26557 | 44.31860 | 44.32949
8 | 1964 | 2000 | 48.67913 | 48.68493 | 49.57141 | 49.57733

## Slide 7: Test 1b. MAC Overhead with RTS/CTS
Simulation Parameters
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s) and MCS8 (78 Mbit/s)
  RTS/CTS: on
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 500, 1000, 1500, 2000 bytes
  Application data size: 464, 964, 1464, 1964 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP1

## Slide 8: Test 1b. Check Points
MSDU size = 1500 bytes, MCS0
Test Items | Check points | Standard definition | Matching?
RTS duration | Tcp2 - Tcp1 = 52 us | ceil((RTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES
CTS duration | Tcp4 - Tcp3 = 44 us | ceil((CTSFrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES
Frame duration | Tcp6 - Tcp5 = 3824 us | ceil((FrameLength*8)/rate/OFDMsymbolduration) * OFDMsymbolduration + PHY Header | YES

## Slide 9: Test 1b. Simulation Time Trace
CP1 start of RTS, [sec] |  | 34.329152003165
CP2 end of RTS, [sec] |  | 34.329204019832
 | CP2-CP1, [us] | 52.016667
 | Expected RTS duration, [us] | 52.0
 | Difference, [us] – signal propagation delay | 0. 016667
CP3 start of CTS, [sec] |  | 34.329220019832
 | CP3-CP2, [us] | 16
 | Expected SIFS duration, [us] | 16
CP4 end of CTS, [sec] |  | 34.329264036498
 | CP4-CP3, [us] | 44.016667
 | Expected CTS duration, [us] | 44.0
 | Difference, [us] – signal propagation delay | 0. 016667
CP5 start of A-MPDU, [sec] |  | 34.329280036498
 | CP5-CP4, [us] | 16
 | Expected SIFS duration, [us] | 16
CP6 end of A-MPDU, [sec] |  | 34.333104053165
 | CP6-CP5, [us] | 3824.016667
 | Expected A-MPDU duration, [us] | 3824
 | Difference, [us] – signal propagation delay | 0.016667

## Slide 10: Test 1b. Throughput Results
MCS index | Application data size, [Bytes] | MSDU size, [Bytes] | Numerical L4 Throughput, [Mbit/s] | Simulated L4 Throughput, [Mbit/s] | Numerical MAC Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
0 | 464 | 500 | 4.42555 | 4.42499 | 4.76891 | 4.76830
0 | 964 | 1000 | 5.30849 | 5.30908 | 5.50673 | 5.50734
0 | 1464 | 1500 | 5.66134 | 5.66016 | 5.80056 | 5.79935
0 | 1964 | 2000 | 5.85228 | 5.85183 | 5.95955 | 5.95910
8 | 464 | 500 | 15.94730 | 15.94436 | 17.18459 | 17.18142
8 | 964 | 1000 | 27.08182 | 26.96925 | 28.09317 | 27.97640
8 | 1464 | 1500 | 34.98556 | 34.98834 | 35.84586 | 35.84872
8 | 1964 | 2000 | 40.62398 | 40.62964 | 41.36861 | 41.37439

## Slide 11: Test 2a. Deferral Test1
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s)
  RTS/CTS: [OFF, ON]
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 500, 1000, 1500, 2000 bytes
  Application data size: 464, 964, 1464, 1964 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP 2
AP1
STA 2
(AP1 and STA2 are essentially co-located)

## Slide 12: Test 2a. Throughput and PER Results
RTS/CTS | Application data size, [Bytes] | MSDU size, [Bytes] | PER | Simulated L4 Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
No | 464 | 500 | 0.10934 | 4.59254 | 4.94887
No | 964 | 1000 | 0.111242 | 5.28223 | 5.47949
No | 1464 | 1500 | 0.112979 | 5.54912 | 5.68559
No | 1964 | 2000 | 0.108886 | 5.68078 | 5.78491
Yes | 464 | 500 | 0.0 | 4.46549 | 4.81195
Yes | 964 | 1000 | 0.0 | 5.30999 | 5.50829
Yes | 1464 | 1500 | 0.0 | 5.65486 | 5.79393
Yes | 1964 | 2000 | 0.0 | 5.86833 | 5.97590

## Slide 13: Test 2b. Deferral Test2
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU, OFF
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s) and MCS8 (78 Mbit/s)
  RTS/CTS: [OFF]
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 1500 bytes
  Application data size: 1464 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP 2
AP1
STA 2

## Slide 14: Test 2b. Throughput and PER Results
FA – frame aggregation
FA | MCS index | Application data size, [Bytes] | MSDU size, [Bytes] | PER | Simulated L4 Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
Yes | 0 | 1464 | 1500 | 0.877915 | 0.950949 | 0.974342
Yes | 8 | 1464 | 1500 | 0.152984 | 33.960896 | 34.796107
No | 0 | 1464 | 1500 | 0.732127 | 1.62026 | 1.66012
No | 8 | 1464 | 1500 | 0.197594 | 28.84498 | 29.55438

## Slide 15: Test 3. NAV Deferral
  Guard interval: long
  Data preamble: 11ac
  Bandwidth: 20 MHz
  A-MPDU aggregation: 2 MPDU per A-MPDU, OFF
  Max retries: 10
  Fixed MCS: MCS0 (6.5 Mbit/s) and MCS8 (78 Mbit/s)
  RTS/CTS: [ON]
  Cwmin: 15
  AIFSN [BE]: 2
  PER: 0
  MSDU length: 1500 bytes
  Application data size: 1464 bytes
  L4 – L3 header overhead: 36 bytes
  SIFS: 16us, DIFS = AIFS [BE] = 34us
STA 1
AP 2
AP1
STA 2

## Slide 16: Test 3. Throughput and PER Results
FA – frame aggregation
FA | MCS index | Application data size, [Bytes] | MSDU size, [Bytes] | PER | Simulated L4 Throughput, [Mbit/s] | Simulated MAC Throughput, [Mbit/s]
Yes | 0 | 1464 | 1500 | 0.0 | 5.610717 | 5.748704
Yes | 8 | 1464 | 1500 | 0.0 | 33.816448 | 34.64802
No | 0 | 1464 | 1500 | 0.0 | 5.194439 | 5.32219
No | 8 | 1464 | 1500 | 0.0 | 21.635812 | 22.167891

## Slide 17: Test 1a. Results Comparison
Configurations (doc. #) | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
14/1342r1 | 4.79111 | 5.55293 | 5.84192 | 5.99482 | 21.9906 | 34.9422 | 43.2656 | 48.6849
14/1191r0 | 4.79 | 5.55 | 5.84 | 6.00 | 21.98 | 34.91 | 43.24 | 48.67
14/1175r1 | 4.81 | 5.55 | 5.84 | 5.99 | 22.4 | 35.2 | 43.25 | 48.9
14/600r0 | 4.76 | 5.53 | 5.82 | 5.98 | 23.92 | 37.25 | 45.55 | 50.81
14/1230r2 | 4.76 | 5.53 | 5.82 | 5.98 | 21.71 | 34.65 | 42.71 | 48.15
14/1217r1 | 4.76 | 5.52 | 5.83 | 5.97 | 21.19 | 34.22 | 41.93 | 47.74
14/1147r0 | 4.79 | 5.54 | 5.84 | 6.00 | 22.00 | 35.00 | 43.20 | 48.40
MCS0
MCS8
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
14/1342r1 | 4.7911 | 5.5529 | 5.8419 | 5.9948
14/1191r0 | 4.79 | 5.55 | 5.84 | 6
14/1175r1 | 4.81 | 5.55 | 5.84 | 5.99
14/600r0 | 4.76 | 5.53 | 5.82 | 5.98
14/1230r2 | 4.76 | 5.53 | 5.82 | 5.98
14/1217r1 | 4.76 | 5.52 | 5.83 | 5.97
14/1147r0 | 4.79 | 5.54 | 5.84 | 6
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
14/1342r1 | 21.9906 | 34.9422 | 43.2656 | 48.6849
14/1191r0 | 21.98 | 34.91 | 43.24 | 48.67
14/1175r1 | 22.4 | 35.2 | 43.25 | 48.9
14/600r0 | 23.92 | 37.25 | 45.55 | 50.81
14/1230r2 | 21.71 | 34.65 | 42.71 | 48.15
14/1217r1 | 21.19 | 34.22 | 41.93 | 47.74
14/1147r0 | 22 | 35 | 43.2 | 48.4

## Slide 18: Test 1b. Results Comparison
Configurations (doc. #) | MCS0 (6.5Mbps) |  |  |  | MCS8 (78Mbps) |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
14/1342r1 | 4.42499 | 5.30908 | 5.66016 | 5.85183 | 15.9444 | 26.9693 | 34.9883 | 40.6296
14/1191r0 | 4.42 | 5.31 | 5.66 | 5.85 | 15.94 | 27.07 | 34.97 | 40.61
14/1175r1 | 4.45 | 5.31 | 5.66 | 5.86 | 16.2 | 27.3 | 35 | 40.8
14/600r0 | 4.4 | 5.29 | 5.64 | 5.84 | 18.64 | 30.75 | 38.94 | 44.51
14/1230r2 | 4.40 | 5.29 | 5.64 | 5.84 | 15.79 | 26.90 | 34.62 | 40.24
14/1217r1 | 4.40 | 5.28 | 5.64 | 5.83 | 15.52 | 26.66 | 34.12 | 39.96
14/1147r0 | 4.42 | 5.30 | 5.67 | 5.85 | 16.00 | 27.10 | 34.97 | 40.40
MCS0
MCS8
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
14/1342r1 | 4.425 | 5.3091 | 5.6602 | 5.8518
14/1191r0 | 4.42 | 5.31 | 5.66 | 5.85
14/1175r1 | 4.45 | 5.31 | 5.66 | 5.86
14/600r0 | 4.4 | 5.29 | 5.64 | 5.84
14/1230r2 | 4.4 | 5.29 | 5.64 | 5.84
14/1217r1 | 4.4 | 5.28 | 5.64 | 5.83
14/1147r0 | 4.42 | 5.3 | 5.67 | 5.85
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
14/1342r1 | 15.9444 | 26.9693 | 34.9883 | 40.6296
14/1191r0 | 15.94 | 27.07 | 34.97 | 40.61
14/1175r1 | 16.2 | 27.3 | 35 | 40.8
14/600r0 | 18.64 | 30.75 | 38.94 | 44.51
14/1230r2 | 15.79 | 26.9 | 34.62 | 40.24
14/1217r1 | 15.52 | 26.66 | 34.12 | 39.96
14/1147r0 | 16 | 27.1 | 34.97 | 40.4

## Slide 19: Test 2a. Results Comparison
Configurations (doc. #) | Without RTS/CTS |  |  |  | With RTS/CTS |  |  | 
 | 500 | 1000 | 1500 | 2000 | 500 | 1000 | 1500 | 2000
14/1342r1 | 4.59254 | 5.28223 | 5.54912 | 5.68078 | 4.46549 | 5.30999 | 5.65486 | 5.86833
14/1191r0 | 4.56 | 5.25 | 5.51 | 5.66 | 4.46 | 5.33 | 5.68 | 5.87
14/1175r1 | 4.62 | 5.28 | 5.54 | 5.66 | 4.5 | 5.34 | 5.68 | 5.88
14/600r0 | 4.57 | 5.26 | 5.53 | 5.67 | 4.45 | 5.32 | 5.67 | 5.86
14/1230r2 | 4.71 | 5.48 | 5.78 | 5.94 | 4.35 | 5.24 | 5.62 | 5.81
14/1217r1 | 4.58 | 5.29 | 5.56 | 5.71 | 4.48 | 5.32 | 5.67 | 5.85
14/1147r0 | 4.58 | 5.25 | 5.45 | 5.66 | 4.49 | 5.35 | 5.70 | 5.88
w/o RTS/CTS
w/ RTS/CTS
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
14/1342r1 | 4.5925 | 5.2822 | 5.5491 | 5.6808
14/1191r0 | 4.56 | 5.25 | 5.51 | 5.66
14/1175r1 | 4.62 | 5.28 | 5.54 | 5.66
14/600r0 | 4.57 | 5.26 | 5.53 | 5.67
14/1230r2 | 4.71 | 5.48 | 5.78 | 5.94
14/1217r1 | 4.58 | 5.29 | 5.56 | 5.71
14/1147r0 | 4.58 | 5.25 | 5.45 | 5.66
Chart: MSDU size, bytes
| 500 | 1000 | 1500 | 2000
14/1342r1 | 4.4655 | 5.31 | 5.6549 | 5.8683
14/1191r0 | 4.46 | 5.33 | 5.68 | 5.87
14/1175r1 | 4.5 | 5.34 | 5.68 | 5.88
14/600r0 | 4.45 | 5.32 | 5.67 | 5.86
14/1230r2 | 4.35 | 5.24 | 5.62 | 5.81
14/1217r1 | 4.48 | 5.32 | 5.67 | 5.85
14/1147r0 | 4.49 | 5.35 | 5.7 | 5.88

## Slide 20: Test 2b. Results Comparison
Scenarios | 14/1342r1 | 14/1191r0 | 14/1175r1 | 14/600r0 | 14/1230r2 | 14/1217r1 | 14/1147r0
No FA, MCS0 | 1.62026 | 1.62 | 1.7 |  |  |  | 
FA, MCS0 | 0.95095 | 1.01 | 1.02 | 0.98 | 0.03631 | 1.20 | 1.06
No FA, MCS8 | 28.845 | 26.54 | 26.8 |  |  |  | 
FA, MCS8 | 33.9609 | 34.75 | 35.0 |  |  | 35.66 | 
Chart: L4 Throughput, Mbits/s
| FA, MCS0 | FA, MCS8
14/1342r1 | 0.95095 | 33.9609
14/1191r0 | 1.01 | 34.75
14/1175r1 | 1.02 | 35
14/600r0 | 0.98
14/1230r2 | 0.03631
14/1217r1 | 1.2 | 35.66
14/1147r0 | 1.06

## Slide 21: Test 3. Results Comparison
Scenarios | 14/1342r1 | 14/1191r0 | 14/1175r1 | 14/600r0 | 14/1230r2 | 14/1217r1 | 14/1147r0
No FA, MCS0 | 5.19444 | 5.15 | 5.14 |  |  |  | 
FA, MCS0 | 5.61072 | 5.58 | 5.58 | 5.55 | 5.63933 | 5.59 | 5.40
No FA, MCS8 | 21.6358 | 22.04 | 22.4 |  |  |  | 
FA, MCS8 | 33.8164 | 34.05 | 34.2 |  |  | 31.35 | 
Chart: L4 Throughput, Mbits/s
| FA, MCS0 | FA, MCS8
14/1342r1 | 5.6107 | 33.8164
14/1191r0 | 5.58 | 34.05
14/1175r1 | 5.58 | 34.2
14/600r0 | 5.55
14/1230r2 | 5.6393
14/1217r1 | 5.59 | 31.35
14/1147r0 | 5.4

## Slide 22: Clarification Issues (1)
Defer & Backoff duration formula in Test 1a
  Correct formula and value
    DIFS(34 us)+backoff (CWmin)/2=34us+n*9/2us = 101.5us
    n = 15

## Slide 23: Clarification Issues (2)
Signal propagation delay
  Signal propagation delay Tprop = d/c
    d – distance between transmitter and receiver
    c – speed of light in vacuum (3*108 m/s)
  A distance of 100m adds 0.333 us propagation delay
  Do we need to consider it?
  What are the proper locations of each check point (CP)? (STA, AP)
    Start of frame Tx must be measured at transmitter, while end of frame Rx must be measured at receiver

## Slide 24: Clarification Issues (3)
A-MPDU Tx time estimation
  In a VHT PPDU, the final A-MPDU subframe is padded to the last octet of the PSDU or to a multiple of 4 octets in length, whichever comes first (802.11ac-2013, 8.6.1)
    Find PSDU_LENGTH (802.11ac-2013, 22.4.3)
    An A-MPDU pre-EOF padding is
      The portion of the A-MPDU up to and including the last A-MPDU subframe if no A-MPDU subframes with 0 in the MPDU Length field and 1 in the EOF field are present, but excluding any subframe padding in the last subframe (802.11ac-2013, 8.6.1)
      APEP_LENGTH = (MSDU + MAC header + delimiter)*2 + padding = (1500 + 30 + 4)*2 + 2 = 3070 bytes

## Slide 25: Clarification Issues (3)
A-MPDU Tx time estimation (cont.)
  A-MPDU size = ((MSDU + MAC header + delimiter )*2 + padding1 + padding2)*8 + service + tail = ((1500 + 30 + 4)*2 + 2 + 1)*8 +16 + 6 = 24590 bits
  A-MPDU duration = ceil((FrameLength*8) /rate /OFDMsymbolduration) * OFDMsymbolduration + PHY Header = ceil(24598/6.5/4) * 4 + 40 = 3824 us
EOF padding is 0 octets
  Since A-MPDU is already aligned to PSDU_LENGTH
Notes:   initial value of A-MPDU_Length[n] for user n is used as the APEP_LENGTH[n] parameter (802.11ac-2013, 9.12.6)
  The A-MPDU_Length[n] for user n is initialized as the length of the resulting A-MPDU pre-EOF padding (802.11ac-2013, 9.12.6)

## Slide 26: Conclusion
MAC calibration results
  Performed simulations for Tests 1 – 3
  Simulation results show similar trend with other companies results

## Slide 27: Reference
[1] 11-14-0980-04-00ax-simulation-scenarios
[2] 11-14-0571-05-00ax-evaluation-methodology
[3] 11-14-1175-01-00ax-mac-calibration-results
[4] 11-14-0600-00-00ax-mac-simulator-calibration
[5] 11-14-1230-00-00ax-mac-calibration-result
[6] 11-14-1217-00-00ax-mac-calibration-results-for-test-1-and-2
[7] 11-14-1191-00-00ax-mac-calibration-huawei-results
[8] 11-14-1147-00-00ax-mac-simulator-calibration-results
[9] 11-14-1192-03-00ax-comparing-mac-calibration-results