## Slide 1: Efficiency Measurement for RTS/CTS
Date: 2014-10-30
Authors:

## Slide 2: Abstract
This document presents the efficiency measurement for RTS/CTS
  Throughput and packet retransmission ratio were measured by the experiment in the dense area
  Measure results show that RTS/CTS can achieve slightly higher performance than the case without using RTS/CTS

## Slide 3: PHY and MAC to Boost Throughput
MAC
access
efficiency
PHY
data
rate
Contribution [1] presented that decreasing collided data is a way to boost throughput.
We assumed RTS/CTS is one of the possible ways to decrease the packet collision.
We performed an experiment to evaluate the efficiency of RTS/CTS in a typical dense area in Tokyo

## Slide 4: Measurement Scenario
~20m
~50m
~100m
AP
@coffee shop
Coffee shop @3rd floor
AP
STA
UDP packets
(1470B)
PC
Frame capture
RTS
CTS
QoS
(UDP)
QoS
(UDP)
QoS
(UDP)
BA
time
time
AP
STA
Frames were captured at the AP side.
UDP throughput and retry rate were measured with/without RTS & CTS on the street which APs had been densely deployed.
CH100+104
(40MHzBW)
CH100
Many SSIDs were observed on CH100.

## Slide 5: Measured Packet Retransmission Ratio
Due to the protection of RTS/CTS, the packet retransmission ratio is always lower than the case without using RTS/CTS
Distance | RTS/CTS | Tx Power |  | 
 |  | Full | -6dB | -10dB
Near (20m) | without | 19.7% | 26.8% | 40.8%
 | with | 18.4% | 24.1% | 35.6%
Middle (50m) | without | 47.9% | 70% | Not connected
 | with | 44.4% | 60.5% | 
Far (100m) | without | 60.9% | Not connected | Not connected
 | with | 50.1% |  | 
The value in each case is an average of 30 measurements

## Slide 6: Measured Throughput (Mbps)
Distance | RTS/CTS | Tx Power |  | 
 |  | Full | -6dB | -10dB
Near (20m) | without | 37.3 | 30.7 | 17.6
 | with | 36.3 | 29.8 | 17.8
Middle (50m) | without | 11.6 | 3.6 | Not connected
 | with | 11.6 | 4.5 | 
Far (100m) | without | 6.6 | Not connected | Not connected
 | with | 7.0 |  | 
In weak signal area, RTS/CTS can achieve higher throughput
  Benefit outweighs overhead
The value in each case is an average of 30 measurements

## Slide 7: Summary
We measured the efficiency of RTS/CTS in a typical dense area in Tokyo
Measurement results show that the benefit of RTS/CTS in throughput outweighs the incurred overhead in the weak signal case

## Slide 8: Reference
11-14/835r2, “Functional Requirements Discursion”, Joe Kwak, et al.