## Slide 1: Novel RTS/CTS Procedure
Date: 2014-10-30
Authors:

## Slide 2: Abstract
This document proposes a novel RTS/CTS procedure to alleviate the exposed terminal issue while handling the hidden terminal issue.
  Measurement in a dense area show that RTS/CTS can achieve higher throughput in weak signal case. [1] However, the achieved gain was very small.
  The proposed scheme is expected to achieve higher throughput while using RTS/CTS. (TGax R1[2])

## Slide 3: Description of the proposed scheme
RTS
CTS
Src
Dst
Gain?
Data
Node_1
Node_2
Src and Dst exchange RTS/CTS frame before Src sends data frames to Dst.
Node_1 can hear RTS from Src but can’t hear CTS from Dst.
Node_2 can hear CTS from Dst but can’t hear RTS from Src.
Node_1 & 2 have to decline their transmissions during NAV set by RTS/CTS.
However, transmission from Node_1 might not affect reception on Dst.

## Slide 4: Proposed RTS/CTS Procedure
RTS1
DATA1
ACK1
S1 (Src)
D1 (Dst)
S2
(Node_1)
SIFS
SIFS
SIFS
D2
CTS1
RTS2
RTS1
CTS2
DATA2
ACK2
CTS2
RTS2
RTS1
CTS1
NAV(RTS1)
Suspension
release
SIFS
SIFS
Random
Back Off
TCTS
TACK1
TACK2
SIFS
S2 received RTS1 but didn’t receive CTS1 during its waiting time (TCTS).
S2 releases Tx suspension then tries to exchange RTS/CTS with D2.
  Carrier sensing is disabled before transmitting of RTS2
When RTS/CTS is succeeded between S2 and D2, data transmission is executed from S2. Tx including ACK2 should be completed before the end of DATA1.

## Slide 5: Summary
RTS/CTS can be used in various cases, e.g., mitigating hidden terminal issue, negotiating bandwidth in 11ac, or protecting frame with weak signal, etc.
  It is necessary to improve the efficiency to achieve higher performance
Aiming at the problem, a novel RTS/CTS procedure is proposed in this document
  Compatible with the existing IEEE 802.11 std.
  Easy to be implemented.

## Slide 6: Reference
11-14/××××, “Efficiency Measurement for RTS/CTS,” B. Zhao and K. Yunoki
11-14/1009r2, “Proposed 802.11ax Functional Requirement”