## Slide 1: Responses to the comments on doc.1169r0
Date: 2014-10-30
Authors:

## Slide 2: Abstract
This contribution is a follow-up of “IEEE 11-14/1169r0, DL-FDMA considerations” which was presented at September 2014 meeting.

## Slide 3: Recap: DL-FDMA
t
t
t
t
AP
STA-1
AP
STA-2
AP
STA-3
AP
STA-4
CCA
DIFS
+ CW
CCA
CCA
CCA
Data to STA-1
Data to STA-2
Data to STA-3
Data to STA-4
ACK
ACK
ACK
ACK
SIFS
CH36
CH40
CH44
CH48
Ex.
Simultaneous data transmissions to multiple STAs using multi-channels.
It may improve access efficiency.

## Slide 4: Comments at September meeting
C1: This proposal is Frequency Division Multiplexing (FDM), it’s not FDMA.
C2: Frame lengths are different for each receiver regarding data size to be sent and data rate.
C3: It is necessary to consider interference mitigation measure for a legacy device at the mixed simultaneous transmission with 11ac devices.
C4: Definition of legacy is needed.

## Slide 5: C1: This proposal is Frequency Division Multiplex. A1: I’m not sure if this access method can be called FDMA.
However, each channel isn’t dedicated to just a certain STA.
t
t
t
t
CH36
CH40
CH44
CH48
Ex.
to STA1
to STA2
to STA3
to STA4
ACK
ACK
ACK
ACK
DIFS+CW
to STA5
to STA6
to STA7
to STA8
ACK
ACK
ACK
ACK
to STA9
to STA10
to STA11
to STA12
ACK
ACK
ACK
ACK
Colors don’t have any meanings.
Just identifying different destinations.

## Slide 6: C2: Frame lengths are different for each receiver. A2: Yes. It’s true.
Similar size packets can easily be sent simultaneously. They will be small size packets. Time length difference among these packets will be adjusted by padding.
to STA1
to STA2
to STA3
to STA4
pad
pad
pad
DIFS+CW
SIFS
t
t
t
t
ACK
ACK
ACK
ACK
Ex.

## Slide 7: C3: Interference mitigation is needed for legacy device. A3: Guard band can be set as a solution when simultaneous transmissions are needed for a legacy device.
to STA1 (11a)
Guard band
(not used)
to STA2 (11ax)
to STA3 (11ax)
DIFS+CW
SIFS
t
t
t
t
ACK
ACK
ACK
When the legacy uses 20MHzBW,
When the legacy uses 40MHzBW,
Primary 20MHz
Secondary 20MHz
to STA1 (11n)
Guard band
(not used)
DIFS+CW
SIFS
t
t
t
t
ACK
ACK
Primary 20MHz
Secondary 20MHz
to STA2 (11ax)

## Slide 8: C4: Definition of legacy device is needed. A4: Legacy means the existing standards as follows:
2.4GHz 11b/g/n
5GHz 11a/g/n/ac

## Slide 9: Summary
This contribution responded to some comments received at September meeting.
Comparing with OFDMA, the proposed access method may not have much better efficiency. However it doesn’t require any negotiation processes before data frame transmissions. It will have advantages to deliver short packets to multiple destinations.

## Slide 10: Straw poll
Do you support to study this access method proposed in doc. 14/1169r0 and this contribution as a possible technique for efficiency improvement for 11ax?
Y/N/A

## Slide 11: References
[1] IEEE 11-14/855r0, “Techniques for Short Downlink Frames”
[2] IEEE 11-14/1169r0, “DL-FDMA considerations”