## Slide 1: NG60 Usage Models
Date: 2014-11-04
Authors:

## Slide 2: Introduction
This contribution details the use-cases for NG60 discussed in IEEE 802 Wireless Interim Meeting in Athens.

## Slide 3: DOCOMO’s view
 | Application | Range | Speed | Security (Confidentiality/Integrity) | Beam Steering (Mandatory/ Optional)
D1 | Traffic offload | <30m | >30Gbps[2] | C/I | M
D2 | Cloud storage | 1 room <10m | >30Gbps[2] | C/I | M
D3 | Mobile backhaul/fronthaul | <200m | <30Gbps[2] | C/I | M
Complement DOCOMO’s previous contribution[1] with some parameters.

## Slide 4: Usage Models discussed in Athens Meeting(1)
No | Name | Requirements |  |  | Document No
 |  | Speed | Range | Others | 
I1 | Backhaul | 2Gbps or higher data rate | 100-150m | Latency -5ms | 14/1249r1[3] (Interdigital)
P1 | USR Mass Data DL/UL | 10Gbps (HD movie of 5GB →5.7s) | 10cm LOS (such as train station airports) | WLAN connectivity | 14/1160r0[4] (Panasonic)
P2 | USR Peer-to-Peer Device Sync | 10Gbps (HD movie of 5GB →5.7s) | 10cm LOS (such as train station airports) | WLAN connectivity | 14/1160r0 (Panasonic)
P3 | USR Touch-and-Get | 10Gbps (HD movie of 5GB →5.7s) | 10cm LOS (such as train station airports) | WLAN connectivity | 14/1160r0 (Panasonic)
H1 | Data Center Inter-Rack Connectivity | <40Gbps | <60’’ (about 152cm) | PER<10E- 2 (requirements of 11ad sub-clause 21.3.3.8) | 14/1185r0[5] (Huawei)

## Slide 5
No | Name | Requirements |  |  | Document No
 |  | Speed | Range | Others | 
H2 | AR VR | <20Gbps | 10ft | PER<10E- 2 jitter<5ms | 14/1185r0 (Huawei)
H3 | Mobile Offloading and Tri-band offloading | <30Gbps | <100m | PER<10E- 2 handoff disconnection <100ms | 14/1185r0 (Huawei)
H4 | Wireless Backhaul Building to Building | <30Gbps | <500m |  | 14/1185r0 (Huawei)
H5 | Video Kiosk | <30Gbps | <10m | Download time 1sec | 14/1185r0 (Huawei)
H6 | Video/Mass-Data Distribution/ Video on Demand System |  | <100m |  | 14/1185r0 (Huawei)
H7 | Wireless Access with roaming devices | <30Gbps | <50m |  | 14/1185r0 (Huawei)
Usage Models discussed in Athens Meeting(2)

## Slide 6: Usage Models mapping
range
throughput
I1
P1
P2
P3
H1
H2
H6
H7
100m
10cm
10m
1m
>30Gbps
10Gbps
20Gbps
No | Usage Models
I1 | Backhaul
P1 | USR Mass Data DL/UL
P2 | USR Peer-to-Peer Device Sync
P3 | USR Touch-and-Get
H1 | Data Center Inter-Rack Connectivity
H2 | AR VR
H3 | Mobile Offloading and Tri-band offloading
H4 | Wireless Backhaul Building to Building
H5 | Video Kiosk
H6 | Video/Mass-Data Distribution/Video on Demand System
H7 | Wireless Access with roaming devices
30Gbps
H3
H4
H5
D1
D2
D3

## Slide 7: Usage Models mapping
range
throughput
100m
10cm
10m
1m
>30Gbps
10Gbps
20Gbps
No | Usage Models
I1 | Backhaul
P1 | USR Mass Data DL/UL
P2 | USR Peer-to-Peer Device Sync
P3 | USR Touch-and-Get
H1 | Data Center Inter-Rack Connectivity
H2 | AR VR
H3 | Mobile Offloading and Tri-band offloading
H4 | Wireless Backhaul Building to Building
H5 | Video Kiosk
H6 | Video/Mass-Data Distribution/Video on Demand System
H7 | Wireless Access with roaming devices
30Gbps
11ad
NG60
I1
P1
P2
P3
H1
H2
H6
H7
H3
H4
H5
D1
D2
D3

## Slide 8: Conclusion
We complemented and summarized usage models discussed in Athens meeting.
We think that the targets of NG60 are extension of coverage and increase of data rate.

## Slide 9: Reference
[1]11-14-1166-00-ng60-ng60-use-cases.pptx
[2] 11-14-0606-00-0wng-next-generation-802-11ad.pptx
[3]11-14-1249-01-ng60-backhaul-support-in-ng-60.pptx
[4] 11-14-1160-00-ng60-ultra-short-range-usr-communications-usage-models-for-ng60.pptx
[5] 11-14-1185-00-ng60-ng60-usage-scenarios.pptx